## Slide 1: Discussion on WLAN sensing sequence design
Date: 2020-09-01
Authors:
Name | Affiliation | Address | Phone | Email
Rui Du | Huawei Technologies Co. Ltd | F3, Huawei Base, Shenzhen, China |  | Ray.du@Huawei.com
Chenchen Liu |  |  |  | 
Meihong Zhang |  |  |  | 
Yingxiang Sun |  |  |  | 
Danny Kaipin Tan |  |  |  | 
Edward Au |  |  |  | 

## Slide 2: Outline
Abstract
  Sequence design of communication
  Existing sequences
  Analysis of existing sequences
Sequence design of WLAN sensing
  Ambiguity function
  Metrics for ambiguity function
  Golay sequences
  Analysis of Golay sequences
Summary
References
Rui Du (Huawei)

## Slide 3: Abstract
New waveform/sequence is potentially needed for WLAN sensing [1].
Further information about a new sequence design property is provided in this presentation.
Rui Du (Huawei)

## Slide 4: Sequence design of communications
The following properties have been adopted for sequence design of communications:
Peak to Average Power Ratio
Auto correlation
Cross correlation
Rui Du (Huawei)

## Slide 5: Existing sequences
Frequency domain sequences
OFDM PHY.
STF/LTF/midamble/… at sub 7 GHz.
STF, CEF at 60 GHz (OFDM PHY in 11ay).
Time domain sequences
Single carrier PHY in 11ad and 11ay.
STF, CEF and TRN field at 60 GHz (11ad and SC PHY in 11ay).
Mainly used for synchronization, channel estimation and beam training.
Rui Du (Huawei)

## Slide 6: Analysis of existing sequences
Frequency domain sequences
STF, LTF, midamble, EDMG-STF (OFDM PHY), EDMG-CEF (OFDM PHY)
Auto correlation (e.g. L-STF).
Cross correlation (e.g. MIMO EDMG-CEF).
PAPR (e.g. L-STF, L-LTF, HE-STF, HE-LTF, EHT-LTF, EDMG-STF, EDMG-CEF).
Time domain sequences
Golay sequences in DMG STF/CEF, EDMG STF/CEF (SC PHY), TRN field
Auto correlation (e.g. DMG-STF, DMG-CEF, EDMG-STF, EDMG-CEF)
Cross correlation (e.g. MIMO EDMG-CEF)
Rui Du (Huawei)

## Slide 7: Sequence design of WLAN sensing
Potential property that could be adopted for WLAN sensing sequence design
Ambiguity function
  Auto ambiguity function
  Cross ambiguity function
Rui Du (Huawei)

## Slide 8: Ambiguity function
Ambiguity function is one of the most important tools for radar waveform analysis.
It is a two-dimensional function of time delay and Doppler shift, showing the output of the received signal through match filter, and is defined as
Time
Doppler
Rui Du (Huawei)

## Slide 9: Metrics for ambiguity function
Peak to Sidelobe Level
Integrated Sidelobe Level
Rui Du (Huawei)

## Slide 10: Golay sequences
Golay sequence is mentioned in [2][3] as a candidate for sensing at 60 GHz.
Is Golay sequence good enough for sensing ?
Rui Du (Huawei)

## Slide 11: Analysis of Golay sequences
CAF of Ga128_1 and Gb128_1
AAF of Gb128_1
CAF of Ga128_1 and Ga128_2
Sum of AAF of Ga128_1 and AAF Gb128_1
The analysis show that the ambiguity function of the Golay sequences is far from closely approximating the ideal “thumbtack” ambiguity function.
Sequences with better AAF/CAF properties could be potentially adopted for WLAN sensing.
Rui Du (Huawei)
AAF of Ga128_1

## Slide 12: Summary
In this presentation, ambiguity function for radar waveform analysis is introduced and discussed.
Initial analysis of existing sequences using the ambiguity function is also provided.
Rui Du (Huawei)

## Slide 13: References
[1] 11-19-1500-00-0wng-wi-fi-sensing-follow-up.pptx
[2] 11-18-2094-00-00ay-wlan-radar.pptx
[3] 11-19-1854-00-SENS-wlan-based-radars-in-the-60ghz-band.pptx
Rui Du (Huawei)

## Slide 14: SP
Do you agree to consider ambiguity function as a property for the WLAN sensing sequence design ?
Yes:
No:
Abstain:
Rui Du (Huawei)