## Slide 1: Access mechanisms to meet the requirements of low latency traffics
Date: 2020-09-09
Authors:
Name | Affiliations | Address | Email
Boyce Yangbo | Huawei | Nanjing, China | yangbo59@huawei.com
Lily Yunping Lyu |  | Nanjing, China | lvyunping@huawei.com
Wayne Wei Qiu |  | Nanjing, China | wayne.qiuwei@huawei.com
Notes: September 2012

## Slide 2: Introduction
Latency is critical important for some traffics.
  NS/EP service is agreed to be supported in 11be which requires guaranteed transmission even in worst cases[1].
  Emerging services like online gaming, real-time video, industrial automation are also sensitive to latency[2]
In one-hop WLAN systems, latency is mainly consist of queue delay, channel access delay, retransmission delay
  Queue delay is highly related to the rate gap between backhaul and WLAN air links, which can be greatly alleviated by high throughput feature in 11be.
  Channel access delay varies a great deal depending on channel status. New mechanisms is needed to meet the requirements of low latency traffic.
  Retransmission delay is also highly related to channel access delay.
This contribution provides a resource reservation method offering a protected access period to improve access delay performance.

## Slide 3: Challenges for low latency traffic
Large access delay is even worse than packet failure
  The transmitter can retransmit failed packet with lower MCS
  The transmitter has nothing to do but wait, if it is unable to get access to the channel
    Note: collision contributes to large access delay
EDCA based mechanism has good delay performance in most cases. However, in case of heavy congestion, access delay could be very large
Simulation setup
 | Lowlatency | Regular
User Num | n | 10*n
EDAC para | VO | BE
PPDU Length | 400us | 4ms
Retran delay | 300us | 300us

## Slide 4: Component mechanisms for low latency traffic transmission
Description of low latency traffic
  How to differentiate low latency traffics from regular traffics (new TID, new AC)
Negotiation between AP and non-AP STAs over low latency traffic characteristics and delay requirements
  non-AP STA make a request with uplink traffic characteristics
  AP make a response to indicate whether the request is accepted/modified/denied.
AP announcing prioritized access mechanisms to non-AP STAs
  What is the prioritized access mechanism?
  Principles:
    Almost guaranteed access delay
    Little influence on regular traffic
    Little changes to STAs not supporting low latency traffic
  We focus on this part in following pages.

## Slide 5: Basic IDEAs
In case of heavy congestion, AP should be able to assign some protected resources for high priority frames
  The protected resource is a time-frequency resource where only specified frames are allowed to transmit.
  Reservation of resources for some specified traffic can be announced using a new element in broadcast frames, e.g. Beacon
  STAs without the specified traffic shall not transmit on reserved resources
    Note that this restriction can be relaxed to improve efficiency which is explained in slide 8.
  STAs with the specified traffic are allowed to transmit on reserved resources
  Transmissions of any PPDU but those containing the specified traffic shall complete before the start of reserved resources.
  This actually creates a much less congested channel access window for critical communications.

## Slide 6: Illustrations and Notes
Channel access on reserved resources could be EDCA based or other protocols.
The following information is need in the new defined element
  RR mode (Type of traffics allowed to be sent on reserved resources, AKA traffic identifier), RR count, RR offset, RR interval, RR duration, RR period
The resource reservation is setup and released dynamically according to link status and traffic buffer status.
  For an AP MLD, resource reservation can be setup on one link only
Identification/notification of traffics that requires resource reservation is out of scope of this contribution:
  Similar topics are under discussion by many contributions[3][4][5][6]
TBTT
TBTT
EDCA based access for all traffics
Reserved for specified traffic
Interval
Duration
Offset

## Slide 7: Example fields in resource reservation element
Count field indicates the number of TBTTs until the beacon interval during which the next reserved resource starts
Offset field indicates the time offset of the start of the reserved resources from the latest TBTT
Interval field indicates interval of two successive reserved resources within a beacon interval
Duration field indicates the duration of the reserved resources
Period field indicates the number of beacon intervals between the start of two successive reserved resources defined by this resource reservation element
Traffic identifier field indicates the traffic type that has higher priority to transmit on reserved resources defined by this resource reservation element
RR
Offset
RR
Interval
RR
Duration
RR
Period
RR Mode
(Traffic identifier)
RR
Count
TBD
Field(s)

## Slide 8: Application Examples
Resource reservation for low latency and NS/EP traffics
Resource reservation for AP coordinated transmission
AP MLD 1
AP MLD 2
AP coordinated transmission
Interference to AP coordinated transmission
Ch36
Ch149
Ch149
Ch52
Note: Alignment of reserved resources might be needed for multi-APs which can be easily achieved in AP coordination
RR mode in yellow is set to low latency traffic
RR mode in green is set to NS/EP traffic
RR mode is set to AP-AP traffic

## Slide 9: Application Examples (cont.)
Resource reservation for P2P transmission
  Case 1：P2P transmission with high priority and latency requirement
  P2P transmission protected period is setup to improve P2P latency performance
  RR mode is set to P2P priority access
  Case 2：P2P transmissions cause serious collision problem to AP-STA transmission
  P2P transmission period is setup that P2P PPDU is allowed to be sent within this period only.
  RR mode is set to P2P restricted access.
Note that the exact value of Resource Reservation mode is TBD

## Slide 10: Influence on regular traffics
Efficiency of regular traffics would be degraded because the channel is even more congested
  The cost paid to support higher priority traffics can be reduced by dynamic setup and release.
  In case of heavy congestion, it’s worthwhile to satisfy QoS of some traffic with minor cost.
  The scheduling algorithm in AP should decide whether to setup/release the resource reservation which is out of scope of 11be.
Regular traffics may be allowed to be sent with a lower priority depending on the access mechanism adopted on reserved resources. For example
  EDCA based access mechanism: regular traffics can access channel with a low-priority set of EDCA parameters(e.g. a large AIFSN and CWmin)
  Trigger based access mechanism: regular traffics are scheduled by AP only if there is no low latency traffics to be sent.

## Slide 11: Coexistence with Pre-EHT STAs
In an actual WLAN network, both EHT and pre-EHT STAs may exist. It’s not fair and not helpful to mute EHT STAs only.
Quiet element can be used with a new defined resource reservation element when both EHT and pre-EHT STAs need to be muted.
  Multiple Quiet elements can setup/release reserved resources as shown in previous pages
  Resource reservation element is used to notify EHT STA which traffic is allowed to transmit
  Pre-EHT STAs are muted by Quiet elements
  EHT STAs without the traffic specified in RR element are also muted
  EHT STAs with the traffic specified in RR element can access channel to transmit
Resource reservation element should have a short variant when used together with quiet elements
  STAs can obtain the information(like resource reservation period, offset, interval, duration) from quiet elements. It would be redundant to include those information in resource reservation element.
Notes: See more info in p23

## Slide 12: Support of Non-periodic Burst Traffic
Recall the low latency traffics defined in[2], 7 use cases with different traffic models are discussed. Many of them have non-periodic low latency traffics.
Extendable duration of reserved resource could be included to balance between efficiency and burst traffic QoS.
TBTT
TBTT
Regular resource reservation variant carried in Beacon frame
temp resource reservation variant carried in action frame
regular duration
extended duration for burst traffic
Regular duration could be setup according to the statistic characters of non-periodic traffic, for example average amount of traffic, 2 sigma amount of traffic, etc.
Extended duration is setup by a temp resource reservation variant carried in an action frame sent by AP according to amount of burst traffics and unexpected interference.

## Slide 13: Influence on standard work
Resource reservation mechanism is a very simple and effective design which is consistent with previous version of standard.
  Quiet element has already been introduced in existing standard.
  What the group need to do is to introduce a new element.
  What the STA need to do is quite similar to existing Quiet procedures (when to mute, how long to mute for, mute period and interval). The only thing new to EHT STA is to recognize which type of traffic is allowed to unmute.
Again, we want to point out that this resource reservation mechanism does not restrict how to use reserved resources, for example
  An easy way: we use existing EDCAF or trigger-based access mechanism on reserved resources, no extra efforts needed.
  An elaborate way: we introduce a new access mechanism for better access performance.
Note that, this mechanism actually provides mutual protection
  It protects low latency traffic from congestion of regular traffics
  It protects regular STAs from additional complexity by any new defined access mechanism applied on reserved resources

## Slide 14: Summary
A resource reservation mechanism is proposed to improve delay performance in heavy congestion cases.
  A very brief summary of our idea is that we add an exception in quiet procedure by adding a new defined element.
  Benefits
  The standard work related to this mechanism is very simple and it adds no complexity to regular STAs.
  Any access mechanism is supported on reserved resources with almost no influence on regular STAs
  Latency performance would not be degraded with the existence of pre-EHT STAs
  The mechanism can further differentiate priorities of multiple low-latency traffics with different delay requirements.
  Influence on regular traffics can be reduced by dynamic setup and release
Notes: Regular traffics just need to keep silent in protected period and do access as usual in other time.

## Slide 15: Straw Poll 1
Do you agree that 11be introduces a resource reservation element including the following information.
  Traffic identifier
  Count
  Offset
  Duration
  Interval
  Period
Note:
  The new element is used by EHT AP to announce the reserved resources for prioritized transmission of low latency traffics
  The definitions of above fields are in slide 7
  Traffic identifier is expressed in TBD.
  Other information in resource reservation element is TBD
Notes: Traffic identifier field indicates the traffic type that has higher priority to transmit on reserved resources defined by this resource reservation element
Count field indicates the number of TBTTs until the beacon interval during which the next reserved resource starts
Offset field indicates the time offset of the start of the reserved resources from the latest TBTT
Duration field indicates the duration of the reserved resources(expressed in TUs)
Interval field indicates interval of two successive reserved resources (expressed in TUs) within a beacon interval
Period field indicates the number of beacon intervals between the start of two successive reserved resources defined by this resource reservation element

## Slide 16: Straw Poll 2
Do you agree that 11be introduces a restricted access mechanism on reserved resources as follows:
  EHT AP may advertise reserved resources for AP transmission opportunities (TXOPs).
  EHT AP may allow STAs with specific traffic to contend for reserved resources
Note:
  For TXOPs on reserved resources, AP should give higher priority to specified type of low latency traffics as indicated in resource reservation element
Notes: Resources may be reserved for AP transmission opportunities
Resources may be reserved for EHT STAs with specified traffic
Other access mechanism are also not excluded on reserved resources.

## Slide 17: References
[1] 11-20-0566-59-00be-compendium-of-straw-polls-and-potential-changes-to-the-specification-framework-document
[2] 11-18-2009-06-0rta-rta-report-draft
[3] 11-20-0418-03-00be-low-latency-service-in-802-11be
[4] 11-20-1006-01-00be-new-methods-to-meet-low-latency-requirements
[5] 11-20-1067-00-00be-traffic-indication-of-latency-sensitive-application
[6] 11-20-1041-02-00be-edca-queue-for-rta

## Slide 18: Backup

## Slide 19: Definition of Delays in slide 2
  Buffer Delay (MSDU based)
    Buffer delay is measured from the time the MSDU is passed to MAC until the point at which the corresponding MPDU/trigger starts EDCA access (i.e. set backoff counter).
    Buffer delay consist of the time in DDR waiting for scheduling, scheduling time, the time waiting in AC queue
  Channel access delay(MPDU based)
    Channel access delay is measured from the time the EDCAF begins CSMA/CA access until the actual frame transmission start time.
  Retransmission delay(MPDU based)
    Retransmission delay depends on the scheduling algorithm in AP
    Retransmission delay is approximately the sum of retransmission scheduling delay and channel access delay

## Slide 20: Discussion on Low latency features in 11be
The standard (i.e. 11be) can not provide any guaranteed QoS of Low latency traffic but a supportive mechanism.
  The implementation specific algorithms are responsible for the QoS performance which seems to be extremely difficult by current channel access mechanism under heavy congested situations
Guaranteed access delay is not a deterministic delay but a high probabilistic delay.
  The numerical delay bound guaranteed by an AP is a implementation related parameter, which depends on the scheduling algorithms adopted.
    For example, an AP may provide access delay up bound 10ms with 90% and 50ms with 99.9%
    Note that: the description is related to reliability as well. Since reliability is also related to MCS selection, ARQ, TX power adaptation, etc, we should focus on delay of a single access.

## Slide 21: Data cursor for simulations results of access latency under EDCA
 | 10%ile (ms) | 1%ile (ms) | 0.1%ile (ms)
1-10 | 12.56 | 25.41 | 41.64
2-20 | 14.54 | 31.85 | 50.58
3-30 | 17.29 | 30.04 | 56.55
4-40 | 20.59 | 43.26 | 66.56
5-50 | 26.57 | 54.93 | 84.07
6-60 | 34.7 | 70.68 | 106.5
7-70 | 44.9 | 91.39 | 136.3
8-80 | 58.45 | 117.4 | 176.1
9-90 | 74.96 | 151.1 | 226.5
Note that: access delay shown here only count low latency traffic.

## Slide 22: Discussion of protected access period
  Protected access period for specified STA or specified Traffic?
    QoS mechanisms should be designed based on traffics not devices
      If a STA has more than one type of traffic, it’s not right to let a low priority traffic (e.g. downloading) have same QoS as high priority traffic (e.g. online game)
    Very limited types of traffics vs variable number of STAs
      A STA has at least one type of traffic, so the number of types is smaller than that of STAs. The notification procedure would be simpler and less cost.
    For STAs having more than one priority access traffics (different delay requirements), it is very difficult to use device based resource reservation to handle this.
      For example, a STA has 2 traffics whose access delay requirements are 20ms and 100ms respectively. Both traffics need 1ms to transmit
      The STA needs 2 different protected access periods which is actually traffic based.
    For non-periodic traffics, statistic multiplexing can be used for traffic based resource reservation to improve channel efficiency.
      Periodic resource reservation can be setup based on concurrency rate of the specified traffic over all STAs

## Slide 23: Influence on other links in case of ML
Protected access periods can be setup on one of the links (link 1) when latency performance is bad. For STR AP MLD:
If non-AP STAs are STR MLDs
    Transmissions on other links would not be affected
If non-AP STAs are NSTR/SR-MLDs
    For regular STAs, transmissions on other links are not affected
    For low latency STAs, transmissions on other links need to stop before the start of protected period as well
If non-AP STAs don’t have ML ability.
    Transmissions on other links would not be affected.

## Slide 24: Alignment of reserved resources for M-AP
Hidden node problem would be very serious in case of AP-AP communication. Resource reservation can be used to mute STAs during AP-AP transmission.
In this case, the reserved resources need to be aligned between 2 or more BSS. The TBTTs of multiple AP can be set as follows to avoid Beacon collisions.
AP1
AP2
AP1
AP2
Option 1
Option 2
Reserved Resources
Beacon
Note that: the exact strategy adopted by AP is implementation dependent.

## Slide 25: Quiet element for resource reservation
TBTT
Duration
Offset
Period (=1)
Multiple Quiet elements and one short resource reservation element can setup multiple reserved resources as follows
Note that: For scenarios with no pre-EHT STAs, one resource reservation element can setup multiple reserved resources as well.

## Slide 26: Example design of resource reservation element
As described above, we need several variant of resource reservation elements: regular setup, short setup, temp setup, temp release and regular release.
Element ID
Length
Resource Reservation Info
Element ID Extension
Control
Control | 
0 | Regular Resource Reservation setup
1 | Short Regular Resource Reservation setup
2 | Temp Resource Reservation setup
3 | Temp Resource Reservation release
4 | Regular Resource Reservation release
Other values are reserved | 

## Slide 27: Example design of resource reservation element (2)
We also need to include the following information in the resource reservation element: Resource Reservation count Resource Reservation offset, Resource Reservation interval, Resource Reservation duration, Resource Reservation period, Resource Reservation mode (Type of traffics allowed to be sent).
Resource Reservation Offset
Resource Reservation Interval
Resource Reservation Duration
Resource Reservation Period
Element ID
Length
Resource Reservation Info
Element ID Extension
Control
Resource Reservation Mode
Regular Resource Reservation Setup variant
Resource Reservation Count
Notes: Has very similar fields to Quiet element which means we have very low risk on this design

## Slide 28: Example Values of Resource Reservation Mode
The values of resource reservation mode is highly related to the description of priority access traffics, we just give some example here.
By different values in RR mode field, the protected access mechanism is very flexible to support many different types of traffic and their combinations
Value | Description | Notes
0 | DFS Channel sensing | No traffic allowed
1 | Low latency traffic type 1 | Delay Requirement: <10ms
2 | Low latency traffic type 2 | Delay Requirement: <20ms
3 | Low latency traffic type 3 | Delay Requirement: <50ms
4 | NS/EP traffic | 
5 | AP-AP traffic | 
6 | P2P critical traffic | Only critical P2P transmission is allowed
7 | P2P restricted traffic | P2P transmission is not allowed at any other time
8 | Unspecified low latency frame | Frames with higher priority, e.g. Control frames
9 | Vendor specific traffic | 
10~255 | To be discussed | 
Note that exact values of resource reservation mode are TBD