## Slide 1: Attacks to Fully Random OFDM Sounding Signal
Date: 2020-11-17

## Slide 2: 11az LB249 CID 3911
CID | Page/Line | Clause | Comment | Proposed resolution
3911 | 153.00 | 11.22.6.4.6 | The Secure LTF mechanism for TB and NTB ranging needs to be improved. A submission will be provided. | As in comment.

## Slide 3: Outline
.
Recap of frequency-domain attack
Complexity of frequency-domain attack
Limitation of frequency-domain attack
Introduction of time-domain attack
Simulations
Summary

## Slide 4: Background
Two proposals are on the table, OFDM-based [5] and time-domain pulse-based [4], which mainly differ by one FFT in implementation
In [1-2], we showed that OFDM-based signal [5] is vulnerable to various frequency-domain attacks
In [4], time-domain pulse signal was proposed, which is similar to UWB and immune to FD attacks
In this contribution, we present a time-domain attack applicable to both TD pulse signal and OFDM signal. In addition, the protection scheme against TD attacks is proposed
.

## Slide 5: Attack Model
Attacker listens to the beginning part, predicts the future part, and sends time-shifted signal of the future part
Slide 5
Time
Time
Genuine signal
Attack signal
Time advancement
Delay
Fake

## Slide 6: Observation Window
Attacker observes the beginning portion and detects the phases of the sinusoids for generating shifted attack signals
…
Observation window
Attack window
Slide 6

## Slide 7: Windowed FFT (1/2)
Time-domain window is applied to weight the input signal and then FFT is performed on the weighted signal

## Slide 8: Windowed FFT (2/2)
The longer the window in time, the fewer the significant taps in frequency

## Slide 9: Windowing in Time, ICI in Frequency
The time-domain windowing introduces inter-carrier interferences in frequency domain

## Slide 10: Windowing in Time, ICI in Frequency
The time-domain windowing introduces inter-carrier interferences in frequency domain

## Slide 11: Linear Filter
The time-domain windowing introduces inter-carrier interferences in frequency domain
qn-1
qn-2
qn-3
qn-4
qn
+
w0
w1
w2
w3
w4
noise
Signals observed by the attacker
Significant taps in Hamming spectrum
qn+1
qn-5
rn-4
QAM symbols the attacker wants to know

## Slide 12: Linear Signal Model
Each received FD sample is a linear mixture of adjacent QAM symbols
Maximum-likelihood solution exists, and near-optimal solutions were well studied and deployed
.
+ n
Sparse matrix

## Slide 13: Vulnerability of OFDM Sounding Signal
Estimating the QAM symbols of OFDM using partially observed signal is equivalent to equalizing an inter-symbol interference (ISI) channel [1], where a large family of solutions exist [1][2]
.
ISI
F
F
ISI
F
F
Not secure
Secure?

## Slide 14: Frequency Domain Attack
The numbers of taps in the equivalent ISI channel are
In [2], decision-feedback equalizer is used, where 4x4 and 5x5 sphere decoders successfully estimated the input 64 and 256-QAM symbols by observing 2/3 and ¾ of the symbol, respectively
For massive MIMO deployment, low-complexity decoding of 16x16 64QAM is developed [3], where K-best algorithm collaborated with SD and reduced the number of visited nodes by an order of magnitude, e.g., only ~10 nodes
.
Observed portion of sounding symbol | 3/4 | 1/2 | 1/3
No. of taps | 5-7 | 8-10 | 11-15
Notes: Complexity scaling, sphere decoder grid

## Slide 15: Complexity doesn’t go up exponentially
The complexity doesn’t increase with the QAM size exponentially
The number of visited nodes depends on the SNR and should be less than 10 for 40dB SNR [3]
It is even possible for the attacker to attack 2/3 of symbol
All constellation points except a handful in a large constellation, e.g., 4kQAM are not visited
y
log2N

## Slide 16: Limitation of FD Attack
No attack signal is sent during the observation window
Attack efficiency can be improved by sending attack signal in the observation window
Time
Time
No attack signal sent
Genuine signal
Attack signal

## Slide 17: Time Domain Attack
Attacker receives one signal sample and sends out one attack sample
Slide 17
Relay on a different band

## Slide 18: Exploiting Correlation in Sounding Signal
Wiener filter predicts the future signal by exploiting the correlation between the signal previously received and the future signal unreceived
Slide 18
Nov 2020
Received signal
Future signal
Correlation
Time advancement of attack signal, e.g., 3, 4, 5 samples

## Slide 19: Linear MMSE Estimator
Wiener filter predicts the future signal by exploiting the correlation between the signal previously received and the future signal unreceived
Wiener filter is of low complexity, O(N2),
Slide 19
Nov 2020
pi
×
p2
p1
p126
…
, where
Bank of filters

## Slide 20
The received signal can be written as
Symbols sent sequentially
Time-domain signal vector for the 1st pulse
Slide 20
Nov 2020
where
Equations are determined after oversampling
Derivation of LMMSE predictor
Time-domain signal vector for the last pulse

## Slide 21
The signal under prediction can be written as
t
Slide 21
Nov 2020
The row of H corresponding to the predicted signal t
The Signal under Prediction

## Slide 22: Linear MMSE Solution
Linear MMSE solution of is given by
Slide 22
Nov 2020
where
+ I

## Slide 23: Pulse Representation of OFDM Signal
OFDM signal can be viewed as a sequence of correlated, Gaussian distributed pulses sent in time, whose pulse shape is determined by frequency domain window
.
IFFT
F
T
QAM
Gaussian
F
T

## Slide 24: Pulse shape determines the correlation
The time-domain correlation is determined by the pulse shape (or frequency-domain window) not the modulation, i.e., OFDM or pulse modulation
.

## Slide 25: What does secure pulse look like?
Slide 25
Information is confined within the pulse width
No information is leaked before the interval
No signal for the attack to change after the pulse interval
Time
Phase and amplitude info
No info about the pulse
Pulse width
No signal to change

## Slide 26: Meeting Spectrum Requirement
Slide 26
Zero power at DC subcarrier
Freq
DC

## Slide 27: Windows and Pulse Shapes
Slide 27
Rectangular, Raised-Cosine (β=0.15), and differential Blackman

## Slide 28: Tail Truncated Pulse (1/2)
Slide 28
The truncated, differential, Hamming pulse with two opposite Hamming sub-pulses has no DC power
Set the tails to zero for full security

## Slide 29: Trail Truncated Pulse (2/2)
The mask weights consist of purely imaginary numbers. No complex multiplication is needed.
Rx doesn’t have to over-sample the received signal, the degradation due to aliasing is negligible, i.e., -34.1dB,

## Slide 30: Simulation Setting
20 MHz bandwidth, 40 dB SNR
Wiener filters generate each attack signal sample
4x oversampling, i.i.d. noise
4kQAM OFDM and BPSK time-domain pulse
FD windows: Rectangular, Raised-Cosine β=0.15, differential Blackman, truncated differential Hamming
Time advancement: 2, 3, 4 Ts, where Ts = 1 / Bandwidth
Received signal
Future signal
Correlation
Time advancement of attack signal, e.g., 3, 4, 5 samples

## Slide 31
Correlation CDF for Time Domain Pulse

## Slide 32
Rectangular and Raised-Cosine
Raised-Cosine is better than Rectangular
Gap

## Slide 33
Diff Blackman and Truncated Diff Hamming
Approach ideal

## Slide 34
Correlation CDF for OFDM

## Slide 35
Rectangular and Raised-Cosine
Raised-Cosine is better than Rectangular
Gap

## Slide 36
Diff Blackman and Diff Hamming
Gap

## Slide 37: Remarks
Without FD windowing or TD pulse shaping, the residual correlation is above 0.3, whose attack signal quality is better than CP replay attack
FD windowing or TD pulse shaping is essentially to reduce the attack signal quality
The FD windowing or TD pulse shaping improves both OFDM and TD pulse signals in similar ways
Ideal performance can be achieved for time advancement of 4 samples with proper windowing/shaping

## Slide 38: Compound Attack to OFDM Signal
Within the observation window of the FD attack, TD attack, e.g., linear MMSE attack can continuously send attack signal such that the attack quality is substantially improved
Time
Time
Genuine signal
Attack signal
TD attack
FD attack

## Slide 39: Conclusions
Time-domain attack is developed
TD attack such as linear MMSE filter is of low implementation complexity
TD attack has similar performances in attacking OFDM and TD pulse
Sounding signal without FD windowing or TD pulse shaping is vulnerable to TD attack
TD attack can work together with FD attack to attack OFDM signal

## Slide 40: Reference
        [1] Q. Li, F. Jiang, X. Chen, and R. Stacey, “Attacks to Fully Random QPSK Sounding Signal,” doc: IEEE 802.11-20-0710r1.
        [2] F. Jiang, Q. Li, X. Chen, and R. Stacey, “Attacks to Fully Random 64QAM Sounding Signal,” doc: IEEE 802.11-20-0964r0.
        [3] A. Dabah, et al., “Performance / Complexity Trade-os of the Sphere Decoder Algorithm for Massive MIMO Systems,” https://arxiv.org/pdf/2002.09561.pdf.
        [4] C. Berger, “Secure LTF using DFT Precdoded OFDM,” doc: IEEE 802.11-20-1097r1.
        [5] B. Tian, et al., “11az Secure LTF Design,” doc: IEEE 802.11-20-836r0.

## Slide 41: Backup

## Slide 42: Illustration of Correlation among OFDM Samples (1/2)
PAM with constellation {-3, -1, +1, +3}
Two samples of 4-PAM in “frequency domain” and are converted to “time domain” by “FFT matrix”
.
P
F
T
4-PAM

## Slide 43: Illustration of Correlation among OFDM Samples (2/2)
Just observing the 1st time-domain sample, the attacker can determine both 4-PAM symbols in “frequency-domain” uniquely
Namely, the 2nd TD sample is not secure because it is exposed ahead of time and can be determined from the 1st sample
.
(-3,-3)
(3,3)
(3,1)
(-3, -1)

## Slide 44: Reducing Out-of-Band Emission by Pulse Removal
Slide 44
Removing the first and last 4 pulses, i.e., adding 0s to the +/-1 sequence, easily eliminates the out-of-band emission. No TD window is needed.
…
Out-ofband emission
Time
Symbol duration
Zero-power GI
0 0 +1 +1 …
T
This Photo by Unknown Author is licensed under CC BY-NC

## Slide 45: Easy Compliance with Spectrum Mask
Slide 45
Easily meet IEEE spectrum mask without additional time-domain windowing

## Slide 46: MatLab Code for T.D.H. Pulse (1/2)

## Slide 47: MatLab Code for T.D.H. Pulse (2/2)