## Slide 1: BW Indication of >160MHz for non-HT and non-HT Duplicated Frames
Date: 2020-08-10
Authors:
Name | Affiliations | Address | Phone | Email
Yunbo Li | Huawei | Shenzhen, China |  | liyunbo@Huawei.com
Yiqing Li |  |  |  | 
Yuchen Guo |  |  |  | 
Ming Gan |  |  |  | 
Guogang Huang |  |  |  | 
Rob Sun |  |  |  | 
Chenchen Liu |  |  |  | 
Wei Lin |  |  |  | 
Jia Jia |  |  |  | 
Notes: September 2012

## Slide 2: Background
Indicate a bandwidth larger than 160MHz in non-HT or non-HT duplicated frames passed motion [1];
  802.11be supports indicating BW larger than 160 MHz through scrambler sequence in non-HT or non-HT duplicated frames. [Motion 115, #SP102, [10] and [87]]
When a new bandwidth is indicated, we need to guarantee the receiver side can clear know whether the new bandwidth information is carried;
Current CH_BANDWIDTH_IN_NON_HT is indicated through Individual/Group bit in TA, but it can not be used to indicate new larger bandwidth.
  Otherwise, receiver STA don’t understand only 20, 40, 80 or 160MHz are indicated through B5B6 in scrambling sequence or new bandwidth is indicated.
Two main points will be discussed in this presentation:
  1) how to indicate the new bandwidth is carried, we call it EHT BW indication in following slides;
  2) which new bandwidth(s) can be carried.

## Slide 3: Explicit Solutions for EHT BW Indication
Two potential places can be used for EHT BW indication
Solution 1: Reserved bits in Frame Control
  There are several subfields (e.g. B8-B11) are reserved and set to 0, it may could be used for EHT BW indication;
  B8-B11 is used for Bandwidth Indication and Dynamic Indication subfields in S1G;
  But base on discussion during 11ac and 11ax periods, some chip vendors have concern to reuse these subfields in 2.4GHz and 5GHz due to vendor specific implementation reasons.
Frame Control field of Control frame in a non-S1G PPDU

## Slide 4: Explicit Solutions for EHT BW Indication
Solution 2: last 9 reserved bits in SERVICE field
  The remaining 9 bits (7–15) of the SERVICE field shall be reserved for future use. All reserved bits shall be set to 0 on transmission and ignored on reception. (from 802.11REVmd D3.0, section 17);
  It could be a good place to carry ETH BW indication;
  SERVICE field already been used on several type of PPDUs
    B8-B15 of SERVICE field in VHT PPDU are used for CRC of VHT-SIG-B
    Scrambler is extended from 7 to 11 bits in EHT PPDU
  The designs in this presentation only used in non-HT PPDU. The designs in VHT and EHT PPDUs will not affect the design here.
SERVICE field

## Slide 5: Explicit Solutions for EHT BW Indication
Let’s further discuss how many new BW modes can be carried
Opt 1: only indicates non-puncture BW modes
  Can reuse B5B6, or just add one more bit (e.g. B3) to indicate the new BW modes (e.g. 320MHz)
Opt 2: indicates non-OFDMA preamble puncture modes
  There are totally 63 modes (see appendix), need 6 bits for indication
  Need to use the bits in Reserved SERVICE Bits
Opt 3: indicates full flexible puncture modes
  Needs 16 bits for 320MHz if use the granularity of 20MHz. There are not enough bits in SERVICE field;
  A simple way is to add the granularity to 40MHz for 320MHz, so 8 bits are enough;
    One extra bit is needed to distinguish <320MHz and 320MHz
SERVICE field

## Slide 6: Implicit Solution for EHT BW Indication
Besides previous explicit solutions, there is also an implicit way for EHT BW indication;
  Pros: Doesn’t need a bit for EHT BW indication; Don’t need to use the reserved SERVICE bits
  Cons: if reserved SERVICE bits are not used, only can carry non-preamble puncture modes
The receiver STA will know whether the new BW modes are carried based on the category of the TX STA
  If the TX STA is an EHT STA, and TA field is a bandwidth signaling TA, then new BW may be carried
  If the TX STA is an non-EHT STA, and TA field is a bandwidth signaling TA, then B5B6 in service field are used to indicate 20, 40, 80, or 160MHz.
Control response (e.g. CTS) usually implemented in low MAC layer, it means that a EHT STA needs to distinguish whether a TX STA is EHT STA or not in low MAC;
It is implementable base on the feedback from product line, and the complexity is acceptable, but it may needs each chip vendor to implement it in low MAC.

## Slide 7: Summary
Indicate a bandwidth larger than 160MHz in non-HT or non-HT duplicated frames passed motion;
Explicit and implicit solutions are provide
  Explicit solution needs to use Reserved SERVICR bits, but can get enough bits to carry preamble puncture modes
  Implicit solution doesn’t need to use reserved SERVICR bits, but only can carry non-preamble puncture modes without using reserved SERVICR bits
  Implicit solution may needs to distinguish the category of TX STA in low MAC

## Slide 8: Straw Poll 1
Which solution do you prefer to indicate BW larger than 160MHz in non-HT or non-HT duplicated frames?
  Opt 1: explicit solution
  Opt 2: implicit solution

## Slide 9: Straw Poll 2
Do you agree to use one bit of Reserved SERVICE bits to indicate whether a BW mode that different from 20MHz, 40MHz, 80MHz, 160MHz or 80+80MHz is carried in a non-HT or non-HT duplicated frame?

## Slide 10: Straw Poll 3
Which option do you prefer to indicate BW larger than 160MHz in non-HT or non-HT duplicated frames?
  Opt 1: only indicates non-puncture BW modes
  Opt 2: indicates non-OFDMA preamble puncture modes
  Opt 3: indicates more flexible modes than non-OFDMA preamble puncture

## Slide 11: Reference
[1] 11-20-0616-00-00be-bandwidth-indication-of-320mhz-for-non-ht-and-non-ht-duplicate-frames

## Slide 12: Appendix

## Slide 13: BW modes for non-OFDMA Preamble Puncture
Total BW | BW modes | Numbers
20MHz | 1 | 1
40MHz | 11 | 1
80MHz | 1111 x111 1x11 11x1 111x | 5
160MHz | 1111 1111 x111 1111 1x11 1111 11x1 1111 111x 1111 1111 x111 1111 1x11 1111 11x1 1111 111x xx11 1111 11xx 1111 1111 xx11 1111 11xx | 13
Total BW | BW modes | Numbers
320MHz | 1111 1111 1111 1111 xx11 1111 1111 1111 11xx 1111 1111 1111 1111 xx11 1111 1111 1111 11xx 1111 1111 1111 1111 xx11 1111 1111 1111 11xx 1111 1111 1111 1111 xx11 1111 1111 1111 11xx xxxx 1111 1111 1111 1111 xxxx 1111 1111 1111 1111 xxxx 1111 1111 1111 1111 xxxx xxxx xx11 1111 1111 xxxx 11xx 1111 1111 xxxx 1111 xx11 1111 xxxx 1111 11xx 1111 xxxx 1111 1111 xx11 xxxx 1111 1111 11xx xx11 xxxx 1111 1111 11xx xxxx 1111 1111 1111 xxxx xx11 1111 1111 xxxx 11xx 1111 1111 xxxx 1111 xx11 1111 xxxx 1111 11xx xx11 1111 xxxx 1111 11xx 1111 xxxx 1111 1111 xx11 xxxx 1111 1111 11xx xxxx 1111 1111 1111 xxxx xx11 1111 1111 xxxx 11xx xx11 1111 1111 xxxx 11xx 1111 1111 xxxx 1111 xx11 1111 xxxx 1111 11xx 1111 xxxx 1111 1111 xx11 xxxx 1111 1111 11xx xxxx xxxx xxxx 1111 1111 xxxx 1111 xxxx 1111 xxxx 1111 1111 xxxx 1111 xxxx xxxx 1111 1111 xxxx 1111 xxxx 1111 1111 xxxx xxxx | 43
Totally 1+1+5+13+43 = 63 modes