## Slide 1: BW320 Signaling
Date: 2020-09-14
Authors:
Name | Affiliations | Address | Phone | email
Ron Porat | Broadcom |  |  | ron.porat@broadcom.com

## Slide 2: Abstract
320MHz channelization has been defined as any two contiguous 160MHz channels [1][2]
Propose to explicitly signal whether a transmission is occupying the light blue or the dark blue set of channels

## Slide 3: Proposed U-SIG BW Signaling
Transmission of 20/40/80/160MHz PPDU is unambiguous in terms of its frequency location since channels are non-overlapping.
However due to the partially overlapping nature of 320MHz channels, a 320MHz device in a 320MHz BSS hearing a 320MHz non-OFDMA PPDU is guaranteed to fail decoding if the PPDU belongs to the other set (sets denoted below by -1 and -2). It is undesirable to enable STA decode PPDU they are bound to fail.
Propose to signal the exact set the PPDU belongs to by having two entries in U-SIG, namely 320_1, 320_2. This will also help identify OBSS PPDU.
UNII5 |  |  |  |  |  | UNII6 | UNII6/7 | UNII7 |  |  | UNII7 /8 | UNII8 | 
80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80
160 |  | 160 |  | 160 |  | 160 |  | 160 |  | 160 |  | 160 | 
320-1 |  |  |  | 320-1 |  |  |  | 320-1 |  |  |  |  | 
 |  | 320-2 |  |  |  | 320-2 |  |  |  | 320-2 |  |  | 

## Slide 4: References
[1] 20/0953 - 320MHz Channelization
[2] 20/1229 – PDT phy channel numbering and channelization

## Slide 5: SP #1
In addition to four entries for 20/40/80/160MHz, do you support having two entries in U-SIG BW field for 320 MHz?
  320-1 if PPDU channel center frequency is 31, 95, 159
  320-2 if PPDU channel center frequency is 63, 127, 191