## Slide 1: HE ER SU PPDU for Control Frame
Date: 2020-09-16
Authors:

## Slide 2: Introduction
In Draft P802.11ax_D7.0 sub-clause 26.15.2, the spec defines the frame format for control frame as follows:
According to this content, HE ER SU PPDU is only applicable for control frame after association. Prior to association, control frames shall be transmitted in non-HT format according to Draft P802.11REVmd_D4.0 sub-clause 10.6.6.1.
A Control frame sent by an HE STA as a response to an HE ER SU PPDU that does not contain a Trigger frame or frame carrying a TRS Control field should be carried in an HE ER SU PPDU unless the most recently received PPDU sent by a recipient of the HE ER SU PPDU to the HE STA after association was not an HE ER SU PPDU in which case the Control frame should be carried in non-HT PPDU.
A Control frame sent by an HE STA as a response to an HE SU PPDU or a non-HT PPDU that does not contain a Trigger frame or frame carrying a TRS Control field should be carried in a non-HT PPDU unless the most recent received PPDU sent by a recipient of the HE SU PPDU to the HE STA after association was an HE ER SU PPDU in which case the Control frame should be carried in an HE ER SU PPDU

## Slide 3: Association Frame Exchange Sequence
When the STA is far from the AP, with smaller STA transmitting power, AP and STA have unbalanced link.
In the association stage, probe request, authentication request and association request, which are management frames, can be sent using HE ER SU PPDU to extend the STA transmission range.
However, the ACK frames for probe response, authentication response and association response may not be heard by the AP.
AP may send authentication response and assoc. response many times, which lead to large overhead.

## Slide 4: Suggestion and Remaining Issues
Hence, we propose to make it possible to transmit ACK in HE ER SU PPDU format during the association stage
However, tracking state of each STA is done after association. Therefore, AP cannot correctly set NAV in frames that solicit ACK carried in ER SU PPDU.
Possible solution to solve unbalanced link and the NAV duration issue could be
  AP calculate duration for HE ER SU ACK prior association
  Allow STA to violate the duration field of the soliciting frames during association stage
  Define mechanism to require AP to transmit trigger for RARU
  Other solutions

## Slide 5: Possible Change
  Opt 1: Add the following lines in the spec:
  “Prior to association, a control frame sent by an HE STA should be carried in an HE ER SU PPDU if it does not violating the duration field defined in the frame that solicits the control frame in any of these two scenarios: 1. it is a response to an HE ER SU PPDU that does not contain a triggering frame, unless the most recent PPDU sent by this HE STA to the recipient(s) of this control frame was not an HE ER SU PPDU 2. it is a response to an HE SU PPDU or a non-HT PPDU that does not contain a triggering frame and the most recent PPDU sent by this HE STA to the recipient(s) of this control frame was an HE ER SU PPDU.”
  Opt 2: Remove the term “after association” in the restrictions.
  Opt 3: Add condition for AP to support RARU.

## Slide 6: SP 1
Do you agree to add the following words to Draft P802.11ax_D7.0 sub-clause 26.15.2?
  Y:
  N:
  A:
  “Prior to association, a control frame sent by an HE STA should be carried in an HE ER SU PPDU if it does not violating the duration field defined in the frame that solicits the control frame in any of these two scenarios: 1. it is a response to an HE ER SU PPDU that does not contain a triggering frame, unless the most recent PPDU sent by this HE STA to the recipient(s) of this control frame was not an HE ER SU PPDU 2. it is a response to an HE SU PPDU or a non-HT PPDU that does not contain a triggering frame and the most recent PPDU sent by this HE STA to the recipient(s) of this control frame was an HE ER SU PPDU.”

## Slide 7: SP 2
Do you agree to remove the term “after association” in the following paragraph in Draft P802.11ax_D7.0 sub-clause 26.15.2?
  Y:
  N:
  A:
A Control frame sent by an HE STA as a response to an HE ER SU PPDU that does not contain a Trigger frame or frame carrying a TRS Control field should be carried in an HE ER SU PPDU unless the most recently received PPDU sent by a recipient of the HE ER SU PPDU to the HE STA after association was not an HE ER SU PPDU in which case the Control frame should be carried in non-HT PPDU.
A Control frame sent by an HE STA as a response to an HE SU PPDU or a non-HT PPDU that does not contain a Trigger frame or frame carrying a TRS Control field should be carried in a non-HT PPDU unless the most recent received PPDU sent by a recipient of the HE SU PPDU to the HE STA after association was an HE ER SU PPDU in which case the Control frame should be carried in an HE ER SU PPDU