## Slide 1: Discussion on Multi-link Setup
Date: 2020-09-02
Authors:
Name | Affiliations | Address | Phone | Email
Guogang Huang | Huawei |  |  | huangguogang1@huawei.com
Ming Gan |  |  |  | 
Yuchen Guo |  |  |  | 
Yunbo Li |  |  |  | 
Yiqing Li |  |  |  | 
Mengyao Ma |  |  |  | 
Notes: September 2012

## Slide 2: Introduction
The following consensus has been reached
  Enable/disable is govern by TID-to-link mapping. In other words, enable/disable is the result of TID-to-link mapping
    Note that frame exchange on a link is subject to the power state of the corresponding non-AP STA.
  [Motion 106, [30] and [235]] An AP MLD can recommend a non-AP MLD to use one or more enabled links.
    The AP’s indication could be carried in a broadcast or a unicast frame.
In this contribution, we seek to clarify how to signal the multi-link setup and link recommendation

## Slide 3: Scenario Considered
For the AP MLD, it has three links which respectively operates at 2.4 GHz, 5 GHz and 6 GHz
For a multiple-radio non-AP MLD，assume that it has two radios, one is only for the 2.4 GHz band, the other one is for either 5 GHz band or 6 GHz band.
When the non-AP MLD requests to setup three links, then link 1 and link 2 will share a common physical STA, as illustrated in the below figure

## Slide 4: Proposal

## Slide 5: Radio ID
According to the following motion, a Radio ID subfield may be needed when a non-AP MLD has multiple affiliated physical STAs
  [Motion 106, [30] and [235]] An AP MLD can recommend a non-AP MLD to use one or more enabled links.
    The AP’s indication could be carried in a broadcast or a unicast frame.
If multiple Per-STA profiles have the same Radio ID, that means these links share a common physical STA.
  The Radio ID of STA transmitted (Re-)Association Request frame is 0 by default.
The Radio ID also can be used in the following operations
  Giving more information to AP to decide the TID-to-link mapping at association time or later
  Change the STA-AP mapping at the association time or later [2].
    Note when only one MAC address for a non-AP MLD is adopted by 11be group in the future [3], there is a need to distinguish affiliated STAs

## Slide 6: Radio ID (Cont.)
Example. Change the STA-AP mapping
  Assuming that AP MLD has three links, which respectively operates at 2.4 GHz (corresponding link 0), 5 GHz (corresponding link 1) and 6 GHz (corresponding link 2)
  Non-AP MLD has three switchable radios which can operate at 2.4 GHz, 5 GHz and 6 GHz, but with different capabilities
Request to setup the following links:
<Link 0, Radio 0>,
<Link 1, Radio 1>,
<Link 2, Radio 2>
Non-AP MLD
AP MLD
(Re)Association Request
(Re)Association Response
Accept to setup the following links:
<Link 0, Radio 0>,
<Link 1, Radio 2>
<Link 2, Radio 1>
Request to setup the following links:
<Link 0, Radio 0>,
<Link 1, Radio 1>,
<Link 2, Radio 2>
Non-AP MLD
AP MLD
(Re)Association Request
(Re)Association Response
Accept to setup the following links:
<Link 0, Radio 0>,
<Link 1, Radio 2>
Case 1. Association time
Case 2. After association time
Recommend to setup <Link 2, Radio 1>

## Slide 7: Power Management and Capability Information
The non-AP MLD can explicitly indicate the power management of each non-transmitting link after the multi-link setup
  Active mode
  Power save mode and its power state is doze by default
This is helpful to reduce the latency of the delay-sensitive traffic when the non-AP MLD is roaming to a new AP MLD
There are two options for the Capability Information indication
  Option 1. Capability Information is MLD-level
  Option 2. Capability Information is link-level
    But the values of some subfields in Capability Information field must keep consistent, e.g. ESS, IBSS, APSD subfields

## Slide 8: Status Code
In the current Spec., the AP MLD maybe accept or reject some requested links with one of the following Status Code values [4]:
  0: SUCCESS
  1: REFUSED_REASON_UNSPECIFIED
  10: REFUSED_CAPABILITIES_MISMATCH
  11: DENIED_NO_ASSOCIATION_EXISTS
  12: DENIED_OTHER_REASON
  17: DENIED_NO_MORE_STAS
  18: REFUSED_BASIC_RATES_MISMATCH
  19: DENIED_NO_SHORT_PREAMBLE_SUPPORT
  22: REJECTED_SPECTRUM_MANAGEMENT_REQUIRED
  23: REJECTED_BAD_POWER_CAPABILITY
  24: REJECTED_BAD_SUPPORTED_CHANNELS
  25: DENIED_NO_SHORT_SLOT_TIME_SUPPORT
  27: DENIED_NO_HT_SUPPORT
  30: REFUSED_TEMPORARILY
  33: DENIED_INSUFFICIENT_BANDWIDTH
  34: DENIED_POOR_CHANNEL_CONDITIONS
  35: DENIED_QOS_NOT_SUPPORTED
  51: DENIED_LISTEN_INTERVAL_TOO_LARGE
Most of them can be link-level.
  92: REFUSED_EXTERNAL_REASON
  93: REFUSED_AP_OUT_OF_MEMORY
  94: REJECTED_EMERGENCY_SERVICES_NOT_SUPPORTED
  99: DENIED_WITH_SUGGESTED_BAND_AND_CHANNEL
  103: DENIED_DUE_TO_SPECTRUM_MANAGEMENT
  104: DENIED_VHT_NOT_SUPPORTED

## Slide 9: Status Code (Cont.)
Then the AP MLD needs to respectively indicate whether the requested link is set up successfully through a corresponding Status Code subfield
  If the transmitting link is rejected, then the association is considered failed
  If the transmitting link is accepted and all of non-transmitting links are rejected, then the STA-level association is considered successful
  If the transmitting link is accepted and at least one of non-transmitting links is accepted, then the MLD-level association is considered successful

## Slide 10: Link Recommendation
AP MLD can send a Link Recommendation notification to the non-AP MLD through one link, which includes the following info
  Recommended link ID
  Change Sequence of the recommended link ID
  (optional) Reason code
    e.g. overload, low RSSI, traffic steering and so on
When the Change Sequence value is different from the locally stored Change Sequence value of the recommended link, the non-AP MLD may send a Probe Request frame with the locally stored Change Sequence in the recommended link
Then AP MLD may reply a Probe Response frame with the corresponding elements whose contents are changed

## Slide 11: Conclusion
We discussed how to signal the Multi-link setup and enable fast link transition. We prefer the links to be setup to be explicitly indicated by inclusion the corresponding Per-STA Profile subelement.
We also proposed that the non-AP includes information of Radio ID in the Per-STA Profile subelement to help the indication of which links sharing a common STA
We also proposed that the non-AP/AP MLD indicates the Power Management for the non-transmitting link in the Per-STA Profile subelement
We also proposed that the AP MLD decides whether or not to accept the setup of each non-transmitting link through Status Code in the Per-STA Profile subelement

## Slide 12: SP 1
Do you support that
  A non-AP MLD with more than one affiliated STA includes a Radio ID field in the Per-STA Profile subelement of a multi-link element included in Association Request frame?

## Slide 13: SP 2
Do you support that
  an AP MLD separately signals whether to accept each request link through a Status Code field in the corresponding Per-STA profile?

## Slide 14: SP 3
Do you support to indicate the Power Management for each non-transmitting link after the multi-link setup as following?
  Active mode
  Power save mode and its power state is doze by default

## Slide 15: Reference
[1] 11-20-1274-02-00be-mac-pdt-mlo-ml-ie-structure.docx
[2] 11-20-1554-01-00be-ml-reconfiguration.pptx
[3] 11-20-1890-00-00be-reconsideration-on-sta-mac-address-of-non-AP-mld.ppt
[4] IEEE 802.11 Rmd 5.0