## Slide 1: TID-to-Link Mapping Negotiation
Date: 2020-09-02
Authors:
Name | Affiliations | Address | Phone | Email
Guogang Huang | Huawei |  |  | huangguogang1@huawei.com
Ming Gan |  |  |  | 
Yuchen Guo |  |  |  | 
Yunbo Li |  |  |  | 
Yiqing Li |  |  |  | 
Mengyao Ma |  |  |  | 
Notes: September 2012

## Slide 2: Introduction (1)
We have the following consensus [1]
  The TID-to-link mapping can be updated after multi-link setup through a negotiation, which can be initiated by any MLD.
    Format TBD.
    NOTE – When the responding MLD cannot accept the update, it can reject the TID-to-link mapping update.

## Slide 3: Introduction (2)
On the one hand, the non-AP MLD may initiate the TID-to-link mapping negotiation request for the following reason(s):
  Link unreachability
  Power save
  Bad QoS for some TID
On the other hand, the AP MLD also can initiate the TID-to-link mapping negotiation request for the following reason(s):
  Admission control based on the type of STAs, STA capabilities and so on
  Load balance
  Separation of delay-sensitive traffic and delay-tolerant traffic
  Separation of downlink traffic and uplink traffic

## Slide 4: Problem Statement
Moreover, if considering that the TID is directional, there are 16 TIDs and each TID may have the different link set
However, the responder may accept or reject the proposed mapping
So the question is how to reduce the number of TID-to-link mapping negotiation and speed up the convergence of the final TID-to-link mapping scheme
TID-to-link Mapping Response
TID-to-link Mapping Request
Non-AP MLD (AP MLD)
AP MLD (Non-AP MLD)
Time

## Slide 5: Proposed Solution (1)
If a non-AP MLD initiates a TID-to-link mapping negotiation, some auxiliary information can be provided to assist the AP MLD to decide the final TID-to-link mapping, e.g.
  Info on Link RSSI Report or Disable Link Set if the TID-to-link mapping negotiation is initiated due to the link unreachability
  Info on Max Number of Enable Links or Disable Link Set if the TID-to-link mapping negotiation is initiated due to the power save
  Info on QoS Report if the TID-to-link mapping negotiation is initiated due to the bad QoS of delay-sensitive TID(s)

## Slide 6: Proposed Solution (2)
Since these auxiliary information is optional, there are two options to signal whether the corresponding info is present
  Option 1. Use a control bit to indicate whether the corresponding info field is present
  Option 2. Define the corresponding info as optional Report elements

## Slide 7: Summary
This contribution proposes that the non-AP MLD provides some auxiliary information to assist the AP MLD to decide the final TID-to-link mapping
  Info on Link RSSI Report or Disable Link Set if the TID-to-link mapping negotiation is initiated due to the link unreachability or some reason
  Info on Max Number of Enable Links or Disable Link Set if the TID-to-link mapping negotiation is initiated due to the power save
  Info on QoS Report if the TID-to-link mapping negotiation is initiated due to the bad QoS of delay-sensitive TID(s)

## Slide 8: Reference
[1] 11-20-0566-69-00be-compendium-of-straw-polls-and-potential-changes-to-the-specification-framework-document.docx

## Slide 9: SP 1
Do you support that
  If a non-AP MLD initiates a TID-to-link mapping negotiation, it may provide Disable Link Set to assist the AP MLD to decide the final TID-to-link mapping?
    How to indicate Disable Link Set is TBD
  Yes
  No
  Abstain

## Slide 10: SP 2
Do you support that
  If a non-AP MLD initiates a TID-to-link mapping negotiation, it may provide a QoS Report to assist the AP MLD to decide the final TID-to-link mapping?
    How to indicate QoS Report is TBD
  Yes
  No
  Abstain