## Slide 1: Wi-Fi FTM Timestamp Optimization
Date: Oct 15, 2020
Authors:

## Slide 2: Issue with current time-stamp reporting
‘Passive TB Ranging broadcasting large number of 48 bit timestamps occupying many OFDM symbols.’

## Slide 3: Time-stamp Resolution
Currently we use 48 bits in units of 1 picosecond = 0.3 mm
A resolution of 128 ps = 3.84 cm should be enough.
By reducing the resolution we can save bits!

## Slide 4: Time-stamp Max Value
Current timestamps span 0 to 218 seconds = 84 million km.
We don’t need timestamps that can span this long times and/or propagation distances
By reducing the max value we can save bits!

## Slide 5: Ranging Ambiguity – High level
The basic ambiguity range is:
R_amb = c*T_timestamp_max/2
However, when taking the differences in the clock rates into account we actually get two slightly different range ambiguities for the differential range ranging case.

## Slide 6: Resolving Differential Range Ambiguity 1(5)
Again:
Let t1_I and t4_I be the TOD and TOA time stamps for the ISTA, in the ISTA’s clock domain.
Let t2_R and t3_R be the TOA and TOD time stamps for the RSTA, in the RSTA’s clock domain.
Let t5_P and t6_P be the TOA time stamps for the PSTA, in the PSTA’s clock domain.
Furthermore:
Let t1_P and t4_P be the TOD and TOA time stamps for the ISTA, in the PSTA’s clock domain.
Let t2_P and t3_P be the TOA and TOD time stamps for the RSTA, in the PSTA’s clock domain.
Let t_P = (1+a_I)t_I+b_I define how a timestamp, t_P, in the PSTA’s clock domain relates to a timestamp, t_I, in the ISTA’s clock domain, where a_I is the differential rate of the PSTA’s clock as compared to the ISTA’s clock, and b_I is an offset.
Let t_P = (1+a_R)t_R+b_R define how a timestamp, t_P, in the PSTA’s clock domain relates to a timestamp, t_R, in the RSTA’s clock domain, where a_R is the differential rate of the PSTA’s clock as compared to the RSTA’s clock, and b_R is an offset.
Let t_R_r = t_R mod T_timestamp_max be the value of the RSTA timestamp reported to the ISTA, where T_timestamp_max is the max value for the representation of the timestamp before it wraps back to zero.
Let t_I_r = t_I mod T_timestamp_max be the value of the ISTA timestamp reported to the ISTA, where T_timestamp_max is the max value for the representation of the timestamp before it wraps back to zero.
Alternatively we can express this as
t_R = k*T_timestamp_max + t_R_r, where k is an integer (negative, zero or positive), and
t_I = k*T_timestamp_max + t_I_r, where k is an integer (negative, zero or positive).
Lets call k an ambiguity count.
.
RSTA
ISTA
t2_R
t1_I
t4_I
t3_R
R2I NDP
I2R NDP
t1_I_r, t4_I_r
I2R LMR
Broadcast of
RSTA and ISTA LMR
t2_R_r, t3_R_r, t1_I_r and t4_I_r
I2R NDP
R2I NDP
PSTA
t5_P
t6_P

## Slide 7: Resolving Differential Range Ambiguity 2(5)
Here we can write [1,2]:
DToF_PRI = t6_P – t5_P – 0.5t3_P +0.5t2_P – 0.5t4_P + 0.5t1_P
= t6_P – t5_P + 0.5(1+a_R)(t2_R - t3_R) + 0.5(1+a_I)(t1_I - t4_I)
= t6_P – t5_P + 0.5(1+a_R)(t2_R_r-t3_R_r) + 0.5(1+a_I)(t1_I_r – t4_I_r) +
0.5(1+a_R)(k2-k3)T_timestamp_max + 0.5*(1+a_I)(k1-k4)T_timestamp_max
where k2 and k3 are the ambiguity counters for the t2_R_r and t3_R_r time stamps, respectively, and k1 and k4 are the ambiguity counters for the t1_I_r and t4_I_r time stamps, respectively.
We get two, approximately equal, range ambiguities:
R_amb_R = c(1+a_R)T_timestamp_max/2, and
R_amb_I = c(1+a_I)T_timestamp_max/2.
(1)

## Slide 8: Resolving Differential Range Ambiguity 3(5)
Let us for the simplicity of the discussion here now ignore the propagation delays, or assume them to be small compared to the range ambiguities R_amb_R and R_amb_I .
We can then write (‘~=‘ stands for ‘approximately equal to’):
t2_P ~= t5_P and t3_P ~= t6_P
Substituting t2_P and t3_P with their representation in t2_R and t3_R we get:
(1+a_R)t2_R + b_R ~= t5_P, and
(1+a_R)t3_R + b_R ~= t6_P,
By substituting the t2_R and t3_R timestamps with the expressions for them in their reported values we get
(1+a_R)(t2_R_r + k2*T_timestamp_max) + b_R ~= t5_P, and (2)
(1+a_R)(t3_R_r + k2*T_timestamp_max) + b_R ~= t6_P. (3)
Subtract (3) from (2) to get:
(1+a_R)(t2_R_r – t3_R_r) + (1+a_R)*T_timestamp_max*(k2-k3) ~= t5_P – t6_P,
which gives us
k2-k3 ~= 1/((1+a_R)*T_timestamp_max)*[t5_P – t6_P – (1+a_R)(t2_R_r – t3_R_r)] (4)
Thus, we have a way to limit the possible values for k2-k3 and by the corresponding calculation we can limit k1-k4 by the approximate relation:
k1-k4 ~= 1/((1+a_I)*T_timestamp_max)*[t5_P – t6_P – (1+a_I)(t1_I_r – t4_I_r)] (5)
When T_timestamp_max is large compared to propagation times we can therefore resolve the ambiguities and uniquely determine the true differential range.

## Slide 9: Resolving Differential Range Ambiguity 4(5)
One way we can form estimates of the true values of k2-k3 and k4-k1 is as follows:
Line 1: k2mk3_int_est = round(k2mk3_raw_est);
Line2: k2mk3_rounding_error = k2mk3_int_est - k2mk3_raw_est;
Line 3: k1mk4_int_est = round(k1mk4_raw_est);
Line 4: k1mk4_rounding_error = k1mk4_int_est - k1mk4_raw_est;
Line 5: if (k2mk3_rounding_error - k1mk4_rounding_error) < 0
Line 6: if abs(k2mk3_rounding_error) > abs(k1mk4_rounding_error)
Line 7: k2mk3_int_est = k2mk3_int_est + 1;
Line 8: else
Line 9: k1mk4_int_est = k1mk4_int_est - 1;
Line 10: end
Line 11: end
Where:
k2mk3_raw_est = 1/((1+a_R)*T_timestamp_max)*[t5_P – t6_P - (1+a_R)(t2_R_r – t3_R_r)], and
k1mk4_raw_est = 1/((1+a_I)*T_timestamp_max)*[t5_P – t6_P - (1+a_I)(t1_I_r – t4_I_r)].
Once computed, replace k2-k3 and k1-k4 with the estimates k2mk3_int_est and k1mk4_int_est respectively in equation 1 for to compute DToF_PRI.

## Slide 10: Resolving Differential Range Ambiguity 5(5)
To resolve the ambiguities and enable finding the correct values for k2-k3 and k4-k1 we need to limit the ranging exchanges propagation distances.
For the estimates of k2-k3 and k4-k1 computed on the previous slide to work we need any propagation distance to be less than:
R_max = min(R_amb_R, R_amb_I) – R_margin ~= 1.25 km for 16 bits timestamps in units of 128 ps
where R_margin > 0 is a margin term. See the figure below:
RSTA
ISTA
PSTA
R_IR < R_max
R_IP < R_max
R_RP < R_max
The STA cannot be separated by more than about 1.25 km.

## Slide 11: Ambiguity Resolution Simulation
The calculations for resolving the ambiguities was tested in a differential range measuring simulation with the following parameter settings:
Max STA separation = 1.1 km
Stdev of TOA measurement error = 0.3 m
Max ‘detour distance’ between ISTA and RSTA = 10 m
Max clock rate difference for RSTA and ISTA w.r.t the PSTA = 60.0 ppm
Max error in PSTAs estimates of the RSTA’s and ISTA’s clock rates = 1 ppm (absolute)
Timestamp resolution = 128 ps
Number of bits in timestamp = 16
Max delay from t2 to t3 events = 5 ms
The resulting error in the differential range estimate after ambiguity resolution show that the method works here:

## Slide 12: Combined Short and Long Timestamps 1(3)
To enable keeping track of timestamps between ranging opportunities we need timestamps that can span times up to, say, 10s.
For this we pretty much need 48 bits as 2^48*128e-12 = 36029 s whereas if we use one byte less we get 2^32*128e-12 = 0.6 s.
A way to solve this problem is to use long timestamps with, say 48 bits, to represent the TOD timestamps and short timestamps with, say 16 bits, to represent the possibly more numerous TOA timestamps.
The long 48 bit TOD timestamp for all practical purposes gives us an unambiguous representation of the each measured TOD.
This means that we know t1_I. That is from the long timestamp we have for t1_I, lets call it t1_I_lr, we can deal with any (long) ambiguities and form an estimate of t1_I, denoted as:
t1_I_est.

## Slide 13: Combined Short and Long Timestamps 2(3)
From the long timestamp t1_I_lr, we can form a virtual reported short timestamp, t1_I_r, as:
t1_I_r = t1_I_lr mod T_timestamp_max_short,
where T_timestamp_max_short is the max value that the short timestamps wrap around.
We can now write:
t1_I_est = k1 * T_timestamp_max_short + t1_I_r
and compute:
k1 = (t1_I_est – t1_I_r)/T_timestamp_max_short.
Since we have a way to successfully estimate k4 – k1 with k1mk4_int_est as described earlier, we can calculate k4 as:
k4_est = k1 - k1mk4_int_est.
Thus we can compute an estimate of the unambiguous timestamp t4_I as:
t4_I_est = k4_est * T_timestamp_max_short + t4_I_r.

## Slide 14: Combined Short and Long Timestamps 3(3)
Correspondingly we can estimate t2_R as:
t3_R_r = t3_R_lr mod T_timestamp_max_short
k3 = (t3_R_est – t3_R_r)/T_timestamp_max_short,
k2_est = k3 + k2mk3_int_est, and
t2_R_est = k2_est * T_timestamp_max_short + t2_R_r.
By combining:
long 48 bit timestamps for the TOD timestamps and
short 16 bit timestamps for the TOA timestamps,
we can reconstruct the unambiguous times also for the TOA timestamps.

## Slide 15: Example Timestamp Reporting Overheads
N_ISTA | BW [MHz] | N_bits | Overhead | Overhead
9 | 40 | 48 | 0.41 ms | 27%
9 | 40 | 24 | 0.25 | 15%
9 | 40 | 16 | 0.16 ms | 11%
9 | 20 | 48 | 0.84 ms | 57%
9 | 20 | 24 | 0.47 | 31%
9 | 20 | 16 | 0.34 ms | 23%
Approximate timestamp overhead in ms and percentage of the complete Passive TB Ranging exchange.
Parameters used:
Broadcast MCS - BPSK rate 1/2
Unicast MCS - 16QAM rate ¾
All ISTA report TOAs for the NDPs from all other ISTAs
For the percentage overhead, only the preambles and the SIFS for the frames in the sequence has been used as the base.

## Slide 16: References
[1] 802.11az D2.4
[2] – ‘Scalable location performance’, Erik Lindskog, Naveen Kakani, and Ali Raissinia, IEEE.11-17/1371r0.

## Slide 17
Thank You!