## Slide 1: 802.11 WLAN and 3GPP 5G System Interworking
Date: 2020-10-06
Author:
Tutorial at IEEE 802 Plenary, October 2020

## Slide 2: Abstract
This document contains the tutorial slides for the 802 Tutorial on “802.11 WLAN and 3GPP 5G System Interworking”
It covers the overall system perspective on the integration and interworking of 802.11 WLAN access networks with the 3GPP 5G system. It provides a system overview of the 5G and WLAN interworking architecture, related functions, procedures, policies and interfaces as defined by 3GPP Releases 15 and 16. It highlights some key technical issues and gaps related to enabling WLAN and 5G system interworking and provides recommendations to guide and facilitate standardization effort to address these issues within the Wi-Fi related standards and/or 3GPP standard.
A technical report is submitted in IEEE AANI SC on WLAN and 5G interworking “Technical report on the interworking between 3GPP 5G system and WLAN” (IEEE 802.11-20/1376r0)

## Slide 3: Outline
Background: WLAN and 5G Interworking
WLAN Integration Architecture
  Untrusted and Trusted WLAN integration
  Support for Wi-Fi only devices
Interworking Related Functions
Interworking Challenges and Gaps
Technical Recommendations
Future Work – TSN Support

## Slide 4: Background: WLAN and 5G Interworking
With continued advancements in Wi-Fi (Wi-Fi 6/6E, Wi-Fi 7), Wi-Fi is well positioned to carry new breed of 5G applications e.g. AR/VR, industrial IoT, edge computing, autonomous driving
New 5G use cases have varied set of requirements on throughput, latency, coverage and reliability and can benefit from combined resources from 5G and Wi-Fi access networks
Interworking between Wi-Fi and 5G can address new market opportunities for emerging verticals and enterprises e.g. Industrial IoT and Connected Cities
Wi-Fi and 5G interworking enables seamless and interoperable services across 3GPP and Wi-Fi access
Cloud/App Level Interworking
Through above IP protocol e.g. MPTCP or MPQUIC. Deployed by Apple iTunes service.
Core Network Level Interworking
Interworking achieved through the 3GPP core network
Defined by 3GPP Release 15/16
Focus of this presentation
RAN Level Interworking
Interworking achieved within the RAN
LWA and LWIP for 3GPP 4G
Not defined for 3GPP 5G system
Interworking can be achieved at three different levels:

## Slide 5: WLAN and 5G Integration Architecture
3GPP 5G architecture supports UE connecting to 5G core network over WLAN access, without requiring primary connectivity over cellular access
5G supports WLAN access integration at the core network level through gateway functions (N3IWF, TNGF and TWIF) for untrusted and trusted WLAN
  PLMN operator makes the decision on whether a WLAN network is considered trusted or untrusted based on security features of WLAN access and/or other reasons
  UE may discover trust relationship for WLAN networks (e.g. over ANQP) or may be configured with trusted WLAN networks
5G core is designed to be access neutral - gateway functions for WLAN integration interface with the 5G Core using same N2/N3 interfaces as used by the 3GPP access
5G has adopted EAP based authentication framework, similar to Wi-Fi, for UE authentication with 5G core
5G signaling and user data are transported over IPsec tunnels established between UE and gateway functions over WLAN
PLMN: Public Land Mobile Network
ANQP: Access Network Query Protocol

## Slide 6: Untrusted WLAN Integration with 5G Core
Untrusted WLAN access is integrated with the 5G Core via N3IWF gateway function
N3IWF interfaces with 5G core over N2/N3 interfaces, used for 3GPP access
N3IWF and WLAN access interface through generic IP transport over Y2
NWu establishes IPsec security associations (SAs) between UE and N3IWF for secure transport of 5G NAS signaling and user data
IPsec SAs over NWu apply both encryption and integrity protection for 5G signaling and user data
N3IWF: Non-3GPP Interworking Function
AMF: Access and Mobility Management Function
UPF: User Plane Function

## Slide 7: Trusted WLAN Integration with 5G Core (1/2)
Trusted WLAN access is integrated with the 5G core via TNGF gateway function
Tight coupling between TNGF and trusted WLAN AP over a AAA based Ta interface
WLAN layer-2 authentication is tied to a key from TNGF, derived based on UE authentication with the 5G Core
NWt establishes IPsec security associations (SAs) between UE and TNGF for transport of 5G NAS signaling and user data
IPsec SAs over NWt apply NULL encryption for signaling & user data to avoid double encryption, since WLAN layer-2 encryption is trusted
TNGF: Trusted Non-3GPP Gateway Function

## Slide 8: Trusted WLAN Integration with 5G Core (2/2)
Devices that do not support 5G NAS signaling over trusted WLAN access (N5CW devices) can still connect to 5G Core over trusted WLAN via TWIF gateway function
TWIF implements NAS protocol on behalf of N5CW devices and performs registration and PDU session management over N1
N5CW device has a USIM and is authenticated with 5G core using EAP-AKA’ method
Like TNGF, WLAN layer-2 authentication is tied to a key derived based on UE authentication with 5G Core
An N5CW device may be a dual radio device operating as a 5G UE over 3GPP access (not shown for simplicity)
TWIF: Trusted WLAN Interworking Function
N5CW: Non-5G-Capable over WLAN
USIM: Universal Subscriber Identity Module
AKA: Authentication and Key Agreement

## Slide 9: Support for Wi-Fi Only Devices
Current 3GPP 5G architecture does not define support for Wi-Fi only devices w/o USIM
3GPP PLMN network only supports SIM based authentication methods (EAP-AKA’ and 5G-AKA), which require USIM on the UE
A Wi-Fi only UE with USIM supporting 5G NAS and user plane functionality over WLAN can connect to 5G core via N3IWF/TNGF
An N5CW Wi-Fi only device is also required to have a USIM
However, since most Wi-Fi only devices do not include a USIM, there is a gap to be addressed

## Slide 10: Interworking Functions
WLAN Access Network Selection
Registration and Authentication
PDU Session Management
UE Route Selection Policy (URSP)
Access Traffic Steering, Switching and Splitting (ATSSS)
5G QoS Model
User Data Transport

## Slide 11: WLAN Access Network Selection
5G policies for WLAN network selection are provided in the Access Network Discovery and Selection Policy (ANDSP) through WLAN Selection Policy (WLANSP) rules
WLANSP rules are used to select a preferred WLAN network for untrusted connectivity to 5G Core via N3IWF
WLANSP rules apply only when a WLAN access can not be selected based on user preferences
UE may decide to establish trusted WLAN connectivity based on UE configurations, capabilities, implementation procedure and types of WLAN network discovered
To connect to trusted WLAN access, UE follows following steps:
  Over ANQP, UE queries PLMNs with which trusted 5G connectivity is supported by WLAN networks
  UE then selects a PLMN to connect from the list of available PLMNs
  Finally, the UE selects a WLAN network providing trusted 5G connectivity to the selected PLMN, using WLANSP rules to prioritize and select a preferred WLAN network
Different WLAN network selection policies may exist on the UE (e.g. policies from end user, device manufacturer, applications, operator and enterprise IT) and interworking across these policies may be device OEM specific

## Slide 12: Registration and Authentication
UE registration with the 5G core over WLAN access is based on the registration procedure defined over the 3GPP access
A vendor specific EAP-5G method is defined by 3GPP to encapsulate NAS registration messages between UE and N3IWF/TNGF
UE authentication over WLAN access is done using EAP-AKA’ or 5G-AKA authentication method, like done over the 3GPP access
A signaling IPsec ESP security association (SA) is established between UE and N3IWF/TNGF during registration using IKEv2 protocol for transport of NAS messages over WLAN access
For untrusted WLAN, UE 5G core authentication happens after WLAN connectivity and authentication is completed
For trusted WLAN, WLAN layer 2 authentication is tied to the UE 5G core authentication
NAS: Non-Access Stratum, IKEv2: Internet Key Exchange Version 2

## Slide 13: IPsec SA over Untrusted WLAN
Signaling IPsec SA Establishment
Control plane for Signaling IPsec SA for Untrusted WLAN
First, UE associates and authenticates over untrusted WLAN access
Next, UE 5G registration/auth is executed over IKEv2, with 5G NAS messages encapsulated over EAP-5G
A signaling IPsec SA is established using common N3IWF key
Signaling IPsec SA applies both encryption and integrity protection
EAP-5G and IKEv2 protocols implemented by 3GPP access & N3IWF
No impact to WLAN STA and AP, however this results in double encryption
*Lower Layers represent L2/L1 for backhaul e.g. Ethernet

## Slide 14: IPsec SA over Trusted WLAN (1/2)
Signaling IPsec SA Establishment
UE establishes L2 association with trusted WLAN AP
UE provides 5G specific NAI in EAP-Response/Identity to trigger EAP-5G session from TNGF over Ta
After UE 5G core authentication, a TNAP key sent to WLAN AP and used as PMK for WLAN 4-way handshake
A signaling IPsec SA is established using common TNGF key
Signaling IPsec SA applies NULL encryption, to avoid double encryption

## Slide 15: IPsec SA over Trusted WLAN (2/2)
EAP-5G protocol is implemented as part of 3GPP Access on the UE and on the TNGF
Support for filtering EAP-5G messages at the WLAN AP
5G NAS messages encapsulated over EAP-5G, then encapsulated over AAA/RADIUS protocol over Ta interface and over IEEE 802.1x/EAPoL on the Wi-Fi link
Signaling IPsec SA is established using IKEv2 protocol
Control plane for Signaling IPsec SA for Trusted WLAN

## Slide 16: PDU Session Management
A PDU connectivity service is supported via PDU sessions to exchange PDUs between UE and data network
PDU session management over WLAN access is based on the procedure defined over the 3GPP access
Over WLAN access, one or more IPsec child SAs are created using IKEv2 protocol between N3IWF/TNGF and UE to transport 5G flows user data
N3IWF/TNGF determines the # of IPsec child SAs to establish and QoS flow(s) associated with each child SA
Multiple QoS flows can be mapped to the same IPsec child SA for a PDU session
N3IWF/TNGF can associate a DSCP value with an IPsec SA, UL and DL IPsec traffic gets marked with that DSCP
Control Plane for establishment of user plane IPsec child SA
For IPsec child SA, endpoints are 3GPP access on the UE and the N3IWF/TNGF
No impact on the WLAN AP or STA for session management
PDU: Protocol Data Unit, DSCP: Differentiated Services Codepoint

## Slide 17: UE Route Selection Policy (URSP)
URSP policy is used by the UE to determine how to route UL traffic for an application. Provided to the UE over 5G NAS messaging.
UL traffic can be routed to an established PDU session, offloaded to non-3GPP access outside a PDU session, or can trigger establishment of a new PDU session (single access or multi-access)
Each URSP rule has three main components:
  Rule Precedence – to determine the priority order of the rule
  Traffic Descriptor – to find the matching application for which rule applies
  List of Route Selection Descriptors – to determine how the matching flow should be routed. Contains one or more Route Selection Component plus validation criteria (time window, location).
    Access Type preference - 3GPP, non-3GPP or Multi-Access PDU session. For an MA PDU session, the ATSSS functionality is invoked.

## Slide 18: Access Traffic Steering, Switching and Splitting (1/2)
Support for Multi-Access PDU (MA PDU) session
  Enables PDU data delivery over 3GPP and WLAN access simultaneously
  MA PDU session establishment - when UE registered over single or both access
  When UE registered over both access, user plane resources established over both access
Support for two steering functionalities
  MPTCP functionality (at high layer), for TCP traffic, with MPTCP converter proxy in UPF
  ATSSS-LL functionality (at low layer) for all traffic types including TCP, UDP, Ethernet traffic
UE/UPF may support one or more steering functionality
  ATSSS-LL mandatory for Ethernet PDU session
Support of Performance Measurement Function (PMF) for ATSSS-LL
  Request access specific performance measurements from UE over user-plane of 3GPP and WLAN access

## Slide 19: Access Traffic Steering, Switching and Splitting (2/2)
UE provides its ATSSS Capability to the network for supported steering functionalities (MPTCP and/or ATSSS-LL)
SMF creates ATSSS rules and N4 rules based on the PCC policy
ATSSS rules sent to the UE for UL traffic distribution, and N4 rules sent to UPF for DL traffic distribution
If MPTCP functionality is selected, the MPTCP Proxy functionality is enabled in the UPF
MPTCP proxy uses converter protocol (RFC 8803)
An ATSSS container IE sent to UE:
  ATSSS Rules
  MPTCP proxy information
  Link specific IP addresses (IP@1, IP@2)
  Measurement Assistance Information for PMF reporting

## Slide 20: ATSSS Rules
An ATSSS rule includes following parts:
Rule Precedence – to determine the priority order of the rule
Traffic Descriptor – to identify matching user data traffic to determine when ATSSS rule applies
Steering Mode – to specify the traffic distribution policy over 3GPP and non-3GPP access.
  Active Standby: Steer traffic on the Active access, when the Active access becomes unavailable switch to Standby access
  Smallest Delay: Steer traffic to the access with smallest RTT delay
  Load Balancing: Split traffic across both access based on percentage specified
  Priority Based: Steer traffic to high-priority access, until that access gets congested. Then steer traffic also to the low-priority access
Steering Functionality – to specify whether the MPTCP or the ATSSS-LL functionality should be used to steer the matching traffic
Current ATSSS feature does not require any enhancements in WLAN STA or WLAN AP.

## Slide 21: 5G QoS Model (1/2)
The 5G QoS model, as used over the 3GPP access, is also followed when UE accesses the 5G core over WLAN access
The QoS Flow (identified by QFI) is the finest granularity of QoS differentiation within the PDU session, both for single access and multi-access (MA) PDU sessions
During PDU session establishment, one or more QoS Flows get associated with the PDU session based on the binding of PCC rule to a QoS Flow
User plane traffic with the same QFI for a PDU session receives same traffic forwarding treatment within the access network
A QoS Flow is not associated with specific access for MA PDU session - same QoS is supported when the flow traffic is distributed over 3GPP access and/or WLAN access
A QoS flow can be either guaranteed bit rate flow (GRB QoS Flow) or non-guaranteed bit rate flow (Non-GBR QoS Flow)

## Slide 22: 5G QoS Model (2/2)
5G QoS Flow – A QoS flow carried over WLAN access has following associated information:
  QoS Profile – specifies QoS parameters for the QoS flow. Provided to N3IWF/TNGF over N2 as part of PDU session management. Used by N3IWF/TNGF to map QoS flows to IPsec child SAs.
  QoS Rules – specifies Packet Filter set to map UL traffic to QoS flows within a PDU session. Either signaled to/derived by UE by applying Reflective QoS control on DL traffic.
  QoS Flow Description – specifies QoS parameters for the QoS flows to the UE. These can be used by the UE to provide QoS differentiation for the indicated QoS flow.
  5G_QOS_INFO Notify Payload – contains QoS specific parameters within the Create_Child_SA request sent to the UE to establish an IPsec child SA over WLAN access.
  Packet Detection Rules (PDR) – specifies Packet Filter set. Provided to the UPF and used to map DL user traffic to N3/N9 core network tunnel with 3GPP or WLAN access
5G QoS Characteristics – A 5QI (5G QoS Identifier) value identifies a set of QoS characteristic associated with a QoS flow. Used within the 5G Core, RAN and UE for QoS treatment.

## Slide 23: 5G QoS Characteristics
QoS Characteristic | Description
Resource Type | Indicates the GBR, Delay-critical GBR or Non-GBR resource type for a QoS Flow.
Priority Level | Indicates a priority in scheduling resources among QoS Flows. The lowest Priority Level value corresponds to the highest priority.
Packet Delay Budget (PDB) | Defines an upper bound for the time that a packet may be delayed between the UE and the UPF.
Packet Error Rate | Defines an upper bound for a rate of non-congestion related packet losses. Same in UL and DL. Used to determine appropriate link layer protocol configurations in 3GPP access network.
Averaging Window | Represents the duration over which the GFBR and MFBR shall be calculated.
Maximum Data Burst Volume (MDBV) | MDBV is applicable only for Delay-critical GBR resource type. It denotes the largest amount of data that the 5G-AN is required to serve within a period of 5G-AN PDB.
Standardized 5QI values and associated QoS characteristics are defined for frequently used services for GBR, Delay-critical GBR and Non-GRB resource types
Dynamically assigned 5QI values and associated characteristics can be defined for services which can not use standardized 5QI values

## Slide 24: 5G QoS Parameters
QoS Profile parameters
QoS Rule parameters
QoS Flow Identifier (QFI)
QoS Rule Identifier (QRI)
Default QoS rule indication
Packet Filter Set
Precedence Value
5G QoS Identifier (5QI) | 
5G QoS Characteristics (optional) | 
Allocation and Retention Priority (ARP) | 
For Non-GBR QoS Flow only | 
Reflective QoS Attribute (RQA) | 
For GBR QoS Flow only | 
Guaranteed Flow Bit Rate (GFBR) - UL and DL | 
Maximum Flow Bit Rate (MFBR) - UL and DL | 
Notification Control | 
QoS Flow Identifier (QFI) | 
5G QoS Identifier (5QI) | 
For GBR QoS Flow only | 
Guaranteed Flow Bit Rate (GFBR) - UL and DL | 
Maximum Flow Bit Rate (MFBR) - UL and DL | 
Averaging Window | 
QoS Flow Description parameters
PDU Session ID
QoS Flow Identifier(s)
DSCP value
Default Child SA indication
Additional QoS Information
5G_QOS_INFO Notify Payload parameters
N3IWF and TNGF map QoS flows to IPsec child SA in an implementation specific way
If multiple flows mapped to same IPsec SA, then TNGF determines QoS characteristics and/or parameters of the aggregated flow
QoS parameters sent to UE in 5G_QOS_INFO Notify payload as part of the Create_Child_SA request
TNGF may reserve WLAN access resources based on QoS profile
UE may reserve WLAN access resources based on QoS parameters

## Slide 25: User Data Transport
Uplink User Data Transport:
UL data is sent over an IPsec child SA associated with the matching QoS flow/PDU session per QoS Rules
UE encapsulates the UL data inside a GRE packet, with GRE header carrying the QFI
GRE packet gets encapsulated into an IP packet and sent to N3IWF/TNGF over selected IPsec child SA in tunnel mode
For UL data over MA PDU session, ATSSS rules are applied
Downlink User Data Transport:
UPF maps DL data to a QoS Flow per packet filters in PDRs
UPF includes QFI and RQI in the encapsulation header over N3
N3IWF/TNGF uses the QFI/PDU session to find the associated IPsec child SA for sending DL user data
N3IWF/TNGF encapsulates the DL packet into a GRE packet, with GRE header carrying the QFI and RQI
GRE packet is encapsulated into an IP packet and sent to UE over the selected IPsec child SA in tunnel mode
If a DSCP value is associated, then the IP packets for the IPsec child SA are marked with that DSCP value
User Plane protocol over WLAN Access
GRE: Generic Routing Encapsulation, QFI: QoS Flow Identifier, RQI: Reflective QoS Indicator

## Slide 26: Interworking Challenges and Gaps
Technical challenges and gaps related to enabling interworking between IEEE WLAN and 3GPP 5G system are identified in three main areas:
Trusted WLAN Integration
End-to-end QoS Support
Support for Wi-Fi Only Devices w/o USIM

## Slide 27: Trusted WLAN Integration
Involves tight coupling between WLAN AP & TNGF/TWIF gateway functions on the network side and between 3GPP Access and WLAN STA on the UE
WLAN Access Network
Standardize AAA based Ta and Yw interfaces. Considered outside of 3GPP scope.
Support TNGF and/or TWIF function
ANQP Server
Advertise list of PLMNs with which trusted 5G connectivity is supported via TNGF or TWIF in the ‘3GPP Cellular Network information’
WLAN Access Point
Support Ta and Yw interfaces
Support invoking Ta based on 3GPP specific NAI
Support filtering EAP-5G protocol messages
Support using TNAP key from TNGF as PMK for the 802.11 4-way handshake
WLAN STA
Discover PLMN lists over ANQP, send to 3GPP access
Provide 3GPP specific NAI for UE identity for access via TNGF
Provide unique UE NAI for access via TWIF
Support EAP-5G messages exchange with 3GPP access on the UE
Following capabilities needed within the WLAN domain

## Slide 28: End-to-End QoS Support - Background
WLAN QoS Management:
802.11 EDCA QoS scheme provides prioritized contention-based access and is the most widely adopted WLAN QoS scheme
  EDCA supports 8 User Priorities (UP) which get mapped to 4 QoS Access Categories (AC) for background, best effort, video and voice traffic (AC_BK, AC_BE, AC_VI, AC_VO)
  Differentiated QoS achieved with different AIFS (Arbitration Interframe Space) and CW (Contention Window) for each AC
  Admission control for QoS traffic streams per AC using ADDTS Request/Response with TSPEC (traffic specification) and TCLAS (traffic classification) elements
  No guarantees can be provided on throughput, latency etc. Only priority-based bandwidth allocation provided based on ACs
Support for mapping data packets to 802.11 UP based on DSCP marking in the IP header

## Slide 29: QoS Differentiation for 5G Flows
To satisfy end-to-end QoS requirements, it is important to provide QoS differentiation for 5G flows within WLAN access using EDCA QoS scheme
Three possible approaches for QoS differentiation over WLAN access:
DSCP Marking based QoS Mapping
QoS differentiation based on DiffServ DSCP marking in IP header for UL and DL user data
Applicable for both untrusted and trusted WLAN integration
Device centric QoS Management based on IPsec SA
QoS differentiation based on identifying and prioritizing IPsec child SAs carrying 5G flows
WLAN STA initiates QoS management using EDCA admission control procedure
Applicable for both untrusted and trusted WLAN integration
Network centric QoS Management based on IPsec SA
QoS differentiation based on identifying and prioritizing IPsec child SAs carrying 5G flows
WLAN AP initiates QoS management using AP-initiated procedure for EDCA admission control
Applicable for trusted WLAN integration only

## Slide 30: DSCP Marking Based QoS Mapping
DSCP marking gets mapped to 802.11 UP/AC on WLAN AP (for DL) and STA (for UL)
WLAN AP can provide 3GPP network specific DSCP to UP mapping to the STA
Requires 5QI to DSCP mapping to be done at the N3IWF/TNGF (for DL) and at the UE (for UL)
Gaps and enhancements needed:
Define standardized 5QI values to DSCP mapping
Support tagging 5G user data packets with appropriate DSCP value per defined mapping
Define 3GPP specific mapping between updated set of DSCP values to 802.11 User Priorities

## Slide 31: QoS Differentiation Based on IPsec SA (1/2)
Device centric approach:
The 5G QoS entity on STA receives 5G QoS information and triggers QoS negotiation through SME for IPsec child SAs using Non-AP-initiated TS Setup procedure
5G QoS information is sent to WLAN domain (STA or AP)
5G QoS Information: 5G QoS characteristics and parameters, IPsec SA info for child SAs (UL and DL), DSCP
IPsec SA: Uniquely identified by SPI (Security Parameter Index), destination IP address and security protocol
5G QoS entity maps 5G QoS characteristics/parameters to 802.11 TSPEC, creates TCLAS from the IPsec SA info
Network centric approach:
The 5G QoS entity on WLAN AP receives 5G QoS information and triggers QoS negotiation through SME for IPsec child SAs using AP-initiated TS setup procedure

## Slide 32: QoS Differentiation Based on IPsec SA (2/2)
N3IWF, 3GPP Access, TNGF
Provide 5G QoS information to UE for flows over untrusted WLAN access as well
Map each 5G QoS flow to separate IPsec child SA
WLAN STA
Support 5G QoS entity for device centric QoS mgmt.
WLAN AP (for Network Centric QoS Mgmt.)
Define TNGF-WLAN AP interface to send 5G QoS information
Integration with TNGF to receive 5G QoS info
Support a 5G QoS entity for network centric QoS
Support AP-Initiated TS setup for 5G flows
WLAN STA, WLAN AP:
Define 5G QoS parameters to TSPEC parameters mapping for QoS TS setup. Address handling for TSPEC parameters not specified (e.g. MSDU size)
Enhance TCLAS element to specify filtering for IPsec traffic based on IPsec SA identifiers (SPI, destination IP address and security protocol ID)
Enhancement to provide all 5G QoS parameters to WLAN AP for resource reservation
Evaluate how 802.11ax capabilities such as TWT scheduling, OFDMA and MU-MIMO can provide fine grain QoS granularity for 5G GBR flows
IEEE 802.11be QoS enhancements should consider how QoS for 5G GBR flows (guaranteed bit rate, latency, PER, Max data burst volume) can be satisfied
Following capabilities needed within WLAN domain
For further study:

## Slide 33: Support for Wi-Fi Only Devices w/o USIM
3GPP Gaps:
Define support for 5G-Capable and Non-5G-Capable Wi-Fi only devices w/o USIM to access 5G Private networks (SNPN) via N3IWF/TNGF and TWIF
Support non-IMSI based identity and EAP-TLS/ EAP-TTLS authentication for Wi-Fi only devices to access SNPN over WLAN access
Consider requiring support for EAP-TLS/EAP-TTLS for these devices in PLMN networks
5G-Capable Wi-Fi Only UE Gaps:
Support a 5G entity providing 5G NAS and user plane functions as defined in 3GPP
  EAP-5G, IKEv2, IPsec/ESP and 5G NAS protocols for 5G control plane functions
  GRE and IPsec/ESP protocols for 5G user plane transport

## Slide 34: Technical Recommendations
Address the gaps and enhancements identified in the three main areas to enable end-to-end system support for WLAN and 5G system interworking
These could lead to IEEE 802.11 standard changes, deployment changes and/or new interface definitions within WLAN domain
Some enhancements would need to be considered in 3GPP standard and could lead to Liaison sent to 3GPP
Trusted WLAN integration
Standardize Ta and Yw interfaces
Support TNGF, TWIF functions
Support EAP-5G messages filtering
Support TNAP key for WLAN 4-way authentication
Advertise PLMN lists via ANQP…
End-to-end QoS Support
Define 5QI to DSCP mapping
Define 3GPP specific DSCP to 802.11 UP mapping
Provide 5G QoS information for untrusted WLAN access
Support IPsec SA based QoS
Mapping of 5G QoS to TSPEC
Enhance TCLAS for IPsec SA
AP integration with TNGF for network centric QoS
Map each 5G QoS flow to separate IPsec child SA…
Support for Wi-Fi only devices w/o USIM
Support 5G-Capable and Non-5G-Capable Wi-Fi only devices over SNPN
Support non-IMSI based identity and EAP-TLS/EAP-TTLS authentication
For 5G-Capable Wi-Fi only UE, support 5G entity providing 5G NAS and user plane functions

## Slide 35: Future Work – TSN Support
5G TSN support
  3GPP has defined architecture to integrate 5G System as a logical TSN bridge
  TSN functions confined to TSN Translator (TT) at the ingress points (AF, UPF, UE)
  Supports 802.1AS based time synchronization – with GM clock on the network side
  Supports Time-aware scheduling (IEEE 802.1Qbv)
802.11 TSN support
  Many 802.1 TSN protocols can be natively supported over 802.11
  Supports 802.1AS time synchronization using Fine/Timing Measurements (F/TM) capabilities
  TSN traffic classification can be achieved using VLAN tagging (802.1Q), supported by TSPEC & TCLAS
  IEEE 802.11ax features like TWT scheduling, OFDMA and MU-MIMO can be used to serve TSN requirements
  IEEE 802.11be is addressing TSN support - priority access for TSN, Multi-link operation, Multi-AP capability
TSN Support for Integrated WLAN and 5G Network
  TSN architecture needs to be defined to integrate a WLAN and 5G integrated network with a TSN system
  Architecture needs to consider native support for many 802.1 TSN standards over IEEE 802.11
  3GPP 5G standard should consider defining a TSN architecture for WLAN and 5G integrated network
5GS integrated as TSN Bridge

## Slide 36: References
3GPP TS 23.501: “System architecture for the 5G System (5GS); Stage 2”
3GPP TS 23.502: "Procedures for the 5G System; Stage 2"
3GPP TS 23.503: "Policies and Charging control framework for the 5G System (5GS); Stage 2"
3GPP TS 24.501: “Non-Access-Stratum (NAS) protocol for 5G System (5GS); Stage 3”
3GPP TS 24.502: “Access to the 3GPP 5G Core Network (5GCN) via Non-3GPP Access Networks (N3AN); Stage 3”
3GPP TS 33.501: “Security architecture and procedures for 5G system”
3GPP TS 24.519: “Time-Sensitive Networking (TSN) Application Function (AF) to Device-Side TSN Translator (DS-TT) and Network-Side TSN Translator (NW-TT) protocol aspects; Stage 3”
IEEE P802.11-REVmd™/D5.0, September 2020, Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications
IEEE Std 802.11™-2016, Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications
RFC 7296, Internet Key Exchange Protocol Version 2 (IKEv2)
RFC 2474, Definition of the Differentiated Services Field (DS Field) in the IPv4 and IPv6 Headers
RFC 2401, Security Architecture for the Internet Protocol
RFC 8803, 0-RTT TCP Convert Protocol
Avnu Alliance® White Paper, Wireless TSN – Definitions, Use Cases & Standards Roadmap, Version #1.0 – Mar 4, 2020

## Slide 37: Backup

## Slide 38: Standardized 5QI to QoS Characteristics Mapping (1/3)
5QI Value | Resource Type | Default Priority Level | Packet Delay Budget | Packet Error Rate | Default Maximum Data Burst Volume | Default Averaging Window | Example Services
1 | GBR | 20 | 100 ms | 10-2 | N/A | 2000 ms | Conversational Voice
2 |  | 40 | 150 ms | 10-3 | N/A | 2000 ms | Conversational Video (Live Streaming)
3 |  | 30 | 50 ms | 10-3 | N/A | 2000 ms | Real Time Gaming, V2X messages. Electricity distribution – medium voltage, Process automation monitoring
4 |  | 50 | 300 ms | 10-6 | N/A | 2000 ms | Non-Conversational Video (Buffered Streaming)
65 |  | 7 | 75 ms | 10-2 | N/A | 2000 ms | Mission Critical user plane Push To Talk voice (e.g., MCPTT)
66 |  | 20 | 100 ms | 10-2 | N/A | 2000 ms | Non-Mission-Critical user plane Push To Talk voice
67 |  | 15 | 100 ms | 10-3 | N/A | 2000 ms | Mission Critical Video user plane
71 |  | 56 | 150 ms | 10-6 | N/A | 2000 ms | "Live" Uplink Streaming
72 |  | 56 | 300 ms | 10-4 | N/A | 2000 ms | "Live" Uplink Streaming
73 |  | 56 | 300 ms | 10-8 | N/A | 2000 ms | "Live" Uplink Streaming
74 |  | 56 | 500 ms | 10-8 | N/A | 2000 ms | "Live" Uplink Streaming
76 |  | 56 | 500 ms | 10-4 | N/A | 2000 ms | "Live" Uplink Streaming
For GBR resource type (TS 23.501):

## Slide 39: Standardized 5QI to QoS Characteristics Mapping (2/3)
5QI Value | Resource Type | Default Priority Level | Packet Delay Budget | Packet Error Rate | Default Maximum Data Burst Volume | Default Averaging Window | Example Services
5 | Non-GBR | 10 | 100 ms | 10-6 | N/A | N/A | IMS Signalling
6 |  | 60 | 300 ms | 10-6 | N/A | N/A | Video (Buffered Streaming) TCP-based (e.g., www, e-mail, chat, ftp, p2p file sharing, progressive video, etc.)
7 |  | 70 | 100 ms | 10-3 | N/A | N/A | Voice, Video (Live Streaming) Interactive Gaming
8 |  | 80 | 300 ms | 10-6 | N/A | N/A | Video (Buffered Streaming) TCP-based (e.g., www, e-mail, chat, ftp, p2p file sharing, progressive video, etc.)
9 |  | 90 |  |  |  |  | 
69 |  | 5 | 60 ms | 10-6 | N/A | N/A | Mission Critical delay sensitive signalling (e.g., MC-PTT signalling)
70 |  | 55 | 200 ms | 10-6 | N/A | N/A | Mission Critical Data (e.g. example services are the same as 5QI 6/8/9)
79 |  | 65 | 50 ms | 10-2 | N/A | N/A | V2X messages
80 |  | 68 | 10 ms | 10-6 | N/A | N/A | Low Latency eMBB applications Augmented Reality
For Non-GBR resource type (TS 23.501):

## Slide 40: Standardized 5QI to QoS Characteristics Mapping (3/3)
5QI Value | Resource Type | Default Priority Level | Packet Delay Budget | Packet Error Rate | Default Maximum Data Burst Volume | Default Averaging Window | Example Services
82 | Delay Critical GBR | 19 | 10 ms | 10-4 | 255 bytes | 2000 ms | Discrete Automation
83 |  | 22 | 10 ms | 10-4 | 1354 bytes | 2000 ms | Discrete Automation V2X messages (UE - RSU Platooning, Advanced Driving: Cooperative Lane Change with low LoA.
84 |  | 24 | 30 ms | 10-5 | 1354 bytes | 2000 ms | Intelligent transport systems
85 |  | 21 | 5 ms | 10-5 | 255 bytes | 2000 ms | Electricity Distribution- high voltage V2X messages (Remote Driving.
86 |  | 18 | 5 ms | 10-4 | 1354 bytes | 2000 ms | V2X messages (Advanced Driving: Collision Avoidance, Platooning with high LoA.
For Delay-Critical GBR resource type (TS 23.501):