## Slide 1: 802.11be AP MLD Architecture Discussion
Date: 2020-11-04
Authors:

## Slide 2: Abstract
This presentation considers architecture concepts for TGbe AP MLDs. This follows ideas in some first presentations in the ARC SC sessions on Aug 6, Aug 24, and Sep 16.

## Slide 3: Need to sort out the functions within an AP MLD – which are “MLD” and which are “AP(s)”
Consider the MAC stack, as shown in 802.11 Figure 5-1:
Might be useful to ask, “Does this function have to be link-specific?” and/or “Is this function explicitly shared across the links?”
For now, ignore “legacy” AP, only affiliated AP(s) are considered

## Slide 4: “MLD-level”, or “per-AP/link-level” - 1
All the figures/discussion presented in discussion so far have had some concept of some MAC functions that are per-link and “lower” in the stack, and some MAC functions that are shared across the links “at MLD level” and shown “higher” in the stack.
A proposed split/allocation of some MAC functions (on this and following slides):
MLD (shared state across all links/can use any available link):
  Security Association/state; PN space [Motion 111 #SP0611-29]
    “802.11be supports that after multi-link setup between two MLDs, the same PMK and the same PTK across links are used with the same PN space for a PTKSA.”
     Therefore, MPDU Encryption/Decryption, is a shared MLD function. (Note: see 11-20/1240, this does NOT mean an implementation is prevented from having parallel blocks.)
  Sequence Number assignment; Receive reordering buffer [Motion 62]
    “For each block ack agreement, there exists one receive reordering buffer based on MPDUs in the MLD which is the recipient of the QoS Data frames for that block ack agreement. The receive reordering buffer operation is based on the Sequence Number space that is shared between the two MLDs.”
     Note that this implies PS buffering (of individually addressed frames, at least) is a shared MLD function, in order to maintain SN ordering.

## Slide 5: “MLD-level”, or “per-AP/link-level” - 2
Retransmission discussion:
Motion 61:
  “The established block ack agreement allows the QoS Data frames of the TID, aggregated within the A-MPDUs, to be exchanged between the two MLDs on any available link.
  NOTE – QoS Data frames that are not fragments might be retransmitted on any available link.”
Motion 61 is from 11-20/0434r3
11-20/0434r3 goes on, with a second Straw Poll, which was never run:
  The MLD MAC address of the recipient MLD is used as the A1 field for the AAD construction.
  The MLD MAC address of the transmitting MLD is used as the A2 field for the AAD and Nonce construction.
  If the Address 3 field of the protected frame carries the BSSID, the MLD MAC Address of the AP MLD is used as the A3 field for the AAD construction. Otherwise, the Address 3 field of the protected frame is used.
If the above (second Straw Poll) is accepted, Retransmission on any link “just works”, without any discussion of “MLD level” or “per-link level” retransmission.
If the above is not accepted, retransmission behavior “on any available link” needs to be defined. There is nothing in the SFD or D0.1 describing this, so far.
Is this all “TBD” in TGbe, still?

## Slide 6: “MLD-level”, or “per-AP/link-level” - 3
Implementation choice (explicitly), of MLD shared or per-link:
  Block-Ack scoreboarding [Motion 63. Motion 114. (Motion 112.) ]
    “The receive status of QoS Data frames of a TID received on a link shall be signaled on the same link and may be signaled on other available link(s).”
    “802.11be shall define mechanism for multi-link operation that enables the following: A STA of a recipient MLD shall provide receive status for MPDUs received on the link that it is operating on and may provide (if available) information on successful reception of MPDUs received by another STA of that MLD.”
    (“An originator MLD of a BA agreement: 1) shall update the receive status for an MPDU corresponding to the BA agreement if the received status indicates successful reception. 2) shall not update the receive status for an MPDU corresponding to the BA agreement that has been already positively acknowledged.”)

## Slide 7: “MLD-level”, or “per-AP/link-level” - 4
Per-link functions:
  CCA, backoff, NAV, etc. (although there may be timing alignment done across the links, which puts restrictions on the EDCA access) [Motion 20]
    “Each of STAs belonging to a MLD performs a channel access over their links independently in order to transmit frames.”
  A-MPDU aggregation/de-aggregation [I’m just assuming, since this is such a low-level function]
  Address 1 matching [Allows per-link MAC address; allows per-link scoreboarding. Although, maybe this should be in the “Implementation choice” category?]
  Group addressed frame transmission
    After multi-link setup between two MLDs, different GTK/IGTK/BIGTK in different links with different PN spaces are used. GTK/IGTK/BIGTK in different links can be delivered in one 4-way handshake. [Motion 71]
    802.11be agrees that each AP in an AP MLD shall independently transmit all bufferable group addressed Management frames after every DTIM beacon in R1. [Motion 131 #SP206]
    No agreement on group addressed data frames (but see 11-20/0661 for discussion of options)

## Slide 8: Implications
Implications:
MLD:
  802.1X controlled/uncontrolled filtering [Done at the MAC SAP]
  RX/TX MSDU rate limiting [Done at the MAC SAP]
  A-MSDU aggregation/deaggregation [Must be done “above” encryption and reordering buffer]
  (  bufferable unicast MMPDUs need to inject into the stack here, so Action frames??)
  PS Defer Queuing (of unicast frames – as discussed on slide 4)
    what about different PS state on different links?? (_all_ doze => buffer; _any_ active => don’t buffer)
   Management frames like Authentication/Association/Reassociation Request/Response [Must be above SN assignment]
  Sequence Number assignment (per slide 4)
  Replay detection on RX [Matches PN assignment on TX]
  MPDU Encryption/Decryption (as discussed on slide 4)
  Duplicate Detection [Goes with receive reordering buffer]
Per-link:
  Control frames (RTS/CTS, Acks, NDP, etc.)
  Management frames: Beacon generation, Probe Request/Response
  MPDU header creation/validation – “actual header”, not “masked header”/AAD for integrity?

## Slide 9
So, something like:

## Slide 10: Data plane/management plane
Note that Figure 5-1 is really just a data plane view. But, we are considering some management plane traffic/functions. It would be helpful to clarify with a diagram that shows management functions.
Many years ago (2008), the ARC SC started work on an overall architecture picture that combines data and management (and some control) functions. See 11-08/949 and 11-08/1298.
That ARC work was intended to be relatively comprehensive, and therefore got complicated (and never finished). We can try something simpler for 11be purposes (next slide).

## Slide 12
Let’s simplify a bit:

## Slide 13
Note that, within any AP (legacy or AP MLD), there is a conceptual table, of peer non-AP STAs:
 | State | Other info
STA1 | State 1 (unauth) | Data rates, HT capabilities, VHT capabilities
STA2 (VHT) | State 4 (RSNA) | Data rates, PS state, RSNA info, HT capabilities, VHT capabilities, FILS info, SN, PN, Block Ack agreements, MSCS agreement, TFS agreement, etc., etc.
STA3 (HT) | State 4 (RSNA) | Data rates, PS state, RSNA info, HT capabilities, VHT capabilities, FILS info, SN, PN, Block Ack agreements, MSCS agreement, TFS agreement, etc., etc.
STA4 (VHT) | State 3 (Assoc, not RSNA) | Data rates, PS state, RSNA info, HT capabilities, VHT capabilities, FILS info, SN, PN, Block Ack agreements, MSCS agreement, TFS agreement, etc., etc.
STA5 (VHT) | State 4 (RSNA) | Data rates, PS state, RSNA info, HT capabilities, VHT capabilities, FILS info, SN, PN, Block Ack agreements, MSCS agreement, TFS agreement, etc., etc.
… | … | …
STA n (VHT) | State 2 (auth, not assoc) | Data rates, PS state, RSNA info, HT capabilities, VHT capabilities, FILS info, SN, PN, Block Ack agreements, MSCS agreement, TFS agreement, etc., etc.

## Slide 14
Consider adding a little info to the table:
Is the peer MLD/MLO?
If yes, which links are connected; which links are enabled; NSTR/STR/Single Radio, etc.
If no, what is the legacy state for each link (since they can be different)
 | State | Other info
STA1 | State 1 (unauth) | Data rates, HT capabilities, VHT capabilities
STA2 (EHT) | State 4 (RSNA) | Data rates, PS state(per link?), RSNA info, HT capabilities, VHT capabilities, FILS info, SN, PN, Block Ack agreements, MSCS agreement, TFS agreement, MLO(STR, link1(E), link2(D), etc.), etc., etc.
STA3 (HT) | State 4 (RSNA) | Data rates, PS state, RSNA info, HT capabilities, VHT capabilities, FILS info, SN, PN, Block Ack agreements, MSCS agreement, TFS agreement, etc., etc.
STA4 (EHT) | State 3 (Assoc, not RSNA) | Data rates, PS state, RSNA info, HT capabilities, VHT capabilities, FILS info, SN, PN, Block Ack agreements, MSCS agreement, TFS agreement, MLO(Single radio, link1(E), link2(D), etc.), etc., etc.
STA5 (VHT) | State 4 (RSNA) | Data rates, PS state, RSNA info, HT capabilities, VHT capabilities, FILS info, SN, PN, Block Ack agreements, MSCS agreement, TFS agreement, not MLO(link1), etc., etc.
STA6 (VHT) | State 4 (RSNA), doing re-association (w/FT) | Data rates, PS state, RSNA info, HT capabilities, VHT capabilities, FILS info, SN, PN, Block Ack agreements, MSCS agreement, TFS agreement, not MLO(link1 associated, link2 authenticated(FT state1)), etc., etc.
STA n (EHT) | State 2 (auth, not assoc) | Data rates, PS state, RSNA info, HT capabilities, VHT capabilities, FILS info, SN, PN, Block Ack agreements, MSCS agreement, TFS agreement, MLO(NSTR, link1(E), link2(D), link3(D), etc.), etc., etc.

## Slide 15
So, we have a small database, shared and accessible by the MAC components:

## Slide 16: “Legacy” AP behaviors
First, note that the AP MLD is handling associations from multiple non-AP STAs/MLDs.
  This implies, for example, multiple PTKSAs, PS buffers/queues, etc.
  Thus, we can think of the MLD AP as being “multi-theaded” in the sense that it is capable of managing an array of state information, one entry per peer non-AP STA/MLD
What does adding “legacy” AP behavior change in this picture?
  Add 1 bit of state, for each non-AP STA/MLD: Is it a “legacy” STA or an MLD?
  Stack layers treat the (small) differences between the two, on a case-by-case basis as the functions are accomplished.
  Thus, there is no need for a separate stack/architectural concept to support the “legacy” interop behaviors.

## Slide 17
Then, consider non-AP peers (MLD or legacy):
When interacting with “STA a”, the peer database tells the AP MLD to enable all the components (blue), and use “MLD signaling enhancements”

## Slide 18
Then, consider non-AP peers (MLD or legacy):
When interacting with “STA b”, the peer database tells the AP MLD to enable only the one link (red), and not use “MLD signaling enhancements”
This can include using legacy behavior for re-association within the link information in the database