## Slide 1: 802.11be AP MLD Architecture Discussion
Date: 2021-01-13
Authors:

## Slide 2: Abstract
This presentation considers architecture concepts for TGbe AP MLDs. This follows ideas in presentations in the ARC SC sessions leading up to and during the Nov plenary session, Jan plenary session, and teleconferences.

## Slide 3: Need to sort out the functions within an AP MLD – which are “MLD” and which are “AP(s)”
Consider the MAC stack, as shown in 802.11 Figure 5-1:
Might be useful to ask, “Does this function have to be link-specific?” and/or “Is this function explicitly shared across the links?”
Initially (in this discussion), ignore “legacy” AP, only affiliated AP(s) are considered, then add legacy (slide 18)

## Slide 4: “MLD-level”, or “per-AP/link-level” - 1
All the figures/discussion presented in discussion so far have had some concept of some MAC functions that are per-link and “lower” in the stack, and some MAC functions that are shared across the links “at MLD level” and shown “higher” in the stack.
A proposed split/allocation of some MAC functions (on this and following slides):
MLD (shared state across all links/can use any available link):
  Security Association/state; PN space [Motion 111 #SP0611-29]
    “802.11be supports that after multi-link setup between two MLDs, the same PMK and the same PTK across links are used with the same PN space for a PTKSA.”
     Therefore, MPDU Encryption/Decryption, is a shared MLD function. (Note: see 11-20/1240, this does NOT mean an implementation is prevented from having parallel blocks.)
  Sequence Number assignment; Receive reordering buffer [Motion 62]
    “For each block ack agreement, there exists one receive reordering buffer based on MPDUs in the MLD which is the recipient of the QoS Data frames for that block ack agreement. The receive reordering buffer operation is based on the Sequence Number space that is shared between the two MLDs.”
     Note that this implies PS buffering (of individually addressed frames, at least) is a shared MLD function, in order to maintain SN ordering.

## Slide 5: “MLD-level”, or “per-AP/link-level” - 2
Retransmission discussion:
Motion 61:
  “The established block ack agreement allows the QoS Data frames of the TID, aggregated within the A-MPDUs, to be exchanged between the two MLDs on any available link.
  NOTE – QoS Data frames that are not fragments might be retransmitted on any available link.”
Motion 61 is from 11-20/0434r3
11-20/0434r3 goes on, with a second Straw Poll, which was never run:
  The MLD MAC address of the recipient MLD is used as the A1 field for the AAD construction.
  The MLD MAC address of the transmitting MLD is used as the A2 field for the AAD and Nonce construction.
  If the Address 3 field of the protected frame carries the BSSID, the MLD MAC Address of the AP MLD is used as the A3 field for the AAD construction. Otherwise, the Address 3 field of the protected frame is used.
If the above (second Straw Poll) is accepted, Retransmission on any link “just works”, without any discussion of “MLD level” or “per-link level” retransmission.
If the above is not accepted, retransmission behavior “on any available link” needs to be defined. There is nothing in the SFD or D0.1 describing this, so far.
Is this all “TBD” in TGbe, still?

## Slide 6: “MLD-level”, or “per-AP/link-level” - 3
Implementation choice (explicitly), of MLD shared or per-link:
  Block-Ack scoreboarding [Motion 63. Motion 114. (Motion 112.) ]
    “The receive status of QoS Data frames of a TID received on a link shall be signaled on the same link and may be signaled on other available link(s).”
    “802.11be shall define mechanism for multi-link operation that enables the following: A STA of a recipient MLD shall provide receive status for MPDUs received on the link that it is operating on and may provide (if available) information on successful reception of MPDUs received by another STA of that MLD.”
    (“An originator MLD of a BA agreement: 1) shall update the receive status for an MPDU corresponding to the BA agreement if the received status indicates successful reception. 2) shall not update the receive status for an MPDU corresponding to the BA agreement that has been already positively acknowledged.”)

## Slide 7: “MLD-level”, or “per-AP/link-level” - 4
Per-link functions:
  CCA, backoff, NAV, etc. (although there may be timing alignment done across the links, which puts restrictions on the EDCA access) [Motion 20]
    “Each of STAs belonging to a MLD performs a channel access over their links independently in order to transmit frames.”
  A-MPDU aggregation/de-aggregation [I’m just assuming, since this is such a low-level function]
  Address 1 matching [Allows per-link MAC address; allows per-link scoreboarding. Although, maybe this should be in the “Implementation choice” category?]
  Group addressed frame transmission
    After multi-link setup between two MLDs, different GTK/IGTK/BIGTK in different links with different PN spaces are used. GTK/IGTK/BIGTK in different links can be delivered in one 4-way handshake. [Motion 71]
    802.11be agrees that each AP in an AP MLD shall independently transmit all bufferable group addressed Management frames after every DTIM beacon in R1. [Motion 131 #SP206]
    No agreement on group addressed data frames (but see 11-20/0661 for discussion of options)

## Slide 8: Implications
Implications:
MLD:
  802.1X controlled/uncontrolled filtering [Done at the MAC SAP]
  RX/TX MSDU rate limiting [Done at the MAC SAP]
  A-MSDU aggregation/deaggregation [Must be done “above” encryption and reordering buffer]
  (  bufferable unicast MMPDUs need to inject into the stack here, so Action frames??)
  PS Defer Queuing (of unicast frames – as discussed on slide 4)
    what about different PS state on different links?? (_all_ doze => buffer; _any_ active => don’t buffer)
   Management frames like Authentication/Association/Reassociation Request/Response [Must be above SN assignment]
  Sequence Number assignment (per slide 4)
  Replay detection on RX [Matches PN assignment on TX]
  MPDU Encryption/Decryption (as discussed on slide 4)
  Duplicate Detection [Goes with receive reordering buffer]
Per-link:
  Control frames (RTS/CTS, Acks, NDP, etc.)
  Management frames: Beacon generation, Probe Request/Response
  MPDU header creation/validation – “actual header”, not “masked header”/AAD for integrity?

## Slide 9
So, something like:

## Slide 10: Data plane/management plane
Note that Figure 5-1 is really just a data plane view. But, we are considering some management plane traffic/functions. It would be helpful to clarify with a diagram that shows management functions.
Many years ago (2008), the ARC SC started work on an overall architecture picture that combines data and management (and some control) functions. See 11-08/949 and 11-08/1298.
That ARC work was intended to be relatively comprehensive, and therefore got complicated (and never finished). We can try something simpler for 11be purposes (next slide).

## Slide 12
Let’s simplify a bit:

## Slide 13
Note that, within any AP (legacy or AP MLD), there is a conceptual table, of peer non-AP STAs:
 | State | Other info
STA1 | State 1 (unauth) | Data rates, HT capabilities, VHT capabilities
STA2 (VHT) | State 4 (RSNA) | Data rates, PS state, RSNA info, HT capabilities, VHT capabilities, FILS info, SN, PN, Block Ack agreements, MSCS agreement, TFS agreement, etc., etc.
STA3 (HT) | State 4 (RSNA) | Data rates, PS state, RSNA info, HT capabilities, VHT capabilities, FILS info, SN, PN, Block Ack agreements, MSCS agreement, TFS agreement, etc., etc.
STA4 (VHT) | State 3 (Assoc, not RSNA) | Data rates, PS state, RSNA info, HT capabilities, VHT capabilities, FILS info, SN, PN, Block Ack agreements, MSCS agreement, TFS agreement, etc., etc.
STA5 (VHT) | State 4 (RSNA) | Data rates, PS state, RSNA info, HT capabilities, VHT capabilities, FILS info, SN, PN, Block Ack agreements, MSCS agreement, TFS agreement, etc., etc.
… | … | …
STA n (VHT) | State 2 (auth, not assoc) | Data rates, PS state, RSNA info, HT capabilities, VHT capabilities, FILS info, SN, PN, Block Ack agreements, MSCS agreement, TFS agreement, etc., etc.

## Slide 14
Consider adding a little info to the table:
Is the peer MLD/MLO?
If yes, which links are connected; which links are enabled; NSTR/STR/Single Radio, etc.
If no, what is the legacy state for each link (since they can be different)
 | State | Other info
STA1 | State 1 (unauth) | Data rates, HT capabilities, VHT capabilities
STA2 (EHT) | State 4 (RSNA) | Data rates, PS state(per link?), RSNA info, HT capabilities, VHT capabilities, FILS info, SN, PN, Block Ack agreements, MSCS agreement, TFS agreement, MLO(STR, link1(E), link2(D), etc.), etc., etc.
STA3 (HT) | State 4 (RSNA) | Data rates, PS state, RSNA info, HT capabilities, VHT capabilities, FILS info, SN, PN, Block Ack agreements, MSCS agreement, TFS agreement, etc., etc.
STA4 (EHT) | State 3 (Assoc, not RSNA) | Data rates, PS state, RSNA info, HT capabilities, VHT capabilities, FILS info, SN, PN, Block Ack agreements, MSCS agreement, TFS agreement, MLO(Single radio, link1(E), link2(D), etc.), etc., etc.
STA5 (VHT) | State 4 (RSNA) | Data rates, PS state, RSNA info, HT capabilities, VHT capabilities, FILS info, SN, PN, Block Ack agreements, MSCS agreement, TFS agreement, not MLO(link1), etc., etc.
STA6 (VHT) | State 4 (RSNA), doing re-association (w/FT) | Data rates, PS state, RSNA info, HT capabilities, VHT capabilities, FILS info, SN, PN, Block Ack agreements, MSCS agreement, TFS agreement, not MLO(link1 associated, link2 authenticated(FT state1)), etc., etc.
STA n (EHT) | State 2 (auth, not assoc) | Data rates, PS state, RSNA info, HT capabilities, VHT capabilities, FILS info, SN, PN, Block Ack agreements, MSCS agreement, TFS agreement, MLO(NSTR, link1(E), link2(D), link3(D), etc.), etc., etc.

## Slide 15
So, we have a small database, shared and accessible by the MAC components:

## Slide 16
Now consider the BSS(s). Each Beaconing component (“AP”?), on each link, would traditionally be considered to create its own BSS:

## Slide 17
But, a non-AP MLD “associates” (we’ll call it for now) to the AP MLD as a whole, establishing multiple links. And, both devices use any of the links equivalently – single security, PN/SN, etc. (per earlier slides). So, the multiple links act like a single logical “multi-link”? BSS, for MLO non-AP MLDs that are associated.
Note that some non-AP MLDs may have different (subsets) of the links. But, all non-AP MLDs share a PN/SN, etc., context.

## Slide 18: “Legacy” AP behaviors – alternative 1
Keep legacy behavior separate, within a physical device:

## Slide 19: “Legacy” AP behaviors – alternative 1
Could share the PHY, like baseline MM-SME – see Figure 4-27:
But, need to sort out the data plane at the top of stack. Similar to current multiple (logical) AP device – separate ESS and DS?
Multiple Beacons, etc., for each BSS, on each medium

## Slide 20: “Legacy” AP behaviors – alternative 2
First, note that the AP MLD is handling associations from multiple non-AP STAs/MLDs.
  This implies, for example, multiple PTKSAs, PS buffers/queues, etc.
  Thus, we can think of the MLD AP as being “multi-theaded” in the sense that it is capable of managing an array of state information, one entry per peer non-AP STA/MLD
What does adding “legacy” AP behavior change in this picture?
  Add 1 bit of state, for each non-AP STA/MLD: Is it a “legacy” STA or an MLD?
  Stack layers treat the (small) differences between the two, on a case-by-case basis as the functions are accomplished.
  Thus, there is no need for a separate stack/architectural concept to support the “legacy” interop behaviors.

## Slide 21: “Legacy” AP behaviors – evolution and status
From the discussion on November 16 telecon, started with the figure on slide 18, then:
  Realized that a goal of 11be (and current direction in SFD/motions) is to have a single PHY for both legacy and the component of the MLD that is on the same band/channel. So, modified the figure to share the PHY (similar to slide 19).
  Next step was to realize/agree that there is only one Beacon, shared between legacy and the MLD component. And, other “low-level” MAC functions that are link-specific are also shared. Modified the figure to show this sharing – shared the “Lower MAC and PHY” function.
See next slide for current figure/status

## Slide 22: With legacy added, WIP figure:

## Slide 23: “Legacy” AP behaviors – discussion
What is left in the “Upper legacy MAC” component?
  Note that for the MLD components, the Management, etc., functions that are unique per-link are already “pulled out, to the side” per the prior discussions on the “W” shaped MLD figure.
  It seems that all the matching legacy functions are also handled in this component.
  So, the remainder of the “Upper legacy MAC” component are data plane, and higher-level management (Auth/Assoc, Action frames, etc.).
  This is very similar to the “Upper MLD MAC” functions
  The Upper MLD MAC component already has many behaviors that are per-peer, based on the peer’s capabilities and state.
  So, are the legacy behaviors anything more than an extension of the per-peer state and behavior already built-in to the Upper MLD MAC? If not, consider combining the legacy support into the Upper MLD MAC.

## Slide 24: With legacy added, first alternative (Alternative1):

## Slide 25: With legacy added, alternative from Dec 7 (Alt2):

## Slide 26
Alternative 2: Revisit stack operations and how they are split:

## Slide 27: Analysis of alternatives – what is where; what is different?
 | Alternative 1 | Alternative 2
Security SAs/Keys (In MLO, agreement, there is 1 PTK/PMK per “MLD-MLD (P2P) association”, managed by MLD stack) (GTKs are distributed via MLD-MLD association) | PTK/PMK: Per peer, all in MLD GTK, IGTK, BIGTK: in each legacy stack | PTK/PMK: MLO: PTK/PMK in MLD stack; Legacy: legacy stack’s PTK/PMK; GTK, IGTK, BIGTK: in each legacy stack
(Re)(Dis)Association, (De)Authentication | All go to MLD stack | Split based on Address1 (or MLO indication?)
Authenticator(s) | 1 | 1 per legacy + 1 for MLD * Needs discussion about implications on counts

## Slide 28: Analysis of alternatives – what is where; what is different?
 | Alternative 1 | Alternative 2
Address1 filter/RX frame routing The value of the RA/TA fields sent over-the-air in the MAC header of a frame is the MAC address of the STA affiliated with the MLD corresponding to that link. [Motion 108, [30] and [186]] | All data frames -> MLD; All Auth/Assoc based -> MLD; Most Mgmt -> MLD (?) … Any Mgmt -> legacy?? (maybe only Control frames?) | Can we arrange a clean Address1 split? (Only MLO peers will know the MLD address?)
SAP(s) | 1 * MLD is responsible for “routing” | 1 MLO, 1 per legacy * DS is responsible for “routing” * Need to work through MSDU flow(s) through APs/DS/Portal

## Slide 29: AP Data plane (Alt 2, simplified)
But, how can the Lower MACs know how to route incoming frames?

## Slide 30: AP Data plane discussion
Consider an alternate view, for MLO:
Frames are received at the Lower MAC, relatively arbitrarily (based on the link the TXer chose)
For MLD/MLO peers, the two stacks “share state” (with implementation ‘magic’) for all the per-peer attributes that are needed, but either one can process an incoming frame, using that shared state
So, the Lower MAC doesn’t need to “route” incoming frames, they just always go to the “matching” Upper MAC
Upper MACs can direct transmitted frames into either Lower MAC
(Power save and EDCA queuing FFS, on TX)

## Slide 31: AP Data plane – no MLD stack
The legacy MAC SAP is pretty clear, and (I think) agreed
But where is the MAC SAP for MLO peers?

## Slide 32: Reminder of (legacy) DS structure
Maybe it doesn’t matter where the MLO MAC SAP is?
Each stack has a MAC SAP, which (on an AP) supports a DSAF
The DS doesn’t care (or can be designed/fixed to not care) where uplink frames enter
The DS will route all downlink frames to one of the MAC SAPs (the one that has “registered” this client (really associated, but that’s confusing right now)

## Slide 33: Analysis of alternatives – what is where; what is different?
 | Alternative 1 | Alternative 2
Beacons; Probes | All go to legacy stack | All go to legacy stack
Robust management frames |  | 
GAS/ANQP (Pre-Assoc or post-Assoc) | ?? | ??
QoS queues/retry buffers (includes how to “merge” TX traffic at the lower MAC boundary) | One set, in MLD (but need to merge in mgmt. traffic) | Two sets? (With normal co-located BSS contention between them?)
Block Ack | ?? | ??
MLO channel configuration/modification of operation |  | 

## Slide 34: Analysis of alternatives – what is where; what is different?
 | Alternative 1 | Alternative 2
SN and PN (including QMF) | Single stack, single spaces as per legacy behavior – including across BSSs | Number spaces per stack – need MLO RXr to keep separate
DMS | Messy | Legacy peer: as today; MLO peer: messy
Multiple BSSID sets | ?? (Being discussed) | Are legacy and MLD stacks separate “multiple BSSs”?
Any impacts on DS interface? | Single SAP | Separate SAPs – so what (??)
What is an ESS/BSS? (In MLO, transitions to/from MLO) |  | 
Access Controls? |  | 
Multi-AP coordination? |  | 
(Mixed-mode) Mesh? Relays? OCB? TDLS? |  | 

## Slide 35
Then, consider non-AP peers (MLD or legacy):
When interacting with “STA a”, the peer database tells the AP MLD to enable all the components (blue), and use “MLD signaling enhancements”

## Slide 36
Then, consider non-AP peers (MLD or legacy):
When interacting with “STA b”, the peer database tells the AP MLD to enable only the one link (red), and not use “MLD signaling enhancements”
This can include using legacy behavior for re-association within the link information in the database