## Slide 1: WLAN sensing link level simulation
Date: 2020-10-13
Authors:
Name | Affiliation | Address | Phone | Email
Rui Du | Huawei Technologies Co. Ltd | F3, Huawei Base, Shenzhen, China |  | Ray.du@Huawei.com
Meihong Zhang |  |  |  | 
Chenchen Liu |  |  |  | 
Yingxiang Sun |  |  |  | 
Danny Tan Kai Pin |  |  |  | 
Edward Au |  |  |  | 
Notes: Link level simulation

## Slide 2: Outline
Abstract
WLAN sensing link level simulation
Key modules may need to be calibrated
Common environment model/channel model
Common basic algorithms
Summary
Rui Du, et al. (Huawei)

## Slide 3: Abstract
TG bf has been established recently, and simulation is potentially needed to compare the performance from different contributions.
In this presentation:
WLAN sensing link level simulation is presented and discussed.
two key modules may need calibration are further discussed.
Rui Du, et al. (Huawei)

## Slide 4
1 link level simulation
Rui Du, et al. (Huawei)
 Waveform generation
 Type (new sequence, new waveform, WLAN PPDU,…)
 Parameters (PRI, BW, fs, duration…)
 Transmitter
 Array geometry
 Element radiation pattern (gain)
 ERIP
Location
…
 Receiver
 Array geometry
Element radiation pattern (gain)
 Array and element errors
 Location
Sampling parameters (fs, duration…)
…
 Environment/channel model
Channel
Indoor
Outdoor
Target, interference and noise
 Number of targets
 Parameters (RCS, delay, velocity,…)
 Number of clutter
 Parameters (reflectivity, delay, AoD, AoA,…)
 Noise
 Signal processing and performance evaluation
 Range estimation
 Velocity estimation
 Angle estimation
 …
 Range accuracy
 Velocity accuracy
 Angle accuracy
 …
Performance evaluation
Parameter estimation

## Slide 5
1.1 Waveform generation
Different waveforms are generated in this module which includes:
New sequences
New waveforms
WLAN PPDUs with modification
Normal WLAN PPDU
…
Rui Du, et al. (Huawei)

## Slide 6
1.2 Transmitter
The signal is transmitted in this module with following parameters:
Antenna pattern/array geometry
Element radiation pattern (gain)
EIRP
Transmitter’s location
…
Rui Du, et al. (Huawei)

## Slide 7
1.3 Environment/channel model
The parameters of targets and multipath are added in this module which includes:
Target’s parameters
Numbers, RCS, Delay, Velocity, AOD, AOA, …
Multipath parameters
Inter cluster: Numbers, Delay, Power, AOD, AOA, …
Intra cluster: Average number of rays, Ray arrival rate, Ray power decay time (parameters for Poisson process)
Noise
Rui Du, et al. (Huawei)

## Slide 8
1.4 Receiver
The signal is received in this module with following parameters:
Antenna pattern/array geometry
Element radiation pattern (gain)
Receiver’s location
…
Rui Du, et al. (Huawei)

## Slide 9
1.5 Signal Processing
The received signal is processed with different algorithms to estimate target’s parameters and analyzes its relevant performance metrics:
Range estimation (range accuracy)
Velocity estimation (velocity accuracy)
Angle estimation (angle accuracy)
…
Rui Du, et al. (Huawei)

## Slide 10
2.1 Key modules may need to be calibrated
-common environment model/channel model
A common ‘environment model/channel model’ is needed for the comparison of performance from different contributions. The environment should include[1, 2]:
a few typical scenarios for WLAN sensing
Specific configurations (size of environment, objects properties in the environment, frequency, bandwidth, antenna configuration, …)
Target(s) to be sensed
Specific configurations (location, trajectory, …)
…
Previously discussions indicate that a few types of channel models(e.g. radar channel model, WLAN sensing channel model[1,2]) could be adopted for WLAN sensing. But, no matter which kind of channel model will be adopted by the group finally, it should be calibrated.
Rui Du, et al. (Huawei)

## Slide 11: 2.2 Key module may need to be calibrated - common basic sensing algorithms
For WLAN sensing, many algorithms are needed for target parameter estimation. There are two options for these algorithms that may be adopted in WLAN sensing.
Option 1: Some basic algorithms could be adopted commonly in the group to analyze the sensing performance (only affected by the standard modification).
Option 2: Put no restrictions on the algorithms and just compare the sensing performance (affected both by the standard modification and algorithms).
Rui Du, et al. (Huawei)

## Slide 12: Summary
A potential link level simulation for WLAN sensing and its initial analysis is presented in this contribution.
Two key modules (common environment model/channel model and common basic sensing algorithms) may need to be calibrated between different WLAN sensing contributions for the comparison of standard modification are discussed.
Rui Du, et al. (Huawei)

## Slide 13: References
[1] 11-20-0906-00-SENS-discussion-of-channel-model-for-wlan-sensing.pptx
[2] 11-20-1334-00-SENS-a-brief-description-of-the-channel-realization-generation-process.pptx
Rui Du, et al. (Huawei)

## Slide 14: SP 1
Do you support that the link level simulation proposed in slide 4 should be used in WLAN sensing simulation?
Yes:
No:
Abstain:
Rui Du, et al. (Huawei)

## Slide 15: SP 2
Do you support that the modules (environment/channel model and basic sensing algorithms) should be calibrated between different WLAN sensing contributions for the further performance comparison?
Yes:
No:
Abstain:
Rui Du, et al. (Huawei)