## Slide 1: TBDs of 11be PHY Capabilities
Date: 2020-10-14
Authors:
Name | Affiliations | Address | Phone | Email
Bin Tian | Qualcomm |  |  | btian@qti.qualcomm.com
Sameer Vermani |  |  |  | 
Steve Shellhammer |  |  |  | 
Youhan Kim |  |  |  | 
Notes: September 2012

## Slide 2: Introduction
In D0.1, 36.1.1 Introduction to the EHT PHY lists the following TBDs which need to be resolved
  Mandatory or optional support of preamble puncturing
  DCM MCS value and its mandatory or optional support
  Dup Mode MCS and its mandatory or optional support in 6GHz band
  Define ER-SU or not: discussed in 20/1132r0
  Support of LTF+GI combinations.
    Covered in 20/1238r4 SP #216 but M/O requirement is not discussed
  Support of midamble: Covered in 20/1238r4 SP#217
  Non-continuous channel 80+80 and 160+160 mandatory/optional support: discussed in 20/1100r0
  EHT-SIG MCS support: covered in 20/1238r4 SP#214
  RU/MRU restriction on 20MHz only operation non-AP EHT STA: discussed in 20/1441r2

## Slide 3: Support of Preamble Puncturing
Preamble puncturing applies to MU PPDU which are used for DL/UL SU and DL MU/OFDMA transmission
  TB PPDU has its own preamble transmission rule: preamble in the 20MHz channel(s) that contains the assigned RU
11be already defines
  Mandatory support RU/MRU set for OFDMA and non-OFDMA transmission
  OFDMA preamble puncturing pattern to be supported (Motion 131, #SP195)
    Up to one hole per 80MHz segment
    If punctured, the pattern of each 80 MHz segment shall be one of the following: X212, 1X12, 12X2, 121X, XX12, 12XX, 1XX2
11be shall support preamble puncturing but we need to clarify the mandatory/optional support set

## Slide 4: Preamble Puncturing Requirements
For non-AP STA, mandatory to support
  In OFDMA Rx, any preamble puncturing pattern allowed by (Motion 131, #SP195)
  In non-OFDMA Tx and Rx, any preamble puncturing pattern needed to support mandatory MRU for non-OFDMA as specified in D0.1 36.3.2.3.3
For AP, mandatory to support
  In OFDMA Tx and non-OFDMA Tx and Rx, any preamble puncturing pattern that needs to be supported for mandatory MRU in non-OFDMA as specified in D0.1 36.3.2.3.3
Main thoughts
  Provide AP schedule flexibility on DL and UL OFDMA transmission with preamble puncturing
  Client has to support all the potential preamble puncturing modes in OFDMA and non-OFDMA

## Slide 5: DCM Support
802.11be defines DCM for RU/M-RU size <= 996×2 plus RU 996×3 and 996×4 (Motion 122, #SP148)
  DCM +MCS0 is suggested as MCS15 in 20/1377r0
To balance implementation/testing complexity and benefit of DCM, we propose the following requirements for DCM+MCS0 (MCS15) support
  Mandatory in
    RU 26, 52, 106, 242 for all STAs
    RU 26, 52, 106, 242, 484 and 996 for non 20 MHz-only STAs
  Conditional mandatory in
    RU 2x996 when STA support 160 MHz
    RU 2x996 and 4x996 when STA supports 320 MHz
  Optional in
    MRU 52+26, 106+26, 484+242, 996+484, 996+484+242, 3x996
  Not supported in
    MRU 2x996+484, 3x996+484

## Slide 6: DCM + DUP Support
DCM+DUP mode is introduced for range extension in 6 GHz LPI channel
  DCM + DUP is suggested as MCS14 in 20/1377r0
We recommend the optional support of Dup+DCM mode for 6GHz band LPI channel
  Range extension feature may not be needed for some applications and market segments

## Slide 7: Support of LTF + GI Combinations
Prefer to keep the same mandatory/optional requirement as in 11ax except removing 1x LTF +0.8us GI combination for MU PPDU as agreed in 20/1238r4 SP#216
MU PPDU
  2x LTF + 0.8us GI (M)
  2x LTF + 1.6us GI (M)
  4x LTF + 3.2us GI (M)
  4x LTF + 0.8us GI (O)
TB PPDU
  2x LTF+1.6us GI (M)
  4x LTF + 3.2us GI (M)
  1x LTF + 1.6us GI (M)
    Note: this combination is CM in 11ax condition on support of UL MU-MIMO. In 11be UL MU-MIMO support is mandatory for client
NDP
  2x LTF + 0.8us GI (M)
  2x LTF + 1.6us GI (M)
  4x LTF + 3.2us GI (O)

## Slide 8: UL MU-MIMO and LTF
11ax mandates non-AP STA to support three LTF modes for UL MU-MIMO operation
  1x LTF +1.6us CP
    Shortest HE LTF duration so less sensitive to frequency error. In many cases no need for per stream frequency estimation and correction in HE-LTF
  Single stream pilot LTF mode: enable per stream frequency estimate and correction
  Frequency domain masked LTF
    Using frequency domain P mask to help per stream frequency estimate. Performance depends on channel flatness
To cut down mode, we recommend 11be not supporting masked LTF mode and only mandate non-AP STA to support
  1x LTF+1.6us CP mode
  Single stream pilot LTF mode

## Slide 9: Other TBDs Related to MU-MIMO
The non-AP EHT STA shall support transmitting UL MU-MIMO where the total spatial streams summed across all users is less than or equal to TBD
  R1: keep to 8, the same as for 11ax
Passed motion 124, #SP181
  DL MU-MIMO
    Mandatory support for AP with >=4 antennas
    Mandatory support for client
    At least for full BW. RU/M-RU support TBD
  UL MU-MIMO
    Mandatory support for AP with >=4 antennas
    Mandatory support for client
    At least for full BW. RU/M-RU support TBD
  Should clarify full BW here means non-OFDMA. Propose to change the highlighted text to
    Mandatory for non-OFDMA MU-MIMO on all RU/M-RU size >= 242 in supported BW. Optional for OFDMA+MU-MIMO operation

## Slide 10: SP 1
Do you support that in 11be
  For non-AP STA, mandatory to support
    In OFDMA Rx, any preamble puncturing pattern allowed by Motion 131, #SP195
    In non-OFDMA Tx and Rx, any preamble puncturing pattern needed to support mandatory MRU for non-OFDMA as specified in D0.1 36.3.2.3.3
  For AP, mandatory to support
    In OFDMA Tx and non-OFDMA Tx and Rx, any preamble puncturing pattern that needs to be supported for mandatory MRU in non-OFDMA as specified in D0.1 36.3.2.3.3
Y/N/ABS

## Slide 11: SP 2
Do you agree the following DCM+MCS0 support requirement in 11be
  Mandatory in
    RU 26, 52, 106 and 242 for 20 MHz-only STAs
    RU 26, 52, 106, 242, 484 and 996 for non 20 MHz-only STAs
  Conditional mandatory in
    RU 2x996 when STA supports 160 MHz
    RU 2x996 and 4x996 when STA supports 320 MHz
  Optional in
    MRU 52+26, 106+26, 484+242, 996+484, 996+484+242, 3x996
  Not supported in
    MRU 2x996+484, 3x996+484
Y/N/ABS

## Slide 12: SP 3
Do you agree the optional support of Dup+DCM mode for 6GHz band LPI channel in 11be?
Y/N/ABS

## Slide 13: SP 4
Do you agree the following mandatory/optional support requirement of LTF+GI combinations in 11be ?
  MU PPDU
    2x LTF + 0.8us GI (M)
    2x LTF + 1.6us GI (M)
    4x LTF + 3.2us GI (M)
    4x LTF + 0.8us GI (O)
  TB PPDU
    2x LTF+1.6us GI (M)
    4x LTF + 3.2us GI (M)
    1x LTF + 1.6us GI (M)
  NDP
    2x LTF + 0.8us GI (M)
    2x LTF + 1.6us GI (M)
    4x LTF + 3.2us GI (O)
Y/N/ABS

## Slide 14: SP 5
Do you agree that in 11be UL TB PPDU does not support masked LTF mode and only mandate non-AP STA to support
  1x LTF+1.6us CP mode
  Single stream pilot LTF mode
Y/N/ABS

## Slide 15: SP 6
Do you support in 11be the non-AP EHT STA shall support transmitting UL MU-MIMO where the total spatial streams summed across all users is less than or equal to 8 in R1?
  Note: same as in 11ax
Y/N/ABS

## Slide 16: SP 7
Do you support to amend motion 124, #SP181 as
  DL MU-MIMO
    Mandatory support for AP with >=4 antennas
    Mandatory support for client
    Mandatory for non-OFDMA on all RU/M-RU size>=242 in supported BW
    Optional for OFDMA+MU-MIMO operation
  UL MU-MIMO
    Mandatory support for AP with >=4 antennas
    Mandatory support for client
    Mandatory for non-OFDMA on all RU/M-RU size>=242 in supported BW
    Optional for OFDMA+MU-MIMO operation
Y/N/ABS