## Slide 1: Spatial Stream Allocation in Trigger Frames
Date: 2020-10-1
Authors:
Name | Affiliations | Address | Phone | email
Mengshi Hu | Huawei |  |  | humengshi@huawei.com
Ross Jian Yu | Huawei |  |  | ross.yujian@huawei.com
Ming Gan | Huawei |  |  | ming.gan@huawei.com
Junghoon Suh | Huawei |  |  | junghoon.suh@huawei.com
Yan Xin | Huawei |  |  | yan.xin@huawei.com
Osama Aboul-Magd | Huawei |  |  | osama.aboulmagd@huawei.com

## Slide 2: Background
Trigger Frame in 11ax
  A trigger frame allocates resources for and solicits one or more TB PPDU transmissions.
  The User Info List field in a trigger frame contains zero or more User Info fields.
  The allocated RU of a user is indicated by the RU Allocation subfield in the User Info field.
  The spatial stream (SS) allocation of the allocated RU is indicated by the SS Allocation subfield in the User Info field.
Note: This contribution only focuses on the cases when the above green block represents the SS Allocation subfield.
Trigger frame format in 11ax

## Slide 3: SS Allocation subfield in 11ax
In the trigger frame in 11ax, the SS Allocation subfield indicates the spatial streams of the solicited HE TB PPDU and the format can be further shown as follows:
  The Starting Spatial Stream subfield indicates the starting spatial stream and is set to the starting spatial stream minus 1.
  The Number Of Spatial Streams subfield indicates the number of spatial streams, and is set to the number of spatial streams minus 1.
SS Allocation subfield format in 11ax

## Slide 4: Problem of SS Allocation in 11be
The configurations of the number of STS (NUM_STS) in TB PPDU in 11ax and 11be are shown as follows [1-2]:
Case | NUM_STS in 11ax | NUM_STS in 11be
NUM_STS per user per MU-MIMO RU | 1-4 | 1-4
NUM_STS summed over all users per RU | 1-8 | 1-16*1
NUM_STS for an RU assigned to no more than 1 user | 1-8 | 1-16*2
MU-MIMO RU
User x
User 1
1-4 spatial streams in 11ax and 11be
…
1-8 spatial streams in 11ax
1-16 spatial streams in 11be
(*1 Motion: 802.11be supports a maximum of 16 spatial streams (total across all the scheduled STAs) for MU-MIMO)
Non MU-MIMO RU
User 1
1-8 spatial streams in 11ax
1-16 spatial streams in 11be
(*2 Motion: 802.11be defines a maximum of 16 spatial streams for SU-MIMO)

## Slide 5: Problem of SS Allocation in 11be
According to the table, a 6-bit SS Allocation subfield is enough to indicate Starting Spatial Stream and Number Of Spatial Streams in 11ax.
If we follow the 11ax style in 11be, an 8-bit SS Allocation subfield is needed, where 4 bits for Starting Spatial Stream and 4 bits for Number Of Spatial Streams.
  An 8-bit SS Allocation subfield seems unacceptable if we have the same length of User Info field as in 11ax, because there is no enough room for it. Therefore, in the following we propose to indicate SS Allocation with smaller bits for both MU-MIMO and non-MU-MIMO users.
Case | NUM_STS in 11ax | NUM_STS in 11be
NUM_STS per user per MU-MIMO RU | 1-4 | 1-4
NUM_STS summed over all users per RU | 1-8 | 1-16
NUM_STS for an RU assigned to no more than 1 user | 1-8 | 1-16

## Slide 6: Option 1: MU-MIMO/Non-MU-MIMO Indication
Here we propose to indicate SS Allocation with 7 bits. To support this, an MU-MIMO/Non-MU-MIMO indication is suggested to be added to the User Info field. The detail is shown as follows:
From the above table, 7 bits (1+4+2 bits) are enough for SS Allocation indication.
  When the MU-MIMO/Non-MU-MIMO indicates an MU-MIMO user, a 4-bit Starting Spatial Stream and a 2-bit Number Of Spatial Streams is enough for SS Allocation of an MU-MIMO user.
  When the MU-MIMO/Non-MU-MIMO indicates a non-MU-MIMO user, a 4-bit Number Of Spatial Streams is enough for SS Allocation of a non-MU-MIMO user.
  Note 1: The 1 bit MU-MIMO/Non-MU-MIMO can either belong to SS Allocation subfield or not.
  Note 2: The above two reserved bits can be used for other indications.

## Slide 7: Option 2: Implicit MU-MIMO/Non-MU-MIMO Indication
The User Info field in EHT TF may most likely include the AID, RU Allocation and SS Allocation sub-fields like in 11ax TF.
The receiver decodes the TF up to the FCS, and naturally configures how many times the same RU Allocation repeats across all the User Info fields.
  The same RU Allocation appears multiple times across the multiple User Info fields may imply the MU-MIMO SS Allocation sub-field.
  The RU Allocation appears once in a User Info field may imply the non-MU-MIMO SS Allocation sub-field.
Option 2 requires only 6 bits, since the MU-MIMO/non-MU-MIMO is implicitly indicated as above.
  4 bits for the Starting Spatial Streams and 2 bits for the Number of Spatial Streams in case of MU-MIMO
  4 bits for the Number of Spatial Streams and 2 bits assigned as Reserved in case of non-MU-MIMO
11ax TF Format

## Slide 8: Option 3: Implicit Starting Stream Indication
We propose to implicitly indicate the Starting Stream for the MU-MIMO in Option 3
  SU/MU-MIMO is implicitly configured with checking how many times the same RU Allocation repeats
  When the same RU Allocation repeats multiple times, the receiver computes the sum of Spatial Streams indicated in those User Info fields with the same RU Allocation prior to the corresponding User Info field with the same RU Allocation
    E.g.) User Info field 1:AID abc, RU 1234, Num_SS 2, User Info field 2: AID xyz, RU 1234, Num_SS 4, User Info field 3: AID def, RU 1234, Num_SS 2, User Info field 4: AID ghi, RU 5678, Num_SS 2
      User Info field 1 ~ 3 are for MU-MIMO Users, and User Info field 4 is for an SU-MIMO user
      The Starting Stream for the User Info field 3 is the 7th Stream (Prior Sum of Streams is 2+4).
Option 3 requires only 4 bits.
  2 bits for the Number of Spatial Streams and 2 bits left for the Reserved in case of MU-MIMO
  4 bits for the Number of Spatial Streams in case of non-MU-MIMO

## Slide 9: Summary
Proposed to add an MU-MIMO/Non-MU-MIMO indication to the User Info field in trigger frames.
Option 1: 7 bits (1+4+2 bits) are enough for SS Allocation indication.
Option 2: 6 bits (Starting Spatial Stream 4 and Number of Spatial Stream 2bits for MU-MIMO case, Number of Spatial Stream 4 and Reserved 2 bits for non-MU-MIMO case)
Option 3: 4 bits (Number of Spatial Stream 2 and Reserved 2bits for MU-MIMO case, Number of Spatial Stream 4 bits for non-MU-MIMO case)

## Slide 10: Straw Poll #1
  Do you agree that a 4-bit Number Of Spatial Streams is used for SS Allocation of a non-MU-MIMO user in the User Info field of a trigger frame?
  Y
  N
  A

## Slide 11: Straw Poll #2
  Do you agree that a 4-bit Starting Spatial Stream and a 2-bit Number Of Spatial Streams are used for SS Allocation of an MU-MIMO user in the User Info field of a trigger frame?
  Y
  N
  A

## Slide 12: Straw Poll #3
Do you agree that a 1-bit MU-MIMO/Non-MU-MIMO indication is added to the User Info field of a trigger frame?
  Y
  N
  A

## Slide 13: Straw Poll #4
Do you agree to implicitly indicate the MU-MIMO and non-MU-MIMO in the User Info fields?
  Y
  N
  A

## Slide 14: Straw Poll #5
In case of implicit indication of MU-MIMO/non-MU-MIMO in User Info fields, do you support to have 2 bits for the MU-MIMO Number of Spatial Streams in User Info field without the Starting Stream indication?
  Y
  N
  A

## Slide 15
[1] IEEE P802.11ax™/D7.0
[2] IEEE 802.11-20/0566r74 Compendium of straw polls and potential changes to the Specification Framework Document
[3] IEEE 802.11-20/1429r2 Enhanced Trigger Frame for EHT Support
References