## Slide 1: TWT for MLD
Date: 2020-11-01
Authors:

## Slide 2: Background
We agree that the individual TWT agreement(s) could be set up on a setup link for more than one setup link in R1 [1].
  The same TWT parameters could be applied for more than one link, such as Target Wake time, Nominal Minimum TWT Wake Duration and TWT Wake Interval
  Support both the peak throughput and power save
In this contribution, we address the remaining issue of TWT setup for multi-link device

## Slide 3: Recap-TWT
TWT element

## Slide 4: TWT for multi-link device
We propose to add “Link ID Bitmap Present” bit to the Control field of the TWT element
  “Link ID Bitmap Present” bit indicates if Link ID Bitmap subfield is present
  If “Link ID Bitmap Present” bit is set to 1, then Link Bitmap subfield will be present in TWT parameter Information field
  Link ID Bitmap subfield indicate the links to which the TWT element negotiated by a STA is applied
 | NDP Paging Indicator | Responder PM Mode | Negotiation Type | TWT Information Frame disable | Wake Duration Unit | Multi-link | Reserved
Bits: | 1 | 1 | 2 | 1 | 1 | 1 | 1
 | Request Type | Target Wake Time | TWT Group Assignment | Nominal Minimum TWT Wake Duration | TWT Wake Interval Mantissa | TWT Channel | NDP Paging (optional) | Link ID Bitmap
Octets: | 2 | 8 or 0 | 9 or 3 or 0 | 1 | 2 | 1 | 0 or 4 | 0 or 1
Control field
TWT parameter Information field

## Slide 5: Summary
In this contribution, we address the remaining issue of individual TWT setup for multi-link device
  Add Link ID Bitmap Present bit to the Control field of the TWT element
  Add Link Bitmap subfield to the TWT parameter Information field of the TWT element

## Slide 6: References
[1] 11-19-1988-03-00be-power-save-for-multi-link

## Slide 7: SP 1
Do you agree to add the following signal to TWT element for individual TWT setup between two MLDs
  Add Link ID Bitmap Present bit to the Control field of the TWT element
  Add Link Bitmap subfield to the TWT parameter Information field of the TWT element