## Slide 1: IEEE 802.11ax Backward Compatible Trigger Frame RU Allocation Table
Date: 2020-12-15
Authors:
Name | Affiliations | Email
Steve Shellhammer | Qualcomm | shellhammer@ieee.org
Ron Porat | Broadcom | ron.porat@broadcom.com
DJ Moelker |  | dignus-jan.moelker@broadcom.com

## Slide 2: Revision Edits
Added a Straw Poll on the use of Primary/Secondary indication for the RU/MRUs in the RU Allocation Table
Relabel the “LU” bit to the “PS160” bit
Description of the logic for the use of primary/secondary signaling is provided in,
  S. Shellhammer, et. al., ”Enhanced Trigger Frame for EHT Support,” IEEE 802.11-20/1429r3, December 2020

## Slide 3: IEEE 802.11ax RU Allocation Table
Entries 0-68 already assigned
Entries 69-127 available for additional RUs/MRUs
  59 available entries

## Slide 4: MRU26+52 – Indexing
The draft does not assign MRU indices to small MRUs
These indices are needed for the RU Allocation Table
If we were to assign indices in frequency order, we find that the indices of the MRUs within a 40 MHz PPDU do not match the indices of the MRUs within the lower half of the 80 MHz PPDU

## Slide 5: MRU26+52 – Recommended Indexing
With this recommended Indexing the indices in the 40 MHz PPDU match those of the lower part of the 80 MHz PPDU
With this approach the MRU Index uniquely identifies the MRU, within a 20 MHz, 40 MHz or 80 MHz PPDU

## Slide 6: MRU26+106 – Recommended Indexing
With this recommended indexing the MRU index uniquely identifies the MRU within a 20 MHz, 40 MHz or 80 MHz PPDU

## Slide 7: RU Allocation Table Entries
B7-B1 of the RU Allocation Subfield | MRU | MRU Index
69 | RU996x4 | RU1
70-75 | MRU26+52 | MRU1 to MRU6, respectively
76 | Reserved | 
77-80 | MRU26+52 | MRU8 to MRU11, respectively
81 | Reserved | 
82-86 | MRU26+106 | MRU1 to MRU5, respectively
87-88 | Reserved | 
89 | MRU26+106 | MRU8
90-93 | MRU484+242 | MRU1 to MRU4, respectively
Add in RU996x4 and the MRUs < 80 MHz
This leaves 34 table entries (94 to 127)

## Slide 8: Remaining RUs/MRUs
MRU | Total Number in 320 MHz
MRU996+484 | 8
MRU996+484+242 | 16
MRU2x996+484 | 12
MRU3x996 | 4
MRU3x996+484 | 8
TOTAL | 48

## Slide 9: MRU996+484
B0
B7-B1
0
0
94
95
1
1
94
95
B0 and B7-B1 indicate MRU within 160 MHz
PS160 indicates which 160 MHz

## Slide 10: MRU996+484+242
B0
B7-B1
0
0
96
97
0
0
98
99
1
1
96
97
1
1
98
99
B0 and B7-B1 indicate MRU within 160 MHz
PS160 indicates which 160 MHz

## Slide 11: MRU2x996+484
0
0
100
101
0
0
0
0
102
103
0
0
1
1
100
101
0
0
0
0
102
103
1
1
1
1
100
101
1
1
1
1
102
103
1
1
B0
B7-B1
PS160
Encoding/Decoding Rules
PS160 provides location of the 240
B0, B1, B2, PS160 provide location of punctured RU484 within the MRU
Location of punctured RU484 within the MRU using
0
1
2
3
4
5
0
1
2
3
4
5
0
1
2
3
4
5
0
1
2
3
4
5

## Slide 12: MRU3x996
B0
B7-B1
1
0
104
104
1
0
104
104
PS160
0
0
1
1

## Slide 13: MRU3x996+484
B0
B7-B1
0
0
105
106
1
1
105
106
PS160
0
0
0
0
0
0
105
106
1
1
105
106
1
1
1
1

## Slide 14: Reserved Entries
B7-B1 of the RU Allocation Subfield | MRU
107-127 | Reserved
A total of 21 reserved table entries

## Slide 15: RU Allocation Table
Detailed RU Allocation Table Word document, embedded in the Presentation

## Slide 16: Straw Poll #1
Do you agree that in the User Info Field of the Trigger Frame the following bits indicate the following?
  B0 of the RU Allocation subfield indicates Primary/Secondary 80 MHz Channel for RU/MRU 80 MHz, for P160
    Note: This is the same as in 11ax
    Note: For RUs/MRUs > 80 MHz, B0 is used to indicate a specific MRU and does not have a primary/secondary meaning
  PS160 (B39) indicates Primary/Secondary 160 MHz for RU/MRU 160 MHz
    Note: For RUs/MRUs > 160 MHz, PS160 is used to indicate a specific MRU and does not have a primary/secondary meaning
  For S160 the definition of B0 is TBD, for RU/MRU 80 MHz

## Slide 17: Straw Poll #2
Do you agree to include the following entries in the Trigger Frame RU Allocation Table?
B7-B1 of the RU Allocation Subfield | MRU | MRU Index
69 | RU996x4 | RU1
70-75 | MRU26+52 | MRU1 to MRU6, respectively
76 | Reserved | 
77-80 | MRU26+52 | MRU8 to MRU11, respectively
81 | Reserved | 
82-86 | MRU26+106 | MRU1 to MRU5, respectively
87-88 | Reserved | 
89 | MRU26+106 | MRU8
90-93 | MRU484+242 | MRU1 to MRU4, respectively

## Slide 18: Straw Poll #3
Do you agree to include the following entries in the Trigger Frame RU Allocation Table?
B0
B7-B1
0
0
94
95
1
1
94
95
B0 and B7-B1 indicate MRU within 160 MHz
PS160 indicates which 160 MHz

## Slide 19: Straw Poll #4
Do you agree to include the following entries in the Trigger Frame RU Allocation Table?
B0
B7-B1
0
0
96
97
0
0
98
99
1
1
96
97
1
1
98
99
B0 and B7-B1 indicate MRU within 160 MHz
PS160 indicates which 160 MHz

## Slide 20: Straw Poll #5
Do you agree to include the following entries in the Trigger Frame RU Allocation Table?
0
0
100
101
0
0
0
0
102
103
0
0
1
1
100
101
0
0
0
0
102
103
1
1
1
1
100
101
1
1
1
1
102
103
1
1
B0
B7-B1
PS160

## Slide 21: Straw Poll #6
Do you agree to include the following entries in the Trigger Frame RU Allocation Table?
B0
B7-B1
1
0
104
104
1
0
104
104
PS160
0
0
1
1

## Slide 22: Straw Poll #7
Do you agree to include the following entries in the Trigger Frame RU Allocation Table?
B0
B7-B1
0
0
105
106
1
1
105
106
PS160
0
0
0
0
0
0
105
106
1
1
105
106
1
1
1
1

## Slide 23: Straw Poll #8
Do you support the Trigger Frame RU Allocation Table design embedded in Slide 15 of document IEEE 802.11-20/1703r4?