## Slide 1: Table based preamble puncture indication for OFDMA transmission
Date: 2020-10-26
Authors:
Name | Affiliations | Address | Phone | email
Ross Jian Yu | Huawei |  |  | ross.yujian@huawei.com
Mengshi Hu | Huawei |  |  | 
Ming Gan | Huawei |  |  | 

## Slide 2: Introduction and Recap
The following SP has passed:
Straw poll #233
802.11be supports punctured channel information field in U-SIG to be ‘5 bits + 1 reserved bit adjacent to it’ in the version dependent section. ?
  Non-OFDMA: use a 5 bit BW dependent table to signal the puncturing pattern of the entire PPDU BW.
  OFDMA: 4 bits to indicate which 20 MHz is punctured in the current 80 MHz.
  1 bit out of the 5 bits is not used for the OFDMA case.
  1 reserved bit for possible future expansion (e.g., more puncturing patterns in R2) of non-OFDMA puncturing modes.
  Interpretation of the field shall be dependent on the transmission being OFDMA vs. non-OFDMA. [#SP233]
[20/1238r6 (Open Issues on Preamble Design, Sameer Vermani, Qualcomm), SP#1, Y/N/A: 50/7/16]
For OFDMA case, how to indicate preamble puncture for the current 80MHz is TBD.

## Slide 3: Preamble puncture patterns
Preamble puncture pattern for non-OFDMA [1]
Preamble puncture pattern for OFDMA [2]:
  No puncture (same as non-OFDMA case)
  X212 (same as non-OFDMA case)
  1X12 (same as non-OFDMA case)
  12X2 (same as non-OFDMA case)
  121X (same as non-OFDMA case)
  XX12
  12XX
  1XX2
PPDU BW | Cases | # of Entires | Note
80MHz | No puncturing | 1 | 
 | 20MHz punctured | 4 | 
 | Total | 5 | 
160MHz | No puncturing | 1 | 
 | 20MHz punctured | 8 | 
 | 40MHz punctured | 4 | 
 | Total | 13 | 
320MHz | No puncturing | 1 | 
 | 40MHz punctured | 8 | 
 | 80MHz punctured | 4 | 240/160+80MHz: [1 1 1 x], [1 1 x 1], [1 x 1 1], [x 1 1 1]
 | 320-80-40 | 12 | For each contiguous 240MHz ([1 1 1 1 1 1 x x] and [x x 1 1 1 1 1 1]), one out of six 40MHz may be punctured
 | Total | 25 | 

## Slide 4: Unified table based preamble puncture method
PPDU BW | Cases |  | Value
80MHz | No puncturing | [1 1 1 1] | 0
 | 20MHz punctured | [x 1 1 1] | 1
 |  | [1 x 1 1] | 2
 |  | [1 1 x 1] | 3
 |  | [1 1 1 x] | 4
 | Reserved | Reserved | 5-31
Non-OFDMA case
PPDU BW | Cases |  | Value
80MHz/160MHz/320MHz | No puncturing | [1 1 1 1] | 0
 | 20MHz punctured | [x 1 1 1] | 1
 |  | [1 x 1 1] | 2
 |  | [1 1 x 1] | 3
 |  | [1 1 1 x] | 4
 | 40MHz punctured | [x x 1 1] | 5
 |  | [1 1 x x] | 6
 |  | [1 x x 1] | 7
 |  | Reserved | 8-15
OFDMA case
Additional 1 bit reserved for more patterns
A unified table based method for non-OFDMA and OFDMA case is shown below:
  Only define supported entries for now, no need to separately define which mode is supported and which is not
  Same method for the common punctured case
  Support up to 24 types of future extension

## Slide 5: Unified table based preamble puncture method (cont’d)
Two tables can be merged to one if needed:
160MHz non-OFDMA | No puncturing | [1 1 1 1 1 1 1 1] | 0
 | 20MHz punctured | [x 1 1 1 1 1 1 1] | 1
 |  | [1 x 1 1 1 1 1 1] | 2
 |  | [1 1 x 1 1 1 1 1] | 3
 |  | [1 1 1 x 1 1 1 1] | 4
 |  | [1 1 1 1 x 1 1 1] | 5
 |  | [1 1 1 1 1 x 1 1] | 6
 |  | [1 1 1 1 1 1 x 1] | 7
 |  | [1 1 1 1 1 1 1 x] | 8
 | 40MHz punctured | [x x 1 1 1 1 1 1] | 9
 |  | [1 1 x x 1 1 1 1] | 10
 |  | [1 1 1 1 x x 1 1] | 11
 |  | [1 1 1 1 1 1 x x] | 12
 | Reserved | Reserved | 13-31
PPDU BW | Cases |  | Value | Description
80MHz non-OFDMA or 80MHz/160MHz/320MHz OFDMA | No puncturing | [1 1 1 1] | 0 | 
 | 20MHz punctured | [x 1 1 1] | 1 | 
 |  | [1 x 1 1] | 2 | 
 |  | [1 1 x 1] | 3 | 
 |  | [1 1 1 x] | 4 | 
 | 40MHz punctured | [x x 1 1] | 5 | For OFDMA only, reserved for non-OFDMA
 |  | [1 1 x x] | 6 | 
 |  | [1 x x 1] | 7 | 
 |  | Reserved | 8-15 | 
 |  | Reserved | 16-31 | For non-ODFMA only
Note: One digit means 20MHz

## Slide 6: Unified table based preamble puncture method (cont’d)
Two tables can be merged to one if needed:
PPDU BW | Cases |  | Value
320MHz non-OFDMA | No puncturing | [1 1 1 1 1 1 1 1] | 0
 | 40MHz punctured | [x 1 1 1 1 1 1 1] | 1
 |  | [1 x 1 1 1 1 1 1] | 2
 |  | [1 1 x 1 1 1 1 1] | 3
 |  | [1 1 1 x 1 1 1 1] | 4
 |  | [1 1 1 1 x 1 1 1] | 5
 |  | [1 1 1 1 1 x 1 1] | 6
 |  | [1 1 1 1 1 1 x 1] | 7
 |  | [1 1 1 1 1 1 1 x] | 8
 | 80MHz punctured | [x x 1 1 1 1 1 1] | 9
 |  | [1 1 x x 1 1 1 1] | 10
 |  | [1 1 1 1 x x 1 1] | 11
 |  | [1 1 1 1 1 1 x x] | 12
PPDU BW | Cases |  | Value
320MHz non-OFDMA | 320-80-40 | [x x x 1 1 1 1 1] | 13
 |  | [x x 1 x 1 1 1 1] | 14
 |  | [x x 1 1 x 1 1 1] | 15
 |  | [x x 1 1 1 x 1 1] | 16
 |  | [x x 1 1 1 1 x 1] | 17
 |  | [x x 1 1 1 1 1 x] | 18
 |  | [x 1 1 1 1 1 x x] | 19
 |  | [1 x 1 1 1 1 x x] | 20
 |  | [1 1 x 1 1 1 x x] | 21
 |  | [1 1 1 x 1 1 x x] | 22
 |  | [1 1 1 1 x 1 x x] | 23
 |  | [1 1 1 1 1 x x x] | 24
 | Reserved | Reserved | 25-31
Note: One digit means 40MHz

## Slide 7: Straw Poll #1
802.11be supports the following:
  For OFDMA: 4 bits to indicate which 20 MHz is punctured in the current 80 MHz, the indication is as follows:
PPDU BW | Cases |  | Value
80MHz/160MHz/320MHz | No puncturing | [1 1 1 1] | 0
 | 20MHz punctured | [x 1 1 1] | 1
 |  | [1 x 1 1] | 2
 |  | [1 1 x 1] | 3
 |  | [1 1 1 x] | 4
 | 40MHz punctured | [1 1 x x] | 5
 |  | [x x 1 1] | 6
 |  | [1 x x 1] | 7
 |  | Reserved | 8-15

## Slide 8
https://mentor.ieee.org/802.11/dcn/20/11-20-1238-07-00be-open-issues-on-preamble-design.pptx
https://mentor.ieee.org/802.11/dcn/20/11-20-0566-80-00be-compendium-of-straw-polls-and-potential-changes-to-the-specification-framework-document.docx
References