## Slide 1: 802.11bd NGV Ranging Status and Types
Date: 2020-11-03
Authors:

## Slide 2: Abstract
We review contributions on ranging for 802.11bd NGV and summarize the different ranging types. This leads to straw polls asking:
What preferences does the group have on the different ranging types?

## Slide 3: 802.11bd NGV Documents Addressing Ranging
PAR/FRD [1], [2]: “amendment defines procedures for at least one form of positioning in conjunction with V2X communications”
UC Doc [3]: UC5 Vehicular Positioning & Location, UC8 Train-to-Train, UC9 Vehicle-to-Train
SFD [4]: “11bd supports round-trip-time (RTT) ranging for 10 MHz and 20 MHz bandwidth PPDUs.”
Draft 0.4: “An NGV PHY shall support the following features:
  Round trip time (RTT) based ranging using 10 and 20 MHz bandwidth PPDUs”

## Slide 4: 802.11bd NGV Contributions Addressing Ranging
Positioning Use Cases for NGV [5]
NGV Ranging Discussions [6]: FTM, NTB, TB, and passive TB ranging
Ranging Performance in 11bd [7] : Performance results NTB ranging
Considerations on Ranging in NGV [8]: Performance results one-way TOF & RTT ranging, 60 GHz
On ranging methods for NGV [9]: First comparison one-way TOF, two-way RTT, FTM EDCA, and NTB ranging
Ranging Protocol in 11bd [10]: Ranging advertisement & NTB ranging
Influence of Delay-Close Multi Path Components on FTM-RTT [11]: Performance results RTT ranging

## Slide 5
Ranging type | One-Way TOF [8,9] | Two-way RTT [8,9,11] | FTM EDCA [6,9,11] | NTB [6,7, 9,10] | Passive TOF/RTT/ FTM EDCA /NTB | TB [6] | Passive TB [6]
Standard | - | - | 802.11-2016 | 802.11az | - | 802.11az | 802.11az
Challenges | accurate absolute timing at each STA; TOD (sub ns accuracy) & TX location included in measurement frame | TODs (sub ns accuracy) & TX location included in measurement frame and/or fixed timing for reply ACK | high channel load (≥ 6 frames), 30 ms  100 ms position (no parallel ex-change) | 5 frames in one TXOP, 0.6 ms,  2 ms position | additional measurement reports depending on ranging type | 7-9 frames in one TXOP, AP based, spatial streams UL and DL, not OCB | 13 frames in one TXOP, based on TB
Transmitted frames | 1 | 2 | ≥ 6 | 4-5 | + 1 meas. report | 7-9 | ≥ 13
Security/ Privacy | - | - | - | optionally | depending on type | optionally | No
11bd Changes | strict timing synchronization, TOD in measure-ment frame | TOD in measurement frame, exchange in one TXOP | None, reduce frames, parallel ranging ex-change | ranging NDP | depending on type | adaptation to OCB | Only with TB, adaptation to OCB

## Slide 6
Ranging type | One-Way TOF [8,9] | Two-way RTT [8,9,11] | FTM EDCA [6,9,11] | NTB [6,7, 9,10] | Passive two-way RTT/ FTM EDCA /NTB | TB [6] | Passive TB [6]
Standard | - | - | 802.11-2016 | 802.11az | - | 802.11az | 802.11az
Challenges | accurate absolute timing at each STA; TOD (sub ns accuracy) & TX location included in measurement frame | TODs (sub ns accuracy) & TX location included in measurement frame and/or fixed timing for reply ACK | high channel load (≥ 6 frames), 30 ms  100 ms position (no parallel ex-change) | 5 frames in one TXOP, 0.6 ms,  2 ms position | additional measurement reports depending on ranging type | 7-9 frames in one TXOP, AP based, spatial streams UL and DL, not OCB | 13 frames in one TXOP, based on TB
Transmitted frames | 1 | 2 | ≥ 6 | 4-5 | + 1 meas. report | 7-9 | ≥ 13
Security/ Privacy | - | - | - | optionally | depending on type | optionally | No
11bd Changes | strict timing synchronization, TOD in measure-ment frame | TOD in measurement frame, exchange in one TXOP | None, reduce frames, parallel ranging ex-change | ranging NDP | depending on type | adaptation to OCB | Only with TB, adaptation to OCB
Not feasible
Not feasible

## Slide 7: Mandatory vs. Optional Ranging Types
Optional ranging types
  Need for advertisement and negotiation
  Higher flexibility for different applications
Mandatory ranging type(s)
  All NGV devices possible I/RSTA
  No need for advertisement and negotiation  E.g. NTB ranging advertisement unnecessary
  Mandatory capture of accurate TOA/TOD of frames  E.g. FTM EDCA Ranging FTM Request unnecessary
 Faster ranging and positioning

## Slide 8: Conclusions
Five ranging types plus passive methods
  One-way TOF: time synchronization and fast time stamp
  Two-way RTT: fast time stamp and fixed timing for ACK (processing time)
  FTM EDCA: simplest implementation, but high overhead and slow
  NTB: define additional frames , but smaller overhead and fast
  Passive Two-way RTT/FTM EDCA/NTB: One additional measurement report per ranging exchange and additional info
  TB and passive TB: Significant changes to work OCB
Mandatory vs. optional ranging type(s):
  Flexibility
  Reduced channel use
  Faster ranging and positioning

## Slide 9: References
[1] Project Authorization Request (PAR) 11-18-0861r9
[2] TGbd Functional Requirements Document (FRD) 11-19-0495r3
[3] TGbd Use Case Document 11-19-1342r1
[4] TGbd Spec Framework Document (SFD) 11-19-11-19-0497r7
[5] Location use cases for NGV 11-18-1221r0
[6] NGV ranging discussion 11-18-1250r0
[7] Ranging Performance in 11bd 11-19-0859r0
[8] Considerations on Ranging in NGV 11-19-0788r3
[9] On ranging methods for NGV 11-19-1892r0
[10] Ranging Protocol in 11bd 11-19-2011r0
[11] Influence of Delay-close Multi Path Components on FTM-RTT 11-19-1929r1

## Slide 10: SP #1
Which ranging type should be implemented in 802.11bd NGV?
Ranging type | Two-way RTT [8,9,11] | FTM EDCA [6,9,11] | NTB [6,7,9,10] | Passive two-way RTT | Passive FTM EDCA | Passive NTB
Yes |  |  |  |  |  | 
No |  |  |  |  |  | 
Need more information/ Abstain |  |  |  |  |  | 

## Slide 11: SP #2
Should ranging type X be mandatory or optional in 802.11bd NGV?
Ranging type | Two-way RTT [8,9,11] | FTM EDCA [6,9,11] | NTB [6,7,9,10] | Passive two-way RTT | Passive FTM EDCA | Passive NTB
Mandatory |  |  |  |  |  | 
Optional |  |  |  |  |  | 
Need more information/ Abstain |  |  |  |  |  |