## Slide 1: PDT-TBD-EMLSR mode operation
Date: 2020-11-9
Authors:

## Slide 2: Introduction
In 802.11be D0.1, the following details of the EMLSR mode operation were not decided and left as TBDs:
  Indication of the limitations of the initial Control frame of a frame exchange sequence
    “The initial Control frame of a frame exchange sequence may have one or more limitations for the following parameters: the number of spatial streams, MCS(s) (or data rate(s) for non-HT PPDU), PPDU type(s), and frame type(s).”
  Link switch delay signaling and values
    “The non-AP MLD may indicate its link switch delay in a TBD management frame”
In this presentation, we propose details for the TBDs in Subclause 35.3.13 Enhanced multi-link single radio operation of 802.11be Draft 0.1

## Slide 3: Indication of the limitations of the initial Control frame
Discussions during the D0.1 PDT writing
  For a simple implementation and clear operation of the EMLSR mode, instead of each non-AP MLD indicating the limitations to an AP MLD, it is better to have a set of limitations defined in the spec
  Link switch delay should be considered and frames that can accommodate MAC padding should be used
Proposed set of limitations for the initial Control frame
Parameters | Limitations
Number of spatial streams | 1
PPDU type | Non-HT or non-HT duplicate PPDU
Data rate | 6, 12, 24 Mbps
Frame type | MU-RTS and BSRP Trigger frames (Note: mandatory or optional support for the non-AP MLD is TBD )

## Slide 4: Link switch delay signaling and values
The Padding field in a Trigger frame can be used to add the additional time needed by the non-AP MLD to operate in the EMLSR mode
We propose to define a field (EMLSR Delay field) in a TBD (MLD-level) element
  The field indicates the MAC padding duration of the Padding field for the initial Control frame for the additional time needed by the non-AP MLD when operating in the EMLSR mode
The EMLSR Delay field is 3 bits and encoded as follows
  0: 0 usec
  1: 32 usec
  2: 64 usec
  3: 128 usec
  4: 256 usec
  5-7: reserved

## Slide 5: Proposed changes to the draft text in 35.3.13 Enhanced multi-link single radio operation of 802.11be Draft 0.1
TGbe editor: make the following changes to the paragraph in P104L6 of subclause 35.3.13 Enhanced multi-link single-radio in 802.11be Draft 0.1:
35.3.13 Enhanced multi-link single radio operation
…
When a non-AP MLD is operating in the EMLSR mode with an AP MLD supporting the EMLSR mode the following applies:
— The non-AP MLD shall be able to listen on the enabled links, by having its affiliated STA(s) corresponding to those links in the awake state. The listening operation includes CCA and receiving the initial Control frame of a frame exchange sequence that is initiated by an AP MLD.
— The initial Control frame of a frame exchange sequence shall be sent in the non-HT or non-HT duplicate PPDU format with a rate of 6 Mbps, 12 Mbps, or 24 Mbps.
— The initial Control frame shall be an MU-RTS Trigger frame or a BSRP Trigger frame. (Note: mandatory or optional support for the non-AP MLD of reception of MU-RTS and BSRP Trigger frames is TBD) may have one or more limitations for the following parameters: the number of spatial streams, MCS(s) (or data rate(s) for non-HT PPDU), PPDU type(s), and frame type(s).
— The non-AP MLD may indicate the time needed by the non-AP MLD in the EMLSR Delay field in the TBD element, which is the MLD level capabilities element. its link switch delay in a TBD management frame. The value in the EMLSR Delay field indicates the MAC padding duration of the Padding field of the initial Control frame. The EMLSR Delay field is 3 bits and set to 0 for 0 µsec, set to 1 for 32 µsec, set to 2 for 64 µsec, set to 3 for 128 µsec, set to 4 for 256 µsec, and the values 5 to 7 are reserved.

## Slide 6: Straw Poll 1
Do you support the text changes proposed in Slide 5 of this presentation [11-20/1743r0] for the next revision of 802.11be draft (D0.2)?