## Slide 1: Passive TB Ranging TOA Timestamp Bit Savings
Date: Nov 4, 2020
Authors:

## Slide 2: Issue with current Passive TB Ranging time-stamp reporting
For Passive TB Ranging we end up with a lot of timestamps to send due to:
ISTA cross-reporting,
ISTAs timestamp are sent twice (to and from RSTA), and
With phase shift feedback we send both TOA and PSTOA.
Also, the timestamps are broadcast at low MCS occupying many OFDM symbols.
Using 48 bits in the more numerous TOA timestamps starts to become an issue.

## Slide 3
Example Passive TB Ranging AP RSTAs and Client Anchor ISTAs Deployment
AP RSTA
Client Anchor ISTA
When an AP runs its Passive TB Ranging, all 21 ISTAs and 1 RSTA exchange NDPs.
=> 903 TOA OR 1785 TOA+PSTOA timestamps to report!!!,
Example NDP exchanges

## Slide 4: Timestamp Reporting Overheads – w PSTOA
N_ISTA | BW [MHz] | N_bits | Total preambles length [ms] | Timestamp reporting overhead [ms] | Overhead over preambles
21 | 40 | 48 | 3.1 | 3.82 | 122%
21 | 40 | 32 | 3.1 | 2.56 | 83%
21 | 40 | 24 | 3.1 | 1.96 | 63%
21 | 40 | 16 | 3.1 | 1.33 | 43%
21 | 20 | 48 | 3.1 | 7.94 | 254%
21 | 20 | 32 | 3.1 | 5.36 | 171%
21 | 20 | 24 | 3.1 | 4.07 | 130%
21 | 20 | 16 | 3.1 | 2.78 | 88%
Approximate timestamp overhead in ms and percentage of the complete Passive TB Ranging exchange.
Parameters used:
PSTOA feedback
Broadcast MCS - BPSK rate 1/2
Unicast MCS - 16QAM rate ¾
All ISTA report TOAs for the NDPs from all other ISTAs
For the percentage overhead, only the preambles and the SIFS for the frames in the sequence has been used as the base.

## Slide 5: Passive TB Ranging Timestamps
Max time we need to cover is, say, 5 ms.
However, may want to keep track of timestamps from availability window to availability window, that may be separated by, say 1s.
Solution:
  Keep 48 bits - 1ps, representation of TOD timestamps covering 218 seconds
  Use 32 bits - 16 ps, representation of more numerous TOA timestamps, covering 69 ms.
RSTA
ISTA
t2
t1
t4
t3
R2I NDP
I2R NDP
PSTA
t5
t6
Max, say. 5 ms
Max, say, 5 ms

## Slide 6: Strawpoll
How many bits in the Passive TB Ranging TOA timestamps do you support?
Option 1: 32 bits - Spanning 69 ms.
Option 2: 48 bits - Spanning 218 seconds.
Abstain

## Slide 7
Thank You!

## Slide 8: Timestamp Reporting Overheads
N_ISTA | BW [MHz] | N_bits | Total preambles length [ms] | Timestamp reporting overhead [ms] | Overhead over preambles
21 | 40 | 48 | 3.1 | 1.99 | 63%
21 | 40 | 32 | 3.1 | 1.36 | 43%
21 | 40 | 24 | 3.1 | 1.04 | 33%
21 | 40 | 16 | 3.1 | 0.73 | 23%
21 | 20 | 48 | 3.1 | 4.10 | 133%
21 | 20 | 32 | 3.1 | 2.84 | 90%
21 | 20 | 24 | 3.1 | 2.17 | 69%
21 | 20 | 16 | 3.1 | 1.51 | 48%
Approximate timestamp overhead in ms and percentage of the complete Passive TB Ranging exchange.
Parameters used:
Broadcast MCS - BPSK rate 1/2
Unicast MCS - 16QAM rate ¾
All ISTA report TOAs for the NDPs from all other ISTAs
For the percentage overhead, only the preambles and the SIFS for the frames in the sequence has been used as the base.