## Slide 1: Recommended requirements for TGbb MAC supporting LC HE PHY
Chong Han (pureLiFi)
Date: 2020-11
Authors:
November 2020

## Slide 2: Abstract
Chong Han (pureLiFi)
The presentation provides the review of recommended requirements of the LC HE MAC for TGbb.
The clauses/subclauses referred in the slides come from IEEE P802.11axD7.0.
November 2020

## Slide 3: LC HE MAC
Unchanged text from IEEE P802.11ax:
  Clause 26 (except 26.5)
Modifications:
  26.5 MU operation
    …
    26.5.2 UL MU operation——Modifications proposed on Slide
    …
    26.5.4 UL OFDMA-based random access (UORA) —— LC HE STAs set the OFDMA RA Support subfield to 0
November 2020
Chong Han (pureLiFi)

## Slide 4: UL Random Access
Disable the optional UORA (UL OFDMA-based Random Access)
  In the context of TGbb, association/reassociation is not expected to be as frequent as in IEEE P802.11ax.
  The UORA is designed to serve large amount of users, which is also not the case in TGbb.
  Channel sensing in WiFi cannot easily migrate to TGbb.
LC HE STAs set the OFDMA RA Support subfield to 0
November 2020
Chong Han (pureLiFi)

## Slide 5: UORA (UL OFDMA-based Random Access)
Chong Han (pureLiFi)
No dedicated resource allocation for all; flexibility; uncertainty
Eligible STAs with OBO counter number (<= Available RUs for AID0/2045/2046) compete for RA-RUs
Random selection of AID0(for associated STAs)/2045or2046(for unassociated STAs) RUs causes collisions
November 2020

## Slide 6: Modified UL MU operation
Multi-STA BlockAck
Backoff
AID 3,
RU 5
AID 9,
RU 4
AID 4,
RU 2
AID 4,
RU 3
AID 0,
RU 1
AID 3,
RU 6
Trigger frame
SIFS
HE TB PPDU from STA of AID 3
HE TB PPDU from STA of AID 9
HE TB PPDU from STA of AID 4
HE TB PPDU from STA of AID 4
RU 1 is reserved for Random Access
HE TB PPDU from STA of AID 3
SIFS
Reserve a Resource Unit for Random Access in UL MU operation
  STAs know where to do Random Access.
  Reduce collision probability, wasted resources, and retransmissions.
Chong Han (pureLiFi)
November 2020

## Slide 7: Conclusion
Chong Han (pureLiFi)
The document provides a guidance for the recommended requirements on MAC sub-layer running LC HE PHY.
The random access UL function UORA is disabled to reduce collisions; UL MU operation is modified to provide UL Random Access.
November 2020