## Slide 1: EHT Beamformee NDP and Partial BW Feedback Support
Date: 2020-11-06
Authors:

## Slide 2: Introduction
Partial BW feedback was introduced in 11ax as an optional feature.
One important usage is for OFDMA BF/steering:
  Beamformer to solicit partial BW CSI feedback based on pre-determined per-user partial BW resource allocation (OFDMA).
  Sounding overhead can be reduced prominently.
OFDMA use cases:
  OFDMA to mixed BW STAs: data airtime benefits.
    Achieve airtime gains even with smaller number of STAs.
    More common use cases.
  OFDMA to same BW STAs: CSMA contention/control time benefits.
Further enhance OFDMA in 11be
  Enable BF/steering for OFDMA to mixed BW STAs.

## Slide 3: OFDMA Example
Example 1: same BW OFDMA
  160MHz OFDMA to two 160MHz STAs
Example 2: mixed BW OFDMA
  160MHz OFDMA to 160MHz STA1 and 80MHz STA2 (with or without SST)
996RU to 160MHz STA1
996RU to 160MHz STA2
996*2 RU to 160MHz STA1
996*2 RU to 160MHz STA2
OFDMA
SU
996RU to STA2
996RU to STA1
996RU to 80MHz STA2
996*2 RU to 160MHz STA1
OFDMA
SU
OFDMA airtime gain

## Slide 4: OFDMA to Mixed BW STAs
OFDMA is mandatory supported by all BW STAs.
  11be defines up to 320MHz
  AP can serve mixed BW STA, 20/80/160/320MHz.
  OFDMA can find more use cases to mixed BW STAs.
To better support OFDMA beamforming:
  Define sounding to mixed BW STAs
  Mandate partial BW feedback

## Slide 5: Sounding to Mixed BW STAs
11ac/ax only defines MU sounding to same BW STAs.
  Mixed BW OFDMA: sequential sounding.
  Lose efficiency and add complexity to beamformer
    To handle MU CSI feedback from different NDPs.
  No sounding support for STAs parked on secondary channels (SST).
Proposal: 11be defines MU sounding to mixed BW STAs
  Beamformer can sound multiple STAs with operating BW equal to or smaller than NDP BW.
  Better support OFDMA BF/steering to mixed BW STAs.
  Make better use of partial BW feedback.
  Support sounding to SST STAs.

## Slide 6: Example: Sounding to mixed BW STAs
Example:
  160MHz OFDMA to 160MHz STA1 and 80MHz STA2.
11ax: sequential sounding to each STA
  Beamformer needs to sound them sequentially in different TXOP.
11be: MU sounding to mixed BW STA
  One sounding can collect all partial BW feedback.
  More efficient and easier CSI management at beamformer.
Feedback of STA1
Feedback of STA2
Feedback of STA1
160MHz NDPA
160MHz NDP
BFRP
160MHz NDPA
160MHz NDP
BFRP
80MHz NDPA
80MHz NDP
BFRP
Feedback of STA2
Sounding airtime saved

## Slide 7: Enabler for Sounding to Mixed BW STA
Beamformer: No change.
  NDPA: No change needed
    Partial BW indication already supports feedback smaller than NDP BW.
  NDP: keep current NDP design.
    Using 11be non-OFDMA MU PPDU format
  BFRP: No change needed.
Beamformee:
  Support receiving NDP of BW wider than its operating BW.
    80/160MHz operating STA: easy to support
    40MHz operating STA: no need to support
    20MHz operating STA: more changes are needed
      similar to supporting wideband OFDMA
  Support partial BW feedback

## Slide 8: Wide BW NDP Support
Operating BW | Wide BW NDP | Changes
160MHz | 320MHz | Tone plan on parked 160MHz same as 160MHz NDP. 320MHz EHT-LTF supported for OFDMA.
80MHz | 320MHz, 160Mhz | Tone plan on parked 80MHz same as 80MHz NDP. 160/320MHz EHT-LTF supported for OFDMA.
40MHz | - | No need, as wide-bandwidth OFDMA support is not defined.
20MHz | (320MHz) 160MHz, 80MHz, 40MHz | Tone plan on parked 20MHz different from 20MHz NDP. Similar to wideband OFDMA: shifted tone plan, no DC. 4 pilot tones for non-puncture 80MHz segment. Interpolating CSI feedback around DC tone, pilots, etc. Relatively more changes.

## Slide 9: Proposals for Beamformee Support
Support of NDP of BW wider than operating BW
  Mandate for STAs with operating BW>=80MHz.
  Optional for STAs with operating BW=20MHz.
    242 RU support in wide-bandwidth OFDMA is also optional.
Mandatory support of partial BW feedback
  Important for mixed BW MU sounding and OFDMA with BF.
  Mandate support for all allowed partial BW modes in NDPA.
    Differentiating feature of 11be to augment OFDMA with BF.
    Partial BW feedback granularity of RU242 [1] eases implementation.

## Slide 10: Summary
OFDMA transmission to mixed BW STAs is common use case.
To enhance OFDMA in 11be with beamforming, we propose to define sounding to STAs of mixed BW.
  Beamformer can group STAs of mixed BW in one sounding.
  Beamformee to support wider BW NDP.
  Beamformee to support partial BW feedback.

## Slide 11: SP1
Do you agree 11be to define sounding to STAs of mixed BW?
  Beamformer can group STAs of mixed BW in one NDPA and NDP with NDP BW larger or equal to the STA’s operating BW.
  Beamformee supports receiving NDP of BW wider than its operating BW.
    20MHz operating STA participating in 320MHz NDP is TBD.
    40MHz operating STA is excluded.

## Slide 12: SP2
Do you agree that the beamformee support of receiving NDP with BW wider than STA’s operating BW is
  mandatory for STAs with operating BW>=80MHz
  optional for STAs with operating BW=20MHz

## Slide 13: SP3
Do you agree to 11be beamformee mandatory support all partial BW feedback modes aligned with the large RU/MRU?

## Slide 14: Appendix
[1] Bin Tian and etc., “EHT Punctured NDP and Partial Bandwidth feedback”, 11-20/1161