## Slide 1: Low-Latency Triggered TWT
Date: 2020-12-16
Authors:

## Slide 2: Abstract
Discuss a solution to support low-latency (LL) traffics and peer-to-peer (P2P) communications based on TWT feature.
Proposal :
  Define a Low Latency Service Period (LL SP) based on TB TWT dedicated to LL traffics
  Define LL SP protection mechanisms

## Slide 3: Background
The TWT feature is a mechanism where a set of Service Periods (SPs) are defined and shared between AP and non-AP STAs to reduce medium contention and improve the power efficiency of STAs.
Broadcast TWT: AP can schedule TWT SP(s) with supporting STAs and shares schedule info in Beacon/Probe Response frames.
Doc11-20/1046: introduced protected TWT Enhancement mechanism for Latency Sensitive Traffic to:
  Extend the use of Broadcast TWT for low latency traffics
  Extend the usage of such TWT SPs for P2P communications
  Use of the quiet element
Main constraint: To ensure the accuracy of the starting date of the restricted TWT, all STAs shall stop their transmissions before the starting date of the TWT SP.
  Use of Quiet element is a first answer. Additional rules are required to provide a protection to the Low-Latency Service Period (against BSS STAs, for instance).

## Slide 4: Principles of the Low-Latency Service Period (LL SP)
TXOPAP
LL SP
Reservation by the AP of the TXOPAP Duration
Transmission not restricted to Low Latency
Transmission restricted to Low Latency
Transmission not restricted to Low Latency
Transmission not restricted to Low Latency
TXOPSTA
TXOPSTA
ProvisionPeriod
MaxProvisionTime
Time
T1
T2
T3
T0
EDCA
SIFS
SIFS

## Slide 5: Provision Period - Details
A STA that supports stopping their transmission before the starting date of the LL SP is defined as a Low-Latency (LL) Capable STA.
Medium Access Management during the provision period:
  The reservation frame may be a trigger frame (Basic or MU-RTS).
  The reservation frame may contain an information allowing EDCA mode during the provision period.
  When the AP accesses the medium during a MaxProvisionTime (TBD) before the start of the LL SP, it reserves a TXOP time that encompasses the next LL SP.
  Only LL Capable STAs are allowed to contend the medium during the provision period.
Data transmissions during the provision period:
  The AP may initiate MU/SU data transmissions (DL/UL) to solicit any STAs of the BSS.
  Data transmissions are not restricted for low-latency flows.
  Only the LL Capable STAs are allowed to use EDCA mode to transmit data not restricted for low-latency flows.
NAV Management :
  A LL Capable STA sets its NAV, at the starting date of the provision period, until the starting date of the LL SP unless the AP allows EDCA mode during the provision period.
  Non-LL Capable STAs and OBSS STAs set their NAV, at the starting date of the provision period, until the end of the TXOPap.

## Slide 6: Low-Latency Service Period (LL SP) 1/2
Define a broadcast TWT dedicated to low-latency traffics
Define a new value for the « Broadcast TWT Recommendation» field value for Low-Latency traffics in the TWT Information Element
Restrict the TWT service period to only low-latency traffic transmission.
Support Direct link (P2P) communications (see doc 813r7):
TWT IE
Broadcast TWT Recommandation | Definition
0 | No constraints
1 | PS-Poll, QoS Null, BQR, BSRs frames
2 | PS-Poll, QoS Null, BQR, BSRs frames with TF containing RA-RUs
3 | No constraints on the frames except that the AP transmits a TIM frame
4 | Low Latency
5-7 | Reserved
Slide 6

## Slide 7: Low-Latency Service Period (LL SP) (2/2)
Medium Access Management during the LL SP:
  MU transmissions may be the best solution
    Set « Trigger » field to 1 in the broadcast TWT IE.
    Use trigger frames, during the LL SP, avoids collisions and abuses among STAs participating to the broadcast TWT.
  Support of EDCA mode during the LL SP is TBD.
    Only STAs with low-latency traffics would be allowed to contend the medium during the LL SP if the AP sends no trigger frames.
    Adapted EDCA parameters could optimize the efficiency.
Data transmissions during the LL SP:
  Data transmissions are restricted for low-latency traffics.

## Slide 8: LL SP Example
AP
STA1
STA2
(LL)
STA3
(LL)
STA4
TF
TF
TB PPDU
TB PPDU
SIFS
SIFS
SIFS
TXOPAP
LL SP
MSTA BA
SIFS
TB PPDU
TB PPDU
MSTA BA
UL_Length 1
UL_Length 2
SIFS
ProvisionPeriod
T1
T2
T3
T1bis
EDCA

## Slide 9: Summary
A new triggered LL SP is defined.
This ensures:
  The cancellation of collisions among STAs acting inside the LL SPs
  The AP keeps the control of the medium during all the LL SP
  The QoS is driven by the AP.
  This guarantees a more predictive access to the medium for low-latency traffics and peer-to-peer communications.

## Slide 10
Straw Poll #1
Do you support that 11be defines in R1 a broadcast TWT Service Period for low-latency traffics ?
Results: Y/N/A

## Slide 11
Straw Poll #2
Do you support that a broadcast TWT for low-latency traffics restricts the TWT service period to only low-latency traffic transmission.
Results: Y/N/A

## Slide 12
Straw Poll #3
Do you support that the broadcast TWT for low-latency traffics :
  Is identified by adding a new value in the “Broadcast TWT Recommandation» field.
  Has the « Trigger » field set to 1 to restrict the medium access of the STAs during the broadcast TWT SP dedicated to low-latency traffics.
Results: Y/N/A

## Slide 13
Straw Poll #4
Do you support to add to the 11be SFD in R1:
  An AP supporting low-latency capability, that gains the medium during a provision period before the start time of the LL SP, should extend the TXOP limit in order to encompass the LL SP inside the TXOP.
  The maximum duration of the provision period is TBD.
Results: Y/N/A

## Slide 14: Reference
[1]. 11-20-1046: Protected TWT Enhancement for Latency Sensitive Traffic.