## Slide 1: Low-Latency Triggered TWT
Date: 2021-02-19
Authors:

## Slide 2: Abstract
Discuss a solution to support low-latency (LL) traffics based on TWT feature.
Proposal :
  Define LL SP protection mechanisms
  Define a Low Latency TWT Service Period (LL TWT SP) based on broadcast TWT dedicated to LL traffics

## Slide 3: Background
The TWT feature is a mechanism where a set of Service Periods (SPs) are defined and shared between AP and non-AP STAs to reduce medium contention and improve the power efficiency of STAs.
Broadcast TWT: AP can schedule TWT SP(s) with supporting STAs and shares schedule info in Beacon/Probe Response frames.
Doc11-20/1046: introduced protected TWT Enhancement mechanism for Latency Sensitive Traffic to:
  Extend the use of TWT feature for low latency traffics
  Extend the usage of such TWT SPs for P2P communications
  Use of the quiet element
Main constraint: To ensure the accuracy of the starting date of the restricted TWT, all STAs shall stop their transmissions before the starting date of the TWT SP.
  Use of Quiet element is a first answer. Additional rules are required to provide a protection to the Low-Latency Service Period (against BSS STAs, for instance).

## Slide 4: Principles of the Low-Latency TWT Service Period (LL TWT SP) protection
TXOPAP
LL SP
Reservation by the AP of the TXOPAP Duration
Transmission not restricted to Low Latency
Transmission restricted to Low Latency
Transmission not restricted to Low Latency
Transmission not restricted to Low Latency
TXOPSTA
TXOPSTA
ProvisionPeriod
MaxProvisionTime
Time
T1
T2
T3
T0
EDCA
SIFS
SIFS

## Slide 5: Provision Period - Details
A EHT STA that supports stopping their transmission before the starting time of the LL SP is defined as a Low-Latency (LL) Capable EHT STA.
The Provision Period serves as NAV protection, and ensures an accurate starting time (T2) for the LL TWT SP.
The Provision Period is announced in the TWT IE with the Bit 15 « TWT Protection » used for an Individual TWT.
Medium Access Management during the Provision Period:
  The reservation frame may be a trigger frame (Basic or MU-RTS).
  When the LL Capable EHT AP accesses the medium during a MaxProvisionTime (TBD) before the start of the LL SP, it reserves a TXOP time that encompasses the next LL SP.
  The reservation frame may contain an information allowing EDCA mode during the Provision Period.
  When EDCA is allowed during the provision period, only LL Capable EHT STAs are allowed to contend the medium.
Data transmissions during the Provision Period:
  The AP may initiate MU/SU data transmissions (DL/UL) to solicit any STAs of the BSS.
  Data transmissions are not restricted for low-latency flows.
NAV Management :
  LL Capable EHT STA sets their NAV, at the starting time of the Provision Period, until the starting time of the LL TWT SP unless the AP allows EDCA mode during the Provision Period.
  Non-LL Capable STAs (legacy STAs or Non-LL Capable EHT STAs ) and OBSS STAs set their NAV, at the starting time of the provision period, until the end of the TXOPap.

## Slide 6: Low-Latency TWT Service Period (LL SP) 1/2
Define a broadcast TWT dedicated to low-latency traffics
Define a new value for the « Broadcast TWT Recommendation» field value for Low-Latency traffics in the TWT Information Element
The Provision Period is announced in the TWT IE with the Bit 15 « TWT Protection » used for an Individual TWT.
Restrict the TWT service period to only low-latency traffic transmission.
TWT IE
Broadcast TWT Recommandation | Definition
0 | No constraints
1 | PS-Poll, QoS Null, BQR, BSRs frames
2 | PS-Poll, QoS Null, BQR, BSRs frames with TF containing RA-RUs
3 | No constraints on the frames except that the AP transmits a TIM frame
4 | Low Latency
5-7 | Reserved
Slide 6
TWT
Protection

## Slide 7: Low-Latency TWT Service Period (LL SP) (2/2)
Medium Access Management during the LL TWT SP:
  MU transmissions may be the best solution
    Set « Trigger » field to 1 in the TWT IE.
    Use of trigger frames, during the LL SP, avoids collisions and abuses among STAs participating to the TWT.
  Support of EDCA mode during the LL SP is TBD.
    Only STAs with low-latency traffics would be allowed to contend the medium during the LL TWT SP if the AP sends no trigger frames.
    Adapted EDCA parameters could optimize the efficiency.
Data transmissions during the LL TWT SP:
  Data transmissions are restricted for low-latency traffics.

## Slide 8: LL TWT SP Example
AP
STA1
STA2
(LL)
STA3
(LL)
STA4
TF
TF
TB PPDU
TB PPDU
SIFS
SIFS
SIFS
TXOPAP
LL SP
MSTA BA
SIFS
TB PPDU
TB PPDU
MSTA BA
UL_Length 1
UL_Length 2
SIFS
ProvisionPeriod
T1
T2
T3
T1bis
EDCA

## Slide 9: Summary
A new LL TWT SP and associated NAV-protected mechanisms are defined.
This ensures:
  The cancellation of collisions among STAs acting inside the LL SPs
  The AP keeps the control of the medium during all the LL SP
  The QoS is driven by the AP.
  This guarantees a more predictive access to the medium for low-latency traffics and peer-to-peer communications.

## Slide 10
Straw Poll #1
Do you support that 11be defines in R1 a broadcast TWT Service Period for low-latency traffics ?
Results: Y/N/A
Note: This SP has already been approved
thanks to the doc 1046 (Facebook) – Motion #148 / #150

## Slide 11
Straw Poll #2
Do you support that 11be defines in R1 that ?:
  Broadcast TWT for low-latency traffics (LL TWT) restricts the TWT service period to only low-latency traffic transmission .
  Low-latency traffic restriction is signaled by adding a new value in the “Broadcast TWT Recommandation» field.
Results: Y/N/A

## Slide 12
Straw Poll #3
Do you support that 11be defines in R1 that:
  TWT for low-latency traffics has « Trigger » field set to 1 to restrict the medium access of the STAs during the TWT SP dedicated to low-latency traffics.
Results: Y/N/A

## Slide 13
Straw Poll #4
Do you support to add to the 11be SFD in R1:
  An AP supporting low-latency capability, should ensure the NAV protection such that:
    The AP sets the “TWT Protection” bit (bit 15) to 1 for a broadcast TWT for low-latency traffics to indicate that the LL TWT SP will be NAV-protected before the start time of the LL TWT SP.
    The AP sends a reservation frame (such as a Trigger frame) to gain access to the medium a duration before the start time of the LL TWT SP (called Provision Period).
    NAV protection encompasses the LL TWT SP.
  Note: The maximum duration of the Provision Period is TBD.
Results: Y/N/A
Patrice NEZOU, (Canon), et al

## Slide 14
Straw Poll #5
Do you support to add to the 11be SFD in R1:
  Only LL capable EHT STA can contend to access the medium during a Provision Period
  Note : A Low-Latency (LL) Capable EHT STA is an EHT STA that supports stopping its transmission before the starting time of the LL SP.
Results: Y/N/A
Patrice NEZOU, (Canon), et al

## Slide 15: Reference
[1]. 11-20-1046: Protected TWT Enhancement for Latency Sensitive Traffic.