## Slide 1: Discussion on low latency traffic
Date: 2020-11-2
Authors:
Name | Affiliations | Address | Email
Boyce Bo Yang | Huawei | Nanjing, China | yangbo59@huawei.com
Chenhe Ji |  | Nanjing, China | jichenhe@huawei.com
Lily Yunping Lyu |  | Nanjing, China | lvyunping@huawei.com
Wayne Wei Qiu |  | Nanjing, China | wayne.qiuwei@huawei.com
Notes: September 2012

## Slide 2: Introduction
The group has agreed to define a restricted service period mechanism that provide more predictable latency performance for latency sensitive traffic in R1 [Motion 148, #SP345]
Moreover, TWT setup procedure is agreed as baseline to setup a restricted SP agreement [Motion 150, #SP371]
This contribution is to give a detailed discussion on low latency traffic and restricted SP setup procedure

## Slide 3: Problems need to be considered
Identifiers of low latency traffics are needed
  To differentiate low latency traffic and other traffic.
  To differentiate low latency traffic with different latency requirements
Restricted SPs would impact the efficiency of other traffics.
  EHT STAs supporting low latency feature shall end its TXOP before the start of the restricted SPs
  EHT STAs supporting low latency feature would have lower priority to transmit regular traffics during restricted SPs
  To minimize the impact, restricted SPs should not be setup when the network quality is good
The TWT setup signaling could be a big problem when there are many latency sensitive STAs and when the network is quite congested
Notes: That is to provide QoS to low latency traffics while minimizing the influence on regular traffics

## Slide 4: Discussion on low latency traffic
The QoS requirements of low latency traffic can be classified into two types:
  Latency requirements: related to the interval between two successive restricted SPs
  Throughput requirements: related to the duration of each restricted SPs
The identifier of low latency traffic could be assigned by each STA or by the spec
  Option 1: Each STA can assign a traffic identifier for a type of low latency traffic with specific QoS requirements. This traffic identifier should be used together with AID. However this option is more flexible and Less efforts are needed for the group
  Option 2: The spec can define several types of low latency traffics and assign specified traffic identifier. This traffic identifier can be used alone. Correspondingly, this option is less flexible and More efforts are needed for the group.

## Slide 5: Recall TWT Setup signaling in 11ax
AP
STA 1
STA 2
STA 3
TWT req.
TWT resp.
TWT req.
TWT resp.
TWT resp.
TWT req.
TWT SP
TWT SP
TWT SP
LL traffic arrives
LL traffic arrives
LL traffic arrives
Observations:
Too much signaling
Unnecessary TWT SP would be setup when network quality is good.
The signaling would make the channel more congested when network quality is bad.

## Slide 6: QoS Report and Broadcast Announcement
AP
STA 1
STA 2
STA 3
QoS Report
ACK
QoS Report
ACK
QoS Report
LL traffic arrives
LL traffic arrives
LL traffic arrives
ACK
Restricted SP Announcement for all STAs
TWT SP
When network quality is good and no need to setup TWT SPs, STAs would send QoS Report and the AP would know the overall QoS requirements in the BSS.
When network quality is not so good, the AP can setup one or multiple TWT SPs for all low latency STAs based on the knowledge collected previously.

## Slide 7: TWT based signaling
Change Reserved subfields in Control field to TWT Type subfield
  Value 0: QoS Report for low latency traffic
  Value 1: Restricted SP for low latency traffic
  Value 2: TBD or reserved
  Value 3 TWT SPs for legacy usages in 11ax
Change TWT Parameter Information field to TWT Parameter Information list field.
  Multiple restricted SPs can be setup by a list of TWT Parameter Information fields
  Multiple low latency STAs can be assigned to one restricted SP.
NDP Paging Indicator
Responder PM Mode
Negotiation Type
TWT Information Frame Disabled
Wake Duration Unit
Reserved
Bits:
1
1
2
1
1
2
Element ID
Length
Control
TWT Parameter Information
Octet:
1
1
1
Variable

## Slide 8: Behaviors of AP and non-AP
Behaviors of non-AP STA
  A non-AP STA that has low latency traffic may send a MMPDU containing (modified) TWT IE to AP
    The TWT IE could be a QoS Report if the network quality is good
    The TWT IE could be a restricted SP request if the network quality is not good
    Modified TSPEC IEs may be included in the MMPDU to provided detailed QoS requirements
  A low latency STA that set TWT type subfield to QoS Report would not expect TWT response from AP
Behaviors of AP
  The AP that receives a QoS Report may or may not send a response
    The AP is allowed to send unsolicited response as it is in TWT signaling
  The AP that receives a restricted SP request would send a response
  The AP can use broadcast TWT IE to set up multiple restricted SPs and assign multiple non-AP STAs to any of the restricted SPs
Notes: The AP can use broadcast TWT IE to set up multiple TWT SPs right now. we can extend it to restricted SPs.
Need to allow AP assigning multiple STAs to one restricted SP by one MMPDU.

## Slide 9: Summary
We give a discussion on how to identify low latency traffics in 11be.
We propose a QoS Report mode in TWT SP signaling which is can reduce overhead and avoid unnecessary restricted SPs
  .

## Slide 10: Straw Poll 1
Do you agree to add a QoS report mode in restricted SP setup procedure.
Y/N/A

## Slide 11: Straw Poll 2
Do you agree that an EHT scheduling AP is allowed to setup multiple restricted SPs and assign multiple scheduled STAs to one or multiple restricted SPs in the broadcast signaling.
Y/N/A

## Slide 12: References
[1] 11-20-1355-05-00be-access-mechanisms-to-meet-the-requirements-of-low-latency-traffics
[2] 11-20-1046-08-00be-prioritized-edca-channel-access-slot-management
[3] 11-20-1350-00-00be-enhancements-for-qos-and-low-latency-in-802-11be-r1
[4] 11-18-2009-06-0rta-rta-report-draft

## Slide 13: Backup

## Slide 14: Example design of TWT IE
AID
Traffic identifier
AID
Traffic identifier
Last Broadcast Parameter Set
TWT Request
TWT Setup Command
Trigger
Flow Type
Reserved
Broadcast TWT Recommendation
TWT Wake Interval Exponent
Broadcast TWT Info
Request
Type
Target Wake Time
Nominal Minimum TWT Wake Duration
TWT Wake Interval Mantissa
Bits:
1
1
1
1
3
5
3
1
Octet:
2
2
1
2
2
Existing Broadcast TWT IE can setup multiple TWT SPs with one IE:
  The Last Broadcast Parameter Set subfield of Broadcast TWT Parameter Set fields at front is set to 0.
  The Last Broadcast Parameter Set subfield of the last Broadcast TWT Parameter Set field is set to 1.
Multiple AID subfields and traffic identifier subfields can be added in Broadcast TWT Info subfields to assign multiple low latency STAs to one restricted SP.
  AID subfields are used to identify STAs
  One STA may have different low latency traffics with different latency requirements, so a traffic identifier is needed.
  The traffic identifier can also avoid abuse of restricted SPs by non-AP STAs
Broadcast TWT Parameter Set field
Reserved
Broadcast TWT ID
Broadcast TWT Persistence
….