## Slide 1: Complete BSS Update Report Indication
Date: 2020-11-05
Authors:
Name | Affiliations | Address | Phone | Email
Pooya Monajemi | Cisco |  |  | pmonajem@cisco.com
Brian Hart |  |  |  | brianh@cisco.com
Notes: September 2012

## Slide 2: Background
Out of link BSS parameter updates
  Addressed by multiple contributions so far
  An AP of an AP MLD transmits a Change Sequence Number for each of the other APs belonging to the same AP MLD
  CSN updated to notify the client device that another link of the MLD has had updates in critical BSS parameters
  Once notified of a update, STA may obtain the out-of-link updates from multiple sources
    On-link beacons
    Out-of-link beacons
    Probe requests

## Slide 3: Probe Storm Problem
Problem : Probe Storms
  An indication of update in one link may cause many clients to send probe requests to obtain the updated parameters at the same time
  Storm of probes can be very disruptive to medium
AP 1
Beacons
AP 2
Beacons
Parameter Update
AP1 CSN
Probe Req/Resp
MLD Probe Req/Resp
AP1 CSN-1

## Slide 4: Complete Update Transmission
Probe Storm Prevention vs. Beacon Bloat
  A simple solution is to include the updated parameters in the out-of-link beacons
    Devices then do not need to probe to obtain new parameters
  If always included, this may cause undesirable beacon bloat
AP 1
Beacons
AP 2
Beacons
Parameter Update
AP 1 CSN, All AP1 Updates Included
AP1 CSN-1

## Slide 5: Indication of Complete Updates
Proposal:
  An AP may decide to include all updated parameters from another AP of the same AP MLD in a beacon (in ML element)
    This includes all updates since “CSN-1”
  When all parameters are included, a flag is set in the beacon to indicate that all out-of-link updates are included in the current beacon
    Hence the client device that has all updates until CSN-1 only needs to decode the current beacon to obtain all updated parameters up to CSN, and needs not send probe requests
  It is up to the AP to decide when and for how long to include all out-of-link updates
    AP may include complete update information for a few beacon periods so that most clients in doze state receive the updates and don’t probe
AP 1
Beacons
AP 2
Beacons
Parameter Update
AP 1 CSN, All AP1 Updates Included, Flag set
AP 1 CSN, AP1 Updates omitted, Flag not set
(non-AP STA obtains updates by other means)
AP1 CSN-1

## Slide 6: Extending Beyond 1 CSN
Bits assigned to the indication flag
  If one is assigned, the AP can only signal complete updates since CSN-1
  We may choose to assign more bits, in which case AP can include all parameter updates since CSN-(2^N -1)
AP 1
Beacons
AP 2
Beacons
Parameter Update
CSN+1, All AP1 Updates Included,
Flag set to 1
CSN+2, All AP1 Updates Included since CSN,
Flag set to 2

## Slide 7: Conclusions
A simple method to include all out-of-link updates in beacon is proposed
  AP may decide to report all out-of-link BSS parameter updates in a beacon frame
  A flag is proposed to indicate that all updates are included in the beacon and client should not send probe requests to obtain these updates

## Slide 8: SP1
Do you agree to :
  define a mechanism for an AP of an AP MLD to indicate in a beacon that all updated critical BSS parameters of another AP of the same AP MLD have been included in the beacon?
  A non-AP MLD that receives a beacon with the above indication and that has all critical BSS parameters corresponding to the CSN preceding that indicated by the AP should not send probe requests to obtain the updated parameters.

## Slide 9: SP2
How many bits do you prefer to assign to the complete BSS Update Report Indication flag?
  Option 1 : 1 (one update)
  Option 2 : 2 (up to 3 updates)
  Option 3 : More

## Slide 10: References
[1] 11be SFD
[2] 11-20/0586r7 MLO Indication of Critical Updates