## Slide 1: BSS Parameter Critical Update Follow Up
Date: 2020-11-01
Authors:

## Slide 2: Background
We agree that an AP within an AP MLD shall include in the Beacon and Probe Response frames it transmits a Change Sequence field for each of all APs in the same AP MLD.
  The Change Sequence field for each of other APs of the MLD shall be carried in the MLD Parameters subfield in the TBTT Information field of the Reduced Neighbor Report element corresponding to that AP.
  The Change Sequence field for the AP shall be carried in the TBD field.
  At the non-AP MLD side，it shall
  maintain a record of the most recently received Change Sequence field value for each AP in the AP MLD with which it has multi-link setup.
  In this contribution, we address the two TBD issues for critical update
  The size of Change sequence is TBD
  The schemes for retrieving the critical update at non-AP MLD side are TBD

## Slide 3: TBD Issue 1
The Check Beacon field has one octet and it has the same baseline (Critical Update events) as Change Sequence field in EHT
Moreover, Change Sequence field in 802.11ah is also one octet, and it is carried in SIG Beacon frame which is required to be short, but it has different baseline as Change Sequence field in EHT
  It have fewer Critical Update events than Check Beacon field
Given the above facts and the more critical update events which will be added for EHT, like EHT Operation Element, we propose Change Sequence field in EHT is one octet, otherwise, the space is easily run out

## Slide 4: TBD Issue 2
In the sub-clause 11.2.3.15 (TIM Broadcast ) of 802.11REVmd D5.0，it says
  The non-AP STA shall attempt to receive the next Beacon frame when it receives a Check Beacon field that contains a value that is different from the previously received Check Beacon field.
It does not mention any Probe mechanism for non-AP STA to retrieve the new BSS parameters in this case
As mentioned in reference [1], there will exist probe storm problem if there is an indication of update in one link
  It will cause many clients to send probe requests to obtain the updated parameters at the same time
  Broadcast Probe Response can not address the above issue
  It can not the block the simultaneous EDCA channel access from many clients
  It is not immediate response to Probe Request frame
Hence, Probe mechanism is not recommended in this case

## Slide 5: TBD Issue 2
Now we have two typical types for MLD, one is single radio MLD, and the other multi-radio MLD
For multi-radio MLD, it shall support to receive the next Beacon frame when it receives a Change Sequence field that contains a value that is different from the previously received Change Sequence field.
  Wake up the corresponding STA at TBTT to receive the Beacon frame
  No frequently switch issue
  Do not need to support Probe mechanism
AP 1
AP 2
Link 1
STA1
AP1
STA2
AP2
Link 2
Beacon
AP 3
Beacon
STA 3
AP3
Link 3
STA 1
STA 2
STA 3
Doze state
Awake state
Beacon
CSN1=1， CSN2=3, CSN3=1
CSN1=1, CSN2=1, CSN3=1 at the STA side

## Slide 6: TBD Issue 2
For single-radio MLD, it has frequently switch issue if it needs to retrieve critical update from the corresponding Beacon frame.
We propose it may either send a Probe Request frame or receive the corresponding Beacon frame such that to retrieve the critical update
  Probe Request (if any) shall be sent on the on-going link (link 1 in the following fig.)
  Both of these two schemes have some issue
  Disallow the Probe Request frame sent on another link (Link 2 in the following Fig) since it can receive the corresponding Beacon frame in this case
AP 1
AP 2
Link 1
STA1
AP1
STA2
AP2
Link 2
Beacon
AP 3
Beacon
STA 3
AP3
Link 3
STA 1
Doze state
Awake state
Beacon
CSN1=1， CSN2=3, CSN3=1
CSN1=1, CSN2=1, CSN3=1 at the STA side
STA 1

## Slide 7: Summary
In this contribution, we propose
  Change Sequence field in EHT is one octet
  For multi-radio MLD, it shall support to receive the Beacon frame such that to retrieve the update info
  For single-radio MLD, it may either send a Probe Request frame on the on-going link or receive the corresponding beacon frame such that to retrieve the critical update

## Slide 8: References
[1] 11-20-1862-00-00be-complete-bss-update-report-indication