## Slide 1: MU-MIMO over MCS15
Date: 2020-11-18
Authors:
Name | Affiliations | Address | Phone | email
Ron Porat | Broadcom |  |  | ron.porat@broadcom.com

## Slide 2: Discussion
DL MU-MIMO typically provides gain at medium to high SNR (at very low SNR channel feedback is less accurate and the benefit of increased spatial multiplexing is outweighed by the power reduction due to power split between the STA).
Similarly UL MU-MIMO at very low SNR will suffer compared to UL OFDMA (reduced inter user interference and sensitivity to impairments)
MCS15 can operate at negative SNR and is therefore best used for single user transmissions
 Propose to disallow DL and UL MU-MIMO over MCS15

## Slide 3: SP #1
Do you agree to disallow DL and UL MU-MIMO over MCS15?