## Slide 1: Ranging PHY Security
Date: Jan 6, 2021
Authors:

## Slide 2
Feedback Protected PHY Security

## Slide 3: Detection of PHY attacks
We have repetition of LTFs to enable attack on encrypted LTFs.
  Relies on the peer modem to detect the attack
Consider channel metric feedback to detect PHY attacks
  Utilize reciprocity of channel
  Feed back a metric of the channel estimate
    Whole channel estimate, or e.g.
    Average delay in the channel, i.e. the PS-TOA
  Enables the originating modem to detect the attack

## Slide 4: Attack Scenario
Unlikely that the channels are the same

## Slide 5: PS-TOA Feedback PHY Attack Detection
RSTA
ISTA
Measure t2 and tp2
Measure t4 and tp4
Feedback t2 and tp2
Feedback t4 and tp4
Compare tp2-t2 with tp4-t4!
I2R NDP
R2I NDP
Compare tp2-t2 with tp4-t4!
Forces attacker to attack both links or shift the entire channel estimate.
Probably hard to do without triggering detection of the attack!
Can be combined with LTF encryption!

## Slide 6
Combination with LTF encryption

## Slide 7: PHY attacks when the LTFs are encrypted
When the LTFs are encrypted, attacks may not be possible with perfect LTF replica
  Possibly only some of the tones are estimated correctly
  The attack may only be partial in the time domain
Causes unintended distortions of the channel raising the probability of detection

## Slide 8
Proposed draft changes

## Slide 9: Proposed draft changes
Add optional fields in LMR frame to feedback TOA and PSTOA at the same time.
Add mechanism to negotiate TOA+PSTOA feedback.
Possibly mandate TOA+PSTOA feedback when secure LTFs are negotiated.

## Slide 10: Addition of PSTOA field in LMR frame
Category
CFO Parameter
Octets
Public Action
Octets
Dialog Token
TOD
TOA
TOD Error
TOA Error
R2I NDP Tx Power
I2R NDP Target RSSI
AOA Feedback
(Optional)
Secure LTF Parameters
(Optional)
PSTOA
(Optional)
PSTOA Error
(Optional)
1
1
6
6
6
1
1
2
1
1
13
9
6
1
Add PS-TOA feedback in PHY secure mode as additional protection against attacks!
LMR frame:

## Slide 11: Negotiation of TOA+_PSTOA Feedback
The ISTA can signal both R2I TOA Type and I2R TOA Type = 1, and the RSTA can respond with both fields also set to 1.
This trigger PSTOA feedback type in both directions (assuming R2I LMR is negotiated).
Propose to in this corner case we can require that both PSTOA and TOA is fed back.
Thus, we have a way to negotiate combined PSTOA and TOA feedback without having to add a bit.
Or we can add a byte to the Ranging Parameters Field.
Or we can use a reserved bit in the Non-TB specific subelement.

## Slide 12: Mandate TOA+PSTOA Feedback
Do we want to mandate TOA+PSTOA Feedback when secure LTFs are used?

## Slide 13: Straw Poll 1
Do you support adding mechanism to negotiate and feed back both TOA and PSTOA?
Y/N/A:

## Slide 14: Straw Poll 2
Which do you prefer?
Opt 1: Using R2I TOA Type and I2R TOA Type = 1 to signal feeding back both TOA and PSTOA
Opt 2: Adding a byte to the Ranging Parameters field and using a bit there for negotiation of feeding back both TOA and PSTOA
Opt 3: Neither
Opt 4: Abstain

## Slide 15: Straw Poll 3
Do you support mandating feeding back both TOA and PSTOA when secure LTFs are used?
Y/N/A:

## Slide 16
Thank You!