## Slide 1: Receiver specifications for the optical PHY
Date: 2020-12-14
Authors:

## Slide 2: Abstract
This presentation discusses an approach for the specification of the optical receiver for TGbb.

## Slide 3: Introduction
The 802.11bb specification needs to consider performance requirements for the optical transmitter and receiver
  Transmitter
    Transmit power
    Transmitter spectral mask
    Spectral flatness
    Transmit centre frequency and symbol clock frequency tolerance
    Modulation accuracy
  Receiver
    Receiver minimum input sensitivity
    Adjacent/non-adjacent channel rejection
    Receiver maximum input level

## Slide 4: Optical receiver
This presentation considers approaches for the receiver specifications

## Slide 5: A note on optical power
Because of the (more-or-less) linear relationship between current and optical power for photonic components like LEDs and photo diodes, ratios of optical powers are expressed using 20log(P1/P2) instead of the usual 10log(P1/P2) for RF power
This has some implications
  Receive signal strength (i.e., voltage) in free space falls off according to 1/r4 instead of 1/r2
  “Goldilocks zone” between minimum and maximum signal strength is reduced
  Range of powers for different MCS settings also reduced

## Slide 6: Optical receiver specifications - basics
Reference point is surface of photodiode assembly
  No equivalent of antenna port (like 50 Ω reference point impedance)
Assembly may include lens, filters and other optical components
Field of view is application-dependent and out-of-scope of specification
  Some example scenarios are shown later

## Slide 7: Receiver minimum input sensitivity
Figures in mW/m2
  RMS of AC component of modulation
  Measured/calculated for one or two values and scaled for others
    Example numbers shown in the table
  May be tested at any angle of the DUT’s field of view
Figures targeted at STA
  Low-power
  Small
  Cheap
AP should comfortably exceed these values
  More power
  No size restrictions
  Better optics
Modulation | Minimum sensitivity for Mandatory PHY (mW/m2)
BPSK 1/2 | 350
BPSK 3/4 | 500
QPSK 1/2 | 700
QPSK 3/4 | 1000
16-QAM 1/2 | 1400
16-QAM 3/4 | 2000
64-QAM 2/3 | 2800
64-QAM 3/4 | 4000

## Slide 8: Receiver sensitivity: example scenarios
OFE
AP
OFE
STA
OFE
AP
OFE
STA
OFE
STA
OFE
AP
PC, phone, USB dongle, etc.
Access point in office scenario
Aligned along central axis
Aligned along axis with angled beam
Offset from central axis
Access point in factory/warehouse scenario
High power, no size restrictions, better optics
Mounted at height, beam-forming optics
Aligned along central axis
Low power, small, cheap
Focused beam

## Slide 9: Receiver maximum input level
Need to allow for DC offset and ambient (IR) light
  i.e, not the same as RF Receiver maximum input level
  DC offset is always there, always larger than the AC component
  Ambient light is a product of the environment, difficult to quantify
    Maybe assume worst case of room well-lit by sunlight – large IR component
Aim is to have a level that does not drive OFE into clipping
  In operation, the DC component should have negligible effect on OFE linearity
Only ambient light longer than 800 nm to be considered
  Shorter wavelengths can be filtered, if necessary
Value in W/m2 TBD
  Should apply at all angles of the DUT’s field of view
  Test at peak of field of view?

## Slide 10: Adjacent/non-adjacent channel rejection
Relevant when considering channels on different carrier frequencies
Scale from 11a/11ax specifications?
Or leave for later?
  Not relevant in first generation?

## Slide 11: Thank you!