## Slide 1: Versioning for PHY Security
Date: 2021-01-05
Authors:
Name | Affiliations | Phone | Email
Roy Want | Google Inc. |  | roywant@google.com
Mingguang Xu | Google Inc. |  | mingguangxu@google.com
Raymond Hayes | Google Inc. |  | hayesr@google.cm

## Slide 2
Outline
Background
Problem Statement
Versioning of PHY Security
Summary
Strawpoll
Abstract
The Secure LTF protocol is a potential target for a future as yet unknown attack, and may need to be upgraded if one comes to light.
By planning for this possibility with a Secure LTF version mechanism, we can smoothly upgrade the protocol, make the right decisions in the field, and provide users with feedback about the security options they have; whether to proceed with caution, or not.

## Slide 3: Background
We have been discussing 11az PHY Security options from 2016-2020, and there is still no unanimous consensus on the best approach for a Secure LTF protocol, (although we are close to an agreement on how to proceed).
  Randomized 8PSK[6], 64QAM[2], 64QAM + 4PSK [5], 1024QAM[1,3], DFT Pre-coded OFDM [4]
Attacker methods include using a Viterbi decoder, Sphere decoder in the frequency domain, MMSE sample-by-sample in the time domain.
Attacks don’t need to be perfect, and can take advantage of probabilistic weaknesses in the coding and modulation, and then after several attempts may succeed.

## Slide 4: Problem Statement
After the 11az standard is productized, it’s possible we may find other attacks that need to be addressed with a new, or improved, variant of the Secure PHY protocol (it would become a priority).
As a result, there may be new and old variants of the protocol in the field.
For PHY Security versions, especially for key/lock applications, we would need a coexistence mechanism:
  Negotiation for the highest level of security solution.
  Provide user feedback about why a PHY security negotiation does not proceed OR if the user chooses, let them know the risks of continuing.

## Slide 5: Current Boolean PHY Security Negotiation
The Secure LTF Required field is 1-bit, and Secure LTF Support is 1-bit.
Versioning would require a few additional bits
This field is in the FTMR/IFTM request/response

## Slide 6: Option: Status Indication & Value Field
Value field supports 32 values (5-bits) and is largely unused (reserved in FTMR)
Proposal:
For 1) ISTAs FTMR and
2) RSTA’s IFTM Status Indication set to 1 or 2
The Value field would indicate the version number from 0-31 (only a few needed)
Old Value Field | New Value Field
Reserved | Reserved
Reserved | Version of Secure LTF supported
Reserved | Version of Secure LTF supported
Time in Seconds for retry | Time in Seconds before retry

## Slide 7: Proposed Versioned PHY Security Negotiation
Use for Secure LTF version in FTMR and
IFTM status 1, 2
For simplicity, leaving “Secure LTF Support” as is, qualified by the version.

## Slide 8: How a Secure LTF version would be used.
ISTA negotiates using Secure LTF required, with version X supported in FTMR
RSTA responds with Secure LTF version Y supported in IFTM
  If (X == Y) { Ranging Protocol with Secure LTF continues }
  If (X < Y) { If (ISTA only supports rev X which is older than Y)
  {RSTA rejects assignment and indicates minimum required Secure LTF Rev Y;
  User Feedback – ISTA Does not meet Secure LTF requirements} OR {RSTA proceeds with ranging}
  If (X > Y) { If (RSTA only supports rev Y which is older than rev X)
  {ISTA Terminates, User feedback – RSTA does not meet Secure LTF requirements. } OR
  {ISTA decides to accept lower Secure LTF requirement with Y (with user in loop) and proceeds}
ISTA
RSTA

## Slide 9: Summary
PROs
  Secure LTF versioning allows for devices to negotiate the Secure LTF protocol used
  Versioning enables user feedback describing the security problem.
    - It can indicate a phone upgrade is required; from a Marketing perspective this is a good thing.
  It provides an upgrade path for 11az PHY Security
    (This is not unusual given the history of Wi-Fi WEP, WPA, WPA2, WPA3 and Bluetooth security)
CONs
  Secure LTF version bits may indicate to the market TGaz is unsure about the PHY security solution.
    COUNTER POINT: We have lots of public documents that already indicate this uncertainty. However, it also shows we are committed to maintain the highest-level of security possible.

## Slide 10: References
[1] 802.11-20/0836r0 11az Secure LTF Design
[2] 802.11-20/0964r0 Attacks to Fully Random 64QAM Sounding Signal
[3] 802.11-20/1373r0 Attacks to Fully Random OFDM Sounding Signal
[4] 802.11-20/1097r1 Secure LTF using DFT Precoded OFDM
[5] 802.11-20/1855r0 Further updates on 11az Secure LTF design
[6] TGaz Draft D2.6 (members area)

## Slide 11: Strawpoll
We support developing amendment text to enable Secure LTF versioning in the FTM Request negotiation.
(Y/N/A: / / )