## Slide 1: Clarification on BSS parameter update
Date: 2021-01-05
Authors:
Name | Affiliations | Address | Email
Jeongki Kim | LG Electronics | LG Seocho R&D Campus, Korea | jeongki.kim@lge.com
Namyeong Kim | LG Electronics |  | namyeong.kim@lge.com
Sunhee Baek | LG Electronics |  | sunhee.baek@lge.com
Insun Jang | LG Electronics |  | insun.jang@lge.com
Jinsoo Choi | LG Electronics |  | js.choi@lge.com

## Slide 2: Introduction (1/3)
BSS parameter update procedure in TGbe D0.2
  An AP within an AP MLD shall include in the Beacon and Probe Response frames it transmits a Change Sequence field for each of all APs in the same AP MLD.
    The Change Sequence field for each of other APs of the MLD shall be carried in the MLD Parameters subfield in the TBTT Information field of the Reduced Neighbor Report element corresponding to that AP.
  An AP within an AP MLD shall increase the value of the Change Sequence field for another AP in the same AP MLD when a critical update occurs to any of the elements for that AP.
  An AP within an AP MLD shall provide in the Critical Update Flag subfield of the Capability Information field of the Beacon and Probe Response frames it transmits an indication of an update to the value carried in the Change Sequence subfield of the MLD Parameters field in the Reduced Neighbor Report element for any AP in the same AP MLD. An AP shall provide this indication in the Beacon frame(s) until (and including) the next DTIM Beacon frame on the link that the AP is operating on.
  A non-AP STA within a non-AP MLD may decode the Critical Update Flag subfield in the Capability Information field.

## Slide 3: Introduction (2/3)
And, we need to describe the operation of non-AP MLD that can decode the critical update flag in the spec for clear implementation
  If the critical update flag is set to 0, Non-AP MLD that can decode the critical update flag can skip to parse the change sequence subfield of other APs in the RNR. Otherwise, the MLD will check the change sequence subfield of other APs in the RNR
According to the baseline spec,
  the STA will try to receive the beacon frames every Listen Interval to check if its AP has buffered BUs for the MLD
  When ReceiveDTIMs is false, STA is not required to awaken for every DTIM Beacon frame
When the critical update for other AP(s) happens (i.e., the critical update flag = 1), if the non-AP MLD that can decode the critical update flag is not required to awaken for every DTIM Beacon frame (i.e., ReceiveDTIMs =false), the MLD may miss the Beacon/DTIM Beacon frames containing the critical update flag set to 1 so that the MLD cannot check the critical update of other APs in RNR

## Slide 4: Introduction (3/3)
Example
DTIM
Beacon
CUF=0, RNR (AP2 CSN= 40)
Beacon
CUF=0, RNR (AP2 CSN= 40)
Beacon
CUF=1, RNR (AP2 CSN= 41)
Beacon
CUF=1, RNR (AP2 CSN= 41)
DTIM
Beacon
CUF=1, RNR (AP2 CSN= 41)
Beacon
CUF=0, RNR (AP2 CSN= 41)
DTIM
Beacon
CUF=0, RNR (AP1 CSN= 30)
Beacon
CUF=0, RNR (AP1 CSN= 30)
Beacon
CUF=1, RNR (AP1 CSN= 31)
DTIM
Beacon
CUF=1, RNR (AP1 CSN= 31)
Beacon
CUF=0, RNR (AP1 CSN= 31)
Beacon
CUF=0, RNR (AP1 CSN= 31)
Critical update of AP2
AP1 of
AP MLD
AP2 of
AP MLD
Critical update of AP1
STA2 of
STA MLD
LI = 5 BIs
CUF: Critical Update Flag
CSN: Change sequence number
LI: Listen Interval
BI: Beacon Interval
When the STA2 wakes up to receive Beacon, the STA cannot check the updated CSNs of other APs
Listen Interval
STA2 skips to read RNR because of CUF=0
STA2 skips to read RNR because of CUF=0

## Slide 5: Proposal (1/2)
Option 1: 2 or 3 bits Critical update flag
  The value of critical update flag increases by one whenever any update of the change sequence number subfields of other APs happens
  If the stored critical update flag value is different from the received critical update flag in the Beacon, the STA will parse the RNR and check which AP’s critical update happens
DTIM
Beacon
CUF=1, RNR (AP1 CSN= 30)
Beacon
CUF=1, RNR (AP1 CSN= 30)
Beacon
CUF=2, RNR (AP1 CSN= 31)
DTIM
Beacon
CUF=2, RNR (AP1 CSN= 31)
Beacon
CUF=2, RNR (AP1 CSN= 31)
Beacon
CUF=2, RNR (AP1 CSN= 31)
AP2 of
AP MLD
Critical update of AP1
STA2 of
STA MLD
LI = 5 BIs
Listen Interval
STA2 skips to read RNR because of CUF=1
STA2 tries to read RNR because of CUF=2
Stored CUF=1,
AP1 CSN=30
Stored CUF=2, AP1 CSN=30
CUF: Critical Update Flag
CSN: Change sequence number
LI: Listen Interval
BI: Beacon Interval

## Slide 6: Proposal (2/3)
Option 2: Receiving all DTIMs always
  The STAs that can decode the critical update flag should awaken to receive all DTIM Beacon frames (although they doesn’t want it)
DTIM
Beacon
CUF=0, RNR (AP1 CSN= 30)
Beacon
CUF=0, RNR (AP1 CSN= 30)
Beacon
CUF=1, RNR (AP1 CSN= 31)
DTIM
Beacon
CUF=1, RNR (AP1 CSN= 31)
Beacon
CUF=0, RNR (AP1 CSN= 31)
Beacon
CUF=0, RNR (AP1 CSN= 31)
AP2 of
AP MLD
Critical update of AP1
STA2 of
STA MLD
LI = 5 BIs
Listen Interval
STA2 skips to read RNR because of CUF=0
STA2 skips to read RNR because of CUF=0
STA2 reads RNR because of CUF=1
AP1 CSN=30
AP1 CSN=31
AP1 CSN=31
CUF: Critical Update Flag
CSN: Change sequence number
LI: Listen Interval
BI: Beacon Interval

## Slide 7: Proposal (3/3)
Option 3: Always checking the RNR
  A STA that is not required to awaken for every DTIM Beacon frame and is able to decode the critical update flag should always check the RNR element regardless of the value of critical update flag
DTIM
Beacon
CUF=0, RNR (AP1 CSN= 30)
Beacon
CUF=0, RNR (AP1 CSN= 30)
Beacon
CUF=1, RNR (AP1 CSN= 31)
DTIM
Beacon
CUF=1, RNR (AP1 CSN= 31)
Beacon
CUF=0, RNR (AP1 CSN= 31)
Beacon
CUF=0, RNR (AP1 CSN= 31)
AP2 of
AP MLD
Critical update of AP1
STA2 of
STA MLD
LI = 5 BIs
Listen Interval
STA2 reads RNR although CUF is 0
STA2 reads RNR although CUF is 0
AP1 CSN=30
AP1 CSN=31
CUF: Critical Update Flag
CSN: Change sequence number
LI: Listen Interval
BI: Beacon Interval

## Slide 8: Comparisons
Option1 (2 or 3 bits flag) | Option 2 (Always receive all DTIMs) | Option 3 (Always check RNR)
- Need more than 1 bit for signaling the flag field - Need to store updated flag value | No need further bits for signaling STA that doesn’t want to see every DTIM need to check all DTIM so that the power consumption will be increased | - No need further bits for signaling - STA that doesn’t want to see every DTIM need to check RNR always so that the STA requires parsing process of RNR

## Slide 9: Conclusion
For clarification, we need to describe the expected operation of the non-AP MLD when the MLD can decode the critical update flag
  If the critical update flag is set to 0, Non-AP MLD that can decode the critical update flag can skip to parse the change sequence subfield of other APs in the RNR. Otherwise, the MLD will check the change sequence subfield of other APs in the RNR
Providing some methods to solve problem that the STA MLD does not update the critical update of other AP when the STA MLD is not required to receive every DTIM Beacon frame
  Option 1: 2 or 3 bits critical update flag
  Option 2: The STA should always receive all DTIMs
  Option 3: The STA should always check RNR

## Slide 10: Straw Poll 1
Do you agree to add the following text in Tgbe SFD as R1 feature?
  If the critical update flag is set to 0, Non-AP MLD that can decode the critical update flag can skip to parse the change sequence subfield of other APs in the RNR. Otherwise, the non-AP MLD should check the change sequence subfield of other APs in the RNR

## Slide 11: Straw Poll 2
Which option do you prefer as a method to solve the problem indicated in slide 3 and 4 (Non-AP MLD that is not required to awaken for every DTIM Beacon frame can miss the critical update of other APs) ?
  Option 1: 2 or 3 bits critical update flag
  Option 2: The STA should always receive all DTIMs
  Option 3: The STA should always check RNR