## Slide 1: Procedure of Modified MU-RTS
Date: 2021-01-25
Authors:
Name | Affiliations | Address | Phone | Email
Yunbo Li | Huawei | Shenzhen, China |  | liyunbo@Huawei.com
Yuchen Guo |  |  |  | 
Ming Gan |  |  |  | 
Guogang Huang |  |  |  | 
Yiqing Li |  |  |  | 
Rob Sun |  |  |  | 
Zhenguo Du |  |  |  | 
Notes: September 2012

## Slide 2: Background
A modified MU-RTS will be used by AP for allocating time to a target STA to do SU PPDU transmission.
  In R1, 802.11be shall define a mechanism for an AP to transmit a modified MU-RTS Trigger frame that allocates time within a TXOP for transmitting one or more non-TB PPDUs.
  The time allocation starts after the end of transmission of the MU-RTS frame.
  It is TBD whether the AP can optionally not solicit CTS.
  This is an optional mechanism for non-AP and AP STAs.
  NOTE – The non-TB PPDUs may be transmitted by the non-AP STA to AP or to a peer of a peer-to-peer link.
  [Motion 146, #SP354, [30] and [158]]
How to get back the TXOP from the target STA will be discussed in this presentation.

## Slide 3: Procedure after Modified MU-RTS
The basic procedures after Modified MU-RTS are showed in below.
Modified MU-RTS
CTS
…
SU PPDU
TXOP
BA
…
…
PPDU
SU time period
AP
STA1
Modified MU-RTS
CTS
…
SU PPDU
TXOP
BA
…
…
PPDU
SU time period
AP
STA1
STA2
UL SU case
P2P case

## Slide 4: Problem statement
If there is remaining time in allocated SU time period after the target STA finished the transmission of buffered data, a mechanism is needed to return the control to AP. Otherwise,
  It is a waist for the system, no one can use it;
  The third party STA may contend the channel within this period
There are some minor differences between the procedures under UL SU and P2P cases, will showed in the following slides.
Modified MU-RTS
CTS
…
SU PPDU
TXOP
BA
PPDU
SU time period
AP
STA1
Last buffered data
Remain time T

## Slide 5: TXOP Return in SU Time Period
A-control subfield is a good choice to return TXOP back to AP
  It can be carried in QoS Data frame, so doesn’t need a separate frame. Overhead is low.
For UL SU case, this A-control can be carried in the last QoS data frame that transmit to AP;
Modified MU-RTS
CTS
…
SU PPDU
TXOP
BA
PPDU
SU time period
AP
STA1
UL SU case
Return TXOP to AP

## Slide 6: TXOP Return in SU Time Period
For P2P case, after the last data frame is transmitted by STA1, STA1 needs to transmit a separate QoS Null frame to return the TXOP to AP.
Modified MU-RTS
CTS
…
SU PPDU
TXOP
BA
PPDU
SU time period
AP
STA1
STA2
P2P case
Last buffered data
QoS Null frame to AP
Return TXOP to AP

## Slide 7: TXOP Return in SU Time Period
If the remaining time is not enough to transmit a QoS Null frame. How to return the TXOP to AP?
  May happens in P2P case, or UL SU case that last transmit frame is not a QoS Data frame
Opt 1: allow the QoS Null frame cross the boundary of SU time period
Opt 2: set a time threshold T. If AP correctly receives a frame which is a response frame that target to STA1, and remaining time between the ending time of response frame and the ending boundary of SU time period is less than T, then AP can directly take the control SIFS time after this response frame.
  The value of T can be defined in the spec, which should less than the transmit duration of QoS Null frame
Modified MU-RTS
CTS
…
SU PPDU
TXOP
BA
SU time period
AP
STA1
STA2
P2P case
Last buffered data
QoS Null frame to AP
Return TXOP to AP
Remain time < T

## Slide 8: TXOP Return in SU Time Period
In Opt 2, if the STA2 is hidden from AP in P2P case, BA can not be received by AP, then AP can not take the control SIFS time after BA;
  If P2P communication only allows between STAs that associated with the AP, no hidden node issue will occur
Under the hidden node scenario, the AP will take the control after the SU time period finished.
Modified MU-RTS
CTS
…
SU PPDU
TXOP
BA
SU time period
AP
STA1
STA2
P2P case, STA2 hidden from AP
Last buffered data
AP takes the control
Remain time < T
PPDU

## Slide 9: TXOP Return in SU Time Period
Opt 2 also can used in UL SU case, when the last frame transmit from STA1 to AP is not a QoS Null frame
Modified MU-RTS
CTS
…
SU PPDU
TXOP
BA
PPDU
SU time period
AP
STA1
UL SU case
Not a QoS Data frame, can not return TXOP to AP
Remain time < T
…
…

## Slide 10: Comparison Between Two Opts
Opt 1: allow QoS Null frame cross the ending boundary of the SU time period
  Pro: simple
  Con: less efficiency when the remaining time is short
Opt 2: set a time threshold T that allows AP directly take the control if remaining time is less than T
  Pro: more efficiency
  Cos: a little more complex compare with Opt 1

## Slide 11: Summary
A mechanism is provided for target SU STA to return the TXOP to AP if there is remaining time in SU time period
  A-control subfield is a good candidate to carry the signaling
When the remain time in SU time period is not enough to transmit a QoS Null frame (carrying the TXOP return signaling), two possible way to handle it
  Opt 1: allow QoS Null frame cross the ending boundary of the SU time period
  Opt 2: set a time threshold T that allows AP directly take the control if remaining time is less than T

## Slide 12: Reference
[1] 11-20-1312-08-00be-triggered-su-ppdu-for-11ber1