## Slide 1: Error Recovery for NSTR MLD -Follow up
Date: 2021-01-10
Authors:
Name | Affiliations | Address | Phone | Email
Yunbo Li | Huawei | Shenzhen, China |  | liyunbo@Huawei.com
Yuchen Guo |  |  |  | 
Ming Gan |  |  |  | 
Guogang Huang |  |  |  | 
Yiqing Li |  |  |  | 
Rob Sun |  |  |  | 
Zhenguo Du |  |  |  | 
Notes: September 2012

## Slide 2: Background
A NSTR MLD is allowed to use an IFS larger than SIFS on the successful link to do error recovery according to below Motion;
The exact number of this IFS is TBD for now; Further details are discussed in this presentation.
  In R1, after two PPDUs with end time alignment (and the PPDUs carrying the expected response frames are also with end time alignment) are transmitted by a NSTR MLD on link 1 and link 2 respectively, STA 1 affiliated with this NSTR MLD may use an IFS greater than SIFS between the ending time of PPDU carrying the successful response frame and a following PPDU within a TXOP on link 1 when PHY-RXSTART.indication is received but FCS is not correct for response frame on link 2.
  STA 1 shall transmit the following PPDU only if the ED CS mechanism indicates that the medium is idle;
  The concrete value for the IFS greater than SIFS is TBD, with an upper limit of PIFS;
  The response frames are frames sent from STAs affiliated with the peer MLD in the TXOP in response to the frames carried in the previous PPDUs.
  [Motion 146, #SP346, [30] and [263]]

## Slide 3: Recap
This is a high level example to show how to resolve the error recovery problem for a NSTR MLD in [1];
As mentioned in [2], PPDU ending time alignment need to be considered in this scenario;
The proper IFS that can be used will be discussed in the following slides.
link1
CTS
PPDU11
BA11
PPDU12
BA12
link2
CTS
PPDU21
BA21
PPDU21’
BA21’
SIFS
SIFS
SIFS
PIFS
SIFS
SIFS
SIFS
SIFS
SIFS
PIFS
STA11
STA21
STA12
STA22
PPDU20
BA10
BA20
PPDU10

## Slide 4: Error Recovery for non-STR MLD -Case 1
Case 1
  BA11 is successfully received on link1, BA21 is failed to be received on link2;
  The ending time of BA11 is later than the ending time of BA21 with a time t;
When the starting time of PPDU12 and PPDU21’ are perfectly aligned, IFS on link1 equals to PIFS – t;
Starting time of PPDU12 and PPDU21’ with an offset that less or equal to 4us will not affect the ED sensing before PPDU12 and PPDU21’. So the IFS on link1 could be PIFS – t ± 4us.
link1
PPDU11
BA11
PPDU12
BA12
link2
PPDU21
BA21
PPDU21’
BA21’
SIFS
SIFS
SIFS
SIFS
SIFS
SIFS
SIFS
SIFS
PIFS
STA11
STA21
STA12
STA22
PPDU20
BA10
BA20
PPDU10
PIFS-t
t

## Slide 5: Error Recovery for non-STR MLD -Case 2
link1
PPDU11
BA11
PPDU12
BA12
link2
PPDU21
BA21
PPDU21’
BA21’
SIFS
SIFS
SIFS
SIFS
SIFS
SIFS
SIFS
SIFS
PIFS
STA11
STA21
STA12
STA22
PPDU20
BA10
BA20
PPDU10
PIFS-t
t
Case 2
  BA11 is successfully received on link1, BA21 is failed to be received on link2;
  The ending time of BA21 is later than the ending time of BA11 with a time t;
When the starting time of PPDU12 and PPDU21’ are perfectly aligned, IFS on link2 equals to PIFS – t;
Starting time of PPDU12 and PPDU21’ with an offset less or equal to 4us will not affect the ED sensing before PPDU12 and PPDU21’. So the IFS on link2 could be PIFS – t ± 4us.

## Slide 6: Error Recovery for non-STR MLD -Case 3
link1
PPDU11
BA11
PPDU11’
BA11’
link2
PPDU21
BA21
PPDU21’
BA21’
SIFS
SIFS
SIFS
SIFS
SIFS
SIFS
SIFS
SIFS
PIFS
STA11
STA21
STA12
STA22
PPDU20
BA10
BA20
PPDU10
PIFS-t
t
Case 3
  BA11 is failed to be received on link1, BA21 is failed to be received on link2;
  The ending time of BA21 is later than the ending time of BA11 with a time t;
When the starting time of PPDU11’ and PPDU21’ are perfectly aligned, IFS on link2 equals to PIFS – t;
Starting time of PPDU11’ and PPDU21’ with an offset less or equal to 4us will not affect the ED sensing before PPDU11’ and PPDU21’. So the IFS on link2 could be PIFS – t ± 4us.

## Slide 7: IFS Analysis
t is the time difference of ending time of BAs on two links;
The shadow area shows the possible IFS range for each different t;
When the IFS is greater than PIFS, it will violate the regulation;
When the IFS is smaller than PIFS, it will bring more challenge for implementation of ED sensing. The smaller, the more challenge.
For the IFS range [PIFS-4us, PIFS], it has at least one value that can meet the IFS requirement for any t ≤ 8us;
PIFS
PIFS-4us
PIFS+4us
PIFS-12
t=8us
t=0us
IFS
t
Violate the regulation
Hard for implementation
Suggest IFS range
Suggest to allow IFS with a range of [PIFS-4us, PIFS] for a NSTR MLD to do error recovery.

## Slide 8: Summary
From the summary in below table for all 3 cases, the IFS on the link with earlier ending BA will always be PIFS, and the IFS on the link with later ending BA will always between [PIFS-4us, PIFS].
Cases | IFSs
Case 1: Earlier ending BA is failed, Later ending BA is success | Earlier IFS = PIFS, Later IFS =[PIFS-4us, PIFS]
Case 2: Earlier ending BA is success, Later ending BA is failed | Earlier IFS = PIFS, Later IFS =[PIFS-4us, PIFS]
Case 3: Earlier ending BA is failed, Later ending BA is failed | Earlier IFS = PIFS, Later IFS =[PIFS-4us, PIFS]

## Slide 9: Summary
Base on the analysis, it is suggest that:
After two PPDUs with end time alignment (and the PPDUs carrying the expected response frames are also with end time alignment) are transmitted by a MLD on two links of a NSTR link pair respectively, when PHY-RXSTART.indication is received but FCS is not correct for response frame on one link while successful receive the response frame on another link, or PHY-RXSTART.indication is received but FCS is not correct for response frame on both links, below IFSs before next PPDU on each link are allowed for error recovery
  the IFS on the link with earlier ending response frame will be PIFS,
  the IFS on the link with later ending response frame is a value between [PIFS-4us, PIFS].
Note: when the two response frames with the same ending time, any one of the two response frames can be the earlier ending response frame or later ending response frame.

## Slide 10: Reference
[1] 11-20-1062-05-00be-error-recovery-for-non-str-mld
[2] 11-20-1278-00-00be-error-recovery-in-synchronous-multiple-frame-transmission

## Slide 11: Straw Poll 1
In R1, do you agree that after two PPDUs with end time alignment (and the PPDUs carrying the expected response frames are also with end time alignment) are transmitted by a MLD on two links of an NSTR link pair respectively, when PHY-RXSTART.indication is received but FCS is not correct for response frame on one link while successful receive the response frame on another link, or PHY-RXSTART.indication is received but FCS is not correct for response frame on both links, below IFSs before next PPDU on each link are allowed for error recovery
  the IFS on the link with earlier ending response frame will be PIFS,
  the IFS on the link with later ending response frame is a value between [PIFS-4us, PIFS].
  Note: when the two response frames with the same ending time, any one of the two response frames can be the earlier ending response frame or later ending response frame.
Y/N/A =