## Slide 1: Reducing USIG PAPR via Disregard Bit Value
Date: 2021-01-12
Authors:
Name | Affiliation | Address | Phone | Email
Shimi Shilo | Huawei Technologies |  |  | 
Oded Redlich |  |  |  | 
Genadiy Tsodik |  |  |  | 
Ross Jian Yu |  |  |  | 
Mengshi Hu |  |  |  | 

## Slide 2: Background
  As of 11be D0.2, the agreed U-SIG design for an MU PPDU is the following:
  Similarly, for a TB PPDU the following is current design in D0.2 (including several fields which are TBD):

## Slide 3: Background
  The ‘Disregard’ bits are “don’t care” for an R1 device; they may be used to convey information to R2 devices
  The ‘Validate’ bits are used by R1 devices to determine whether to terminate reception or not
  Since it is used to determine PPDU type/BW/color/TXOP etc., the U-SIG detection performance has to be significantly better than the corresponding data detection rate

## Slide 4: Disregard Bit Value
  In an MU PPDU, the Disregard bits are currently defined as set to ‘1’
  In a TB PPDU, the Disregard bits are copied from the Trigger Frame
    In 11ax, the reserved bits in HE-SIG-A are also copied from the Trigger frame and are set to ‘1’
  Validate bits are also set to ‘1’
  Many U-SIG options are not used – for example, in a 20MHz PPDU, there are only 14 ‘free’ bits (out of 26 bits) in the 1st U-SIG symbol of an MU PPDU
  In the next slide we look at the impact on the U-SIG PAPR

## Slide 5: PAPR Observations
  We compare the PAPR CCDF of both U-SIG symbols for an MU PPDU with that of the data PAPR (assuming MCS 0), in 20MHz
  Due to the large number of fixed U-SIG bits, the remaining number of possible combinations is small, and the PAPR curve is not smooth (CLT doesn’t apply)
  Here, the PAPR of the 1st U-SIG symbol exceeds that of the data PAPR in ~3-4% of the cases (on average)
  There are many cases for which U-SIG values will be fixed over time with high PAPR, for example DL+BSS Color=46+TXOP=127 yields ~11dB PAPR

## Slide 6: Potential Solutions
  We consider here two solutions:
    Solution #1: Choosing the value of the Disregard bits for each BW and PPDU type
    Solution #2: Choosing the value of the Disregard bits for each PPDU type (single value for all BW)
  For the TB PPDU, the single Validate bit can also be copied from the Trigger Frame
  In the next slides we give more details

## Slide 7: Solution #1
  For each PPDU type and BW, we find the Disregard bit sequence that minimizes the PAPR
  For example, for an MU PPDU and 20MHz BW, choosing a value of ‘0 0 1 0 1’ reduces the PAPR consistently

## Slide 8: Solution #1 – cont.
  For a TB PPDU and 20MHz BW, choosing a value of ‘0 1 1 1 1 0’ to be used in the first U-SIG symbol and ‘1 1 1 1 0’ to be used in the second U-SIG symbol leads to lowest PAPR
    In this case, Validate bit is set to ‘1’ (here value of ‘1’ yields lowest PAPR)
  A similar approach can be applied to every BW

## Slide 9: Solution #2
  Instead of defining a different Disregard sequence for each BW, set a universal sequence for all BW values
  Simulations show that for an MU PPDU, value of binary ‘0 0 1 0 1’ (decimal ‘5’) is a good solution for all BW values
  For a TB PPDU, value of binary ‘0 1 1 1 1 0’ (decimal ’30’) for both first and second U-SIG symbols is a good solution for all BW values
  See appendix for more simulation results

## Slide 10: Summary
  We described the existing U-SIG design, in particular the fact that the Disregard bits are set to all 1s, and showed that this yields a high PAPR
  Changing the value of the Disregard bits can reduce the PAPR and improve the performance
  We outlined two simple solutions
  Our preference is solution #2 – defining a single Disregard bits value for each PPDU type

## Slide 11: Straw Poll #1
  Do you support to set the default value of the Disregard bits in an EHT MU PPDU to ‘0 0 1 0 1’ (‘5’ in decimal)?
    This is for R1

## Slide 12: Straw Poll #2
  Do you support to set the default value of the Disregard bits in an EHT TB PPDU to ‘0 1 1 1 1 0 1 1 1 1 0’?
    The default value of the Disregard bits may be defined in the U-SIG field or copied from the Trigger Frame
    This is for R1

## Slide 13: Appendix
  The figure below shows the PAPR CCDF for a 20MHz MU PPDU:

## Slide 14: Appendix
  The figure below shows the PAPR CCDF for a 40MHz MU PPDU:

## Slide 15: Appendix
  The figure below shows the PAPR CCDF for an 80MHz MU PPDU:

## Slide 16: Appendix
  The figure below shows the PAPR CCDF for a 160MHz MU PPDU:

## Slide 17: Appendix
  The figure below shows the PAPR CCDF for a 320MHz MU PPDU:

## Slide 18: Appendix
  The figure below shows the PAPR CCDF for a 20MHz TB PPDU:

## Slide 19: Appendix
  The figure below shows the PAPR CCDF for a 40MHz TB PPDU:

## Slide 20: Appendix
  The figure below shows the PAPR CCDF for a 80MHz TB PPDU:

## Slide 21: Appendix
  The figure below shows the PAPR CCDF for a 160MHz TB PPDU:

## Slide 22: Appendix
  The figure below shows the PAPR CCDF for a 320MHz TB PPDU: