## Slide 1: Collaborative WLAN Sensing – Follow Ups
Date: 2021-3-09
Authors:
Name | Affiliation | Address | Phone | Email
Sang Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | sanggook.kim@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Insun Jang |  |  |  | insun.jang@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
March, 2021

## Slide 2: Introduction
WLAN sensing has drawn increasing attention due to its potential enormous opportunities to create many applications such as in home security, health care, enterprise, and building automation/management markets, etc. [1- 8]
In [7] and [8], the importance of cooperating multiple STAs in terms of performance are noted.
In [4], we considered the group-based WLAN sensing in which multitude of Wi-Fi devices are involved and collaborated and possible benefits are also addressed in addition to overhead to achieve them.
In this contribution, we provide more illustrative information for better understanding of collaborative operation in WLAN sensing.
March, 2021

## Slide 3: Recap: Example – Home Security
Intruder will use the entrances to home such as main entrance, windows, etc.
  Central entity (e.g., AP) can detect the presence of someone in the area of interest using sensing measurements.
  It may inform it to responsible person (e.g., home owner) to check.
  It may alert to responsible person if unusual pattern is detected, e.g., unusual gait pattern.
Wi-Fi devices with limited capabilities in terms of computation, power, etc. can be located around those areas for other purposes. For example, IoT devices can be used to control the curtain or blind for the window.
Devices (IoT devices, home appliances, etc.) around certain area of interest can be grouped and coordinated for home security.
March, 2021

## Slide 4: Recap: Example – Home Security (Cont’d)
Example illustration:
Intruder
Controlled by AP
Controlled by TV
AP can detect the presence of someone in the area of interest. It may simply inform to home owner the presence or may inform when unusual pattern is detected. In this example, sensing agent is located in AP, i.e., AP determines the presence based on the measurements by itself and from other STAs in the group.
“Alert”
Each group may have its
own control point (CP)
for controlling the
operation of the group.
March, 2021

## Slide 5: Recap: Example – Home Security (Cont’d)
Configurations:
Sensing
Initiator (AP)
Sensing
Responder 2
Sensing
Responder 1
Example configuration: One initiator (AP) and two responders.
AP is control point (CP).
CP is triggering the sensing transmissions and
requesting feedbacks.
Sensing transmission and feedback may be burst-based [3] when a session consists of multiple bursts.
Illustration is based on burst-based.
Each burst has sensing measurement and feedback phases.
March, 2021

## Slide 6: Recap: Example – Home Security (Cont’d)
Configurations:
Sensing
Initiator (AP)
Sensing
Responder 2
Sensing
Responder 1
1st Burst: Transmission
Initiator transmits and two responders receive.
Available channel information: Initiator to responder 1 and
initiator to responder 2
Sensing
Initiator (AP)
Sensing
Responder 2
Sensing
Responder 1
1st Burst: Feedback
Two responders feedback the measurements to initiator.
Sensing
Transmitter
Sensing
Receiver
Sensing
Receiver
Feedback
Receiver
Feedback
Transmitter
Feedback
Transmitter
March, 2021

## Slide 7: Recap: Example – Home Security (Cont’d)
Configurations:
Sensing
Initiator (AP)
Sensing
Responder 2
Sensing
Responder 1
Sensing
Initiator (AP)
Sensing
Responder 2
Sensing
Responder 1
2nd Burst: Transmission
Responder 1 transmits, initiator and responder 2 receive.
Available channel information: Responder 1 to initiator and
responder 1 to responder 2.
2nd Burst: Feedback
Responder 2 feedbacks channel measurement between
responder 1 and itself.
Sensing
Receiver
Sensing
Transmitter
Sensing
Receiver
Feedback
Receiver
Feedback
Transmitter
March, 2021

## Slide 8: Illustrative Example: Explicit Feedbacks
STA 1 (AP)
STA 2
STA 3
NDP 1 (1)
NDP 2 (1)
NDP 1 (1)
NDP 2 (1)
NDP 1 (1)
NDP 2 (1)
CH 1  2
CH 1  3
CH 1  2
CH 1 3
Burst #1
STA 1
STA 2
STA 3
Sensing signal transmission
Feedback (Can be simultaneous)
STA 1
STA 2
STA 1
STA 3
Topology
Channel Measurement
Information
STA1: AP, STA2: Responder 1, STA3: Responder 2
Note: 2 consecutive NDP transmissions are assumed for sensing transmission
for illustrative purpose. More than one feedback per burst.
Triggering
Feedback
Request
Feedback
Request
Feedback
Request
Feedback
Request
Triggering
Triggering
CH i  j: Channel measurement information between STA i and STA j.
March, 2021

## Slide 9: Illustrative Example: Explicit Feedbacks
STA 2
STA 1 (AP)
STA 3
NDP 1 (2)
NDP 2 (2)
NDP 1 (2)
NDP 2 (2)
NDP 1 (2)
NDP 2 (2)
CH 2  3
CH 2  3
Burst #2
STA 2
STA 1
STA 3
Sensing signal transmission
Feedback
STA 2
STA 3
Topology
Channel
Measurement
Information
Channel Measurement information Available:
@ Initiator (STA1: AP)
STA 1 & 2 (Burst #1)
STA 1 & 3 (Burst #1)
STA 2 & 3 (Burst #2)
STA1: AP, STA2: Responder 1, STA3: Responder 2
Note: 2 consecutive NDP transmissions are assumed for sensing transmission
for illustrative purpose. More than one feedback per burst.
Triggering
Triggering
Triggering
Feedback
Request
Feedback
Request
CH i  j: Channel measurement information between STA i and STA j.
March, 2021

## Slide 10: Illustrative Example: Implicit Sensing Measurement + Explicit Feedbacks
STA1: AP, STA2: Responder 1, STA3: Responder 2
STA 1 (AP)
STA 2
STA 3
NDP 1 (2)
NDP 2 (2)
NDP 1 (2)
NDP 2 (2)
NDP 1 (1)
NDP 2 (1)
Burst #1
Sensing signal transmission
STA 1
STA 2
STA 3
STA 2
STA 1
Topology
Sensing Transmission for Channel
Measurement
Implicit
Note: 2 consecutive NDP transmissions are assumed for sensing transmission
for illustrative purpose.
Triggering
Triggering
Triggering
March, 2021

## Slide 11: Illustrative Example: Implicit Sensing Measurement + Explicit Feedbacks
STA1: AP, STA2: Responder 1, STA3: Responder 2
STA 1 (AP)
STA 3
STA 2
Burst #2
STA 1
STA 2
STA 3
STA 3
STA 1
STA 2
STA 3
NDP 1 (3)
NDP 2 (3)
NDP 1 (3)
NDP 2 (3)
NDP 1 (3)
NDP 2 (3)
Sensing signal transmission
CH 3  2
CH 3  2
Topology
Explicit
Feedback to
STA 1
Note: 2 consecutive NDP transmissions are assumed for sensing transmission
for illustrative purpose.
Triggering
Triggering
Triggering
Feedback
Request
Feedback
Request
CH i  j: Channel measurement information between STA i and STA j.
Channel Measurement information Available:
@ Initiator (STA1: AP)
STA 1 & 2 (Burst #1)
STA 1 & 3 (Burst #2)
STA 2 & 3 (Burst #3)
Feedback
March, 2021

## Slide 12: Benefits
Accurate sensing over the area of interest can be achievable:
  Multitude of Wi-Fi capable devices selected for sensing (grouping) and their collaboration as a group in orderly fashion can provide additional information.
  Without grouping and collaboration, sensing can be considered as the one between one-to-one device or among one-to-many devices.
  With grouping and collaboration, sensing can be considered as the one among many-to-many devices. More information on channel can be obtained and processed, thus leading to accurate sensing.
  Note that grouping concept is logical on top of existing architecture.
Sensing requirements for different use cases can be tailored:
  Presence detection vs. Health monitoring.
  Less frequent sensing measurements using home appliances in the living room (presence detection).
  More frequent sensing measurements using the home appliances and IoT devices in the bedroom (health monitoring).
  Less number of devices for presence detection than for accurate health monitoring.
March, 2021

## Slide 13: Benefits (Cont’d)
Computational benefit can be exploited by devices with less computational capability and power constraint:
  Sensing measurements can be delivered to AP for useful information extract over the area of interest.
  Computation to extract useful information may be done in AP or Cloud.
Aforementioned benefits, of course, entails increased overhead:
  For example, channel measurement gathering may require additional signaling and time allocation.
  We need to consider the trade-off depending on the applications, and etc.
March, 2021

## Slide 14: Summary
WLAN sensing has drawn increasing attention due to its possible and potential opportunities to create many applications such as in home security, health care, enterprise, and building automation/management markets, etc.
In this contribution, we provide more illustrative information for better understanding of collaborative operation in WLAN sensing.
Consideration on protocol aspects will be followed in a separate contribution.
March, 2021

## Slide 15: References
[1] Wi-Fi Sensing – A New Technology Emerges. v1.0, October 2019, Wireless Broadband Alliance (https://wballiance.com/wba-wi-fi-sensing/)
[2] 11-20/1239r0, Use Cases for Wireless LAN Sensing.
[3] 11-20/1232r0, Overview of WLAN sensing protocol.
[4] 11-20/1533r0, Collaborative WLAN Sensing.
[5] 11-20/1805r0, Discussion on WLAN Sensing Roles.
[6] 11-20/1804r0, Discussion on WLAN Sensing Procedure.
[7] 11-19/1416r0, Wi-Fi Sensing: Cooperation and Standard. Support.
[8] 11-19/1551r1, Wi-Fi Sensing in 60GHz band: Usage models, Performance and What is need in 802.11 Standard
March, 2021

## Slide 16: SP #1
Do you support to have a sensing session that is comprised of multiple burst instances?
March, 2021

## Slide 17: SP #2
Do you support the receiving station reports with the channel information to the initiator?
  Withdrawn
March, 2021

## Slide 18: SP #3
Do you support the receiving station reports with the channel measurement between sensing responders to the initiator?
  Withdrawn
March, 2021

## Slide 19: SP #4
Do you agree to move the following into 11bf SFD?
  More than one sensing responder may participate in a measurement and reporting phases of a sensing session.
March, 2021