## Slide 1: Multi-link TIM follow-up
Date: 2021-01-19
Authors:
Name | Affiliations | Address | Email
Jeongki Kim | LG Electronics | LG Seocho R&D Campus, Korea | jeongki.kim@lge.com
Namyeong Kim | LG Electronics |  | namyeong.kim@lge.com
Sunhee Baek | LG Electronics |  | sunhee.baek@lge.com
Insun Jang | LG Electronics |  | insun.jang@lge.com
Jinsoo Choi | LG Electronics |  | js.choi@lge.com

## Slide 2: Abstract
In this contribution, we propose the method for enhancing MLD level TIM mechanism for considering default TID-to-link mapping

## Slide 3: Introduction
Traffic indication in TGbe D0.3 (35.3.9.4 )
  An AP MLD shall assign a single AID to a non-AP MLD upon successful multi-link setup. All the STAs of the non-AP MLD shall have the same AID as the one assigned to the non-AP MLD during multi-link setup.
  An AP MLD shall indicate pending buffered traffic for non-AP MLDs using partial virtual bitmap of TIM element in a Beacon frame as described in 9.4.2.5 (TIM element).
The MLD level TIM will be used for default TID mapping traffic
  TIM for the specific TID-to-link mapping is TBD
In the REVmd, if a non-AP STA receives the TIM for the STA, the STA sends PS-Poll to indicate its awake state
When a non-AP MLD receive MLD level TIM, the non-AP MLD decides how many STAs in the MLD should be waken up, which will be non-AP MLD’s implementation-specific
  For example, the MLD can decide to wake up all STAs in the MLD to retrieve the DL data fast or one or some STAs in the MLD to save its power more

## Slide 4: Non-AP MLD operation for MLD level TIM
Basically, non-AP MLD does not know how much data AP MLD has for the non-AP MLD and the non-AP MLD decides its wake-up operation without considering a mount of buffered data
  Note that a STA in a single link does not need to know the amount of the DL buffered data because the AP will deliver the DL buffered traffic to the STA on the single link when the STA wakes up
When a single STA in the non-AP MLD wakes up, if the AP MLD has a lot of DL buffered data for the non-AP MLD, the DL data will be delivered to the non-AP MLD lately, especially when the selected link is congested
When all STAs in the non-AP MLD wakes up, if the AP MLD has small amount of DL buffered data for the non-AP MLD, the DL data will be delivered to the non-AP MLD on only one link and other links are not used so that the power consumption of the non-AP MLD will be increased

## Slide 5: Proposal (1/4)
AP MLD can provide the information about the buffered traffic with the non-AP MLD
  Amount of buffered DL data
  TID information related to the buffered DL data
  Others
Based on the received information, the non-AP MLD can decide how many STAs in the MLD should be awaken

## Slide 6: Proposal (2/4)
Case 1: Sending the DL buffered traffic related information with TIM in Beacon
Beacon
AP1 of
AP MLD1
*TIM (MLD1)
* Buffer status of MLD1
STA1 of non-AP MLD1
PS-Poll
Data
BA
STA2 of non-AP MLD1
AP2 of
AP MLD1
STA3 of non-AP MLD1
AP3 of
AP MLD1
PS-Poll
Data
BA
STA1 and STA2 are awaken based on the buffer status

## Slide 7: Proposal (3/4)
Case 2: Including the DL buffered traffic related information in DL data
Beacon
AP1 of
AP MLD1
*TIM (MLD1)
STA1 of non-AP MLD1
PS-Poll
Data +
BSR of MLD 1
BA
STA2 of non-AP MLD1
AP2 of
AP MLD1
STA3 of non-AP MLD1
AP3 of
AP MLD1
PS-Poll
Data
BA
STA1 is awaken

## Slide 8: Proposal (4/4)
Case 3: Hybrid indication to alleviate the Beacon overhead
Beacon
AP1 of
AP MLD1
*TIM (MLD1, 2)
* Buffer status of MLD2
STA1 of non-AP MLD1
PS-Poll
Data +
BSR of MLD 1
BA
STA2 of non-AP MLD1
AP2 of
AP MLD1
PS-Poll
Data
BA
STA1 of MLD 1 is awaken
STA1 of non-AP MLD2
STA2 of non-AP MLD2
PS-Poll
Data
BA

## Slide 9: Example of Signaling
For case 1 (with TIM)
  Buffer status report of non-AP MLD can be carried in the element
For case 2 (within DL data)
  Buffer status report of non-AP MLD can be carried in A-Control field
Control ID
= BSR of non-AP MLD
Queue size of MLD
Scaling factor
Element ID
= BSR of non-AP MLD
Queue size of MLD
Scaling factor
MLD ID information
Length
Repeated for each MLD

## Slide 10: Conclusion
When a non-AP MLD receives TIM indicating the MLD for default mapping traffic, the non-AP MLD need to decide how many links should be awaken
To select the proper number of the links, AP MLD can provide the non-AP MLD with some information such as the buffer status of the non-AP MLD or traffic ID/traffic characteristic
The information can be carried with the TIM information or DL data frame

## Slide 11: Straw Poll 1
Do you agree to add the following in R1?
  When an AP of an AP MLD sends a traffic indication to a non-AP STA of a non-AP MLD with the default TID mapping traffic, the AP can provide the non-AP STA with amount of buffer traffics for the non-AP MLD

## Slide 12: Straw Poll 2
Do you agree to add the following in R1?
  When an AP of an AP MLD sends a non-AP STA of a non-AP MLD the DL data frame, the AP can provide the non-AP STA with amount of buffer traffics for the non-AP MLD