## Slide 1: MLO Group Addressed MSDU Architecture
Date: 2021-03-30
Authors:

## Slide 2: ESS Topology with Two Legacy BSSs and one MLD
MLD AP
MAC_AP_MLD
2.4 GHz AP
BSSID_24
5 GHz AP
BSSID_5
Wired G/W
Legacy MAC_STA1
Legacy MAC_STA2
Non-AP MLD
MAC_NAP_MLD
2.4 STA
5 STA
NOTE: 2.4 GHz and 5 GHz APs advertise the same SSID and are connected to the DS.

## Slide 3: DS Representation of network (no legacy STAs)
DS
MLD AP
MAC_AP_MLD
2.4 GHz AP
BSSID_24
5 GHz AP
BSSID_5
Wired LAN
Non-AP MLD
MAC_NAP_MLD
2.4 STA
MAC_24
5 STA
MAC_5
Portal

## Slide 4: DS Representation of network with legacy STAs
Affiliated APs connect to the DS to service legacy STAs.
DS
MLD AP
MAC_AP_MLD
2.4 GHz AP
BSSID_24
5 GHz AP
BSSID_5
Wired LAN
Legacy MAC_STA1
Legacy MAC_STA2
Non-AP MLD
MAC_NAP_MLD
2.4 STA
MAC_24
5 STA
MAC_5
Portal
NOTE: P802.11be is in the process of agreeing to assign sequence numbers for group-addressed frames at the MLD level. A group-addressed frame will have the same sequence number when it is transmitted by different affiliated APs.

## Slide 5: Case 1. Group-Addressed MSDUs (i.e. data frames) received from LAN
MLD AP
MAC_AP_MLD
2.4 GHz AP
BSSID_24
5 GHz AP
BSSID_5
LAN
Legacy STA 1
MAC_STA1
Legacy MAC_STA2
Non-AP MLD
MAC_NAP_MLD
2.4 STA
MAC_24
5 STA
MAC_5
Portal
DS
2
2
1
2
3
3

## Slide 6: Procedure and Addressing for Case 1
1 – Frame goes from LAN to DS:
  Dest Addr: <BC/MC Address>
  Src Addr: <STA on LAN>
2 – Frame passes from DS to AP MLD and affiliated APs
  AP MLD assigns sequence number and transfers frame to affiliated APs.
  Dest Addr: <BC/MC Address>
  Src Addr: <STA on LAN>
3 – Frame is transmitted by affiliated APs to BSS
  A1: <BC/MC Address>
  A2: <BSSID of affiliated AP>
  A3: <STA on LAN>
  ToDS: 0 FromDS: 1
Note: Affiliated APs receive the group-addressed frame from DS but does not process it.

## Slide 7: 2. Group-Addressed MSDU (i.e. data frame) from Legacy STA (STA 1)
MLD AP
MAC_AP_MLD
2.4 GHz AP
BSSID_24
5 GHz AP
BSSID_5
LAN
Legacy MAC_STA1
Legacy MAC_STA2
Non-AP MLD
MAC_NAP_MLD
2.4 STA
MAC_24
5 STA
MAC_5
Portal
DS
1
2
3
3
3
5
5
4
4
3

## Slide 8: Procedure and Addressing for Case 2
1 – Group-addressed MSDU from Legacy STA to BSSID_24 transmitted as an individually addressed frame:
  A1: BSSID_24
  A2: MAC_STA1
  A3: <BC/MC Address>
  ToDS: 1 FromDS: 0
2 – Affiliated AP (BSSID_24) forwards frame to DS
  Dest Addr: <BC/MC Address>
  Src Addr: <MAC_STA1>
3 – DS distributes frame to the LAN, the AP MLD, and the other affiliated APs
  Dest Addr: <BC/MC Address>
  Src Addr: <MAC_STA1>
4 – Frame is transmitted by affiliated APs to BSS
  AP MLD assigns sequence number and transfers frame to affiliated APs
  A1: <BC/MC Address>
  A2: <BSSID of affiliated AP>
  A3: <MAC_STA1>
  ToDS: 0 FromDS: 1
Note: Other affiliated APs receive the group-addressed frame from the DS but do not process it.

## Slide 9: 3. Group-Addressed MSDU (i.e. data frame) from non-AP MLD
2.4 GHz AP
BSSID_24
MLD AP
MAC_AP_MLD
5 GHz AP
BSSID_5
LAN
Legacy MAC_STA1
Legacy MAC_STA2
Non-AP MLD
MAC_NAP_MLD
2.4 STA
MAC_24
5 STA
MAC_5
Portal
DS
1
2
3
3
3
4
4
4
4
3
NOTE: The non-AP MLD can transmit the group-addressed MSDU to the AP MLD via either affiliated AP.

## Slide 10: Addressing for Case 3
1 – Group-addressed MSDU from non-AP MLD to AP MLD transmitted as an individually addressed through affiliated 2.4 STA.
  A1: BSSID_24 (MAC_AP_MLD in AAD)
  A2: MAC_24 (MAC_NAP_MLD in AAD)
  A3: <BC/MC Address>
  ToDS: 1 FromDS: 0
2 – AP MLD forwards the frame to the DS
  Dest Addr: <BC/MC Address>
  Src Addr: <MAC_NAP_MLD>
3 – The DS distributes the frame to the LAN and affiliated APs
  Dest Addr: <BC/MC Address>
  Src Addr: <MAC_NAP_MLD>
4 – Frame is transmitted by affiliated AP to BSS.
  AP MLD assigns sequence number and transfers frame to affiliated AP.
  A1: <BC/MC Address>
  A2: <BSSID of AP>
  A3: <MAC_NAP_MLD>
  ToDS: 0 FromDS: 1
Note: AP MLD receives frame from non-AP MLD but does not forward on downlink

## Slide 11: SSID, ESS, and MLO
Section 2

## Slide 12: Two Legacy BSSs - Same LAN – 2 ESS’s - Topology
2.4 GHz AP
BSSID_24
5 GHz AP
BSSID_5
Wired G/W
Legacy MAC_STA1
Legacy MAC_STA2
SSID: MyHome-24
SSID: MyHome-5
LAN
Legacy STA needs one saved network configuration

## Slide 13: Two Legacy BSSs - Same LAN – 2 ESS’s – DS view
2.4 GHz AP
BSSID_24
5 GHz AP
BSSID_5
Wired G/W
Legacy MAC_STA1
Legacy MAC_STA2
SSID: MyHome-24
SSID: MyHome-5
LAN
PORTAL
PORTAL
DS
DS
Different ESSs – one for 2.4 and the other for 5
Connection is to the same LAN
No coordination between APs
Legacy STA needs two saved network configurations
BSS Transition won’t work

## Slide 14: Two Legacy BSSs - Same LAN – 1 ESS - Topology
2.4 GHz AP
BSSID_24
5 GHz AP
BSSID_5
Wired G/W
Legacy MAC_STA1
Legacy MAC_STA2
SSID: MyHome
SSID: MyHome
LAN

## Slide 15: Two Legacy BSSs - Same LAN – 1 ESS’s – DS view
2.4 GHz AP
BSSID_24
5 GHz AP
BSSID_5
Wired G/W
Legacy MAC_STA1
Legacy MAC_STA2
SSID: MyHome
SSID: MyHome
LAN
PORTAL
DS
Same ESSs – two APs
Single DS
No coordination between APs
Legacy STA needs one saved network configuration
BSS Transition works.

## Slide 16: MLO ESS Topology with Two Legacy BSSs - Same
MLD AP
MAC_AP_MLD
2.4 GHz AP
BSSID_24
5 GHz AP
BSSID_5
Wired G/W
Legacy MAC_STA1
Legacy MAC_STA2
Non-AP MLD
MAC_NAP_MLD
2.4 STA
5 STA
NOTE: 2.4 GHz and 5 GHz APs advertise the same SSID and are connected to the DS.
SSID: MyHome
SSID: MyHome

## Slide 17: DS Representation MLO with legacy STAs
Affiliated APs connect to the DS to service legacy STAs.
DS
MLD AP
MAC_AP_MLD
2.4 GHz AP
BSSID_24
5 GHz AP
BSSID_5
Wired LAN
Legacy MAC_STA1
Legacy MAC_STA2
Non-AP MLD
MAC_NAP_MLD
2.4 STA
MAC_24
5 STA
MAC_5
Portal
NOTE: P802.11be has agreed to assign sequence numbers for group-addressed frames at the MLD level. A group-addressed frame will have the same sequence number when it is transmitted by different affiliated APs.
SSID: MyHome
SSID: MyHome

## Slide 18: DS Representation MLO with legacy STAs w/separate SSIDs for legacy STAs
Affiliated APs connect to the DS to service legacy STAs.
DS
MLD AP
MAC_AP_MLD
2.4 GHz AP
BSSID_24
5 GHz AP
BSSID_5
Wired Gateway
Legacy MAC_STA1
Legacy MAC_STA2
Non-AP MLD
MAC_NAP_MLD
2.4 STA
MAC_24
5 STA
MAC_5
Portal
NOTE: P802.11be has agreed to assign sequence numbers for group-addressed frames at the MLD level. A group-addressed frame will have the same sequence number when it is transmitted by different affiliated APs.
SSID: MyHome
SSID: MyHome
SSID: MyHome-24
SSID: MyHome-5
DS
DS
Portal
Portal

## Slide 19: Conclusions on DS/RSS/SSID
From this work on group-addressed frame processing, it follows that the affiliated APs need to be connected to the same DS as the AP MLD.
To be part of the same DS, the affiliated APs are required to be part of the same ESS, and hence advertise the same SSID.
As additional references, see
  https://www.ieee802.org/11/email/stds-802-11-tgbe/msg06933.html
  https://mentor.ieee.org/802.11/dcn/21/11-21-1111-10-00be-mld-architecture-part-2.docx

## Slide 20: CID 6725 – Disallow SSID element in STA Profile
CID | Clause | Page | Comment | Proposed Change | Resolution
6725 | 35.3.2.2 | 248.26 | Why disallow SSID element to be included in the STA Profile field? If the different APs of the MLD use different SSIDs, the SSID element should be included in the STA Profile. | Delete SSID element from the list. | REJECTED. The mapping for the AP MLD and affiliated APs and how they fit into the IEEE 802.11 framework has been discussed extensively in the 802.11 ARC standing committee and is reflected in contributions https://mentor.ieee.org/802.11/dcn/21/11-21-1111-10-00be-mld-architecture-part-2.docx and https://mentor.ieee.org/802.11/dcn/21/11-21-0209-00-00be-mlo-broadcast-architecture.pptx. For MLO to work, the AP MLD and the affiliated APs are required to be connected to the same DS. Furthermore, the task group has agreed that group-addressed frames are assigned an SN at the AP MLD, which reinforces that the AP MLD and affiliated APs are connected to the same DS. Given that in the baseline, APs that are connected to the same DS are part of the same ESS and advertise the same SSID, it follows that AP's affiliated with an AP MLD advertise the same SSID.

## Slide 21: CIDs 4919 – Clarify SSID for affiliated APs
CID | Clause | Page | Comment | Proposed Change | Resolution
4919 | 35.3.2.2 | 0.00 | SSID settings of the affiliated APs of an AP MLD is not clear | Add a note to clarify all affilicated APs of an AP MLD use the same SSID - adopt the latest revision of 21/537 | REVISED All APs affiliated with the same AP MLD have the same SSID. The proposed resolution adds a NOTE in clause 35.3.2.2 to clarify this aspect. TGbe editor: Relative to D1.5, please add the following note in clause 35.3.2.2 before the paragraph starting with “An example of Basic Multi-Link element, carrying …” [D1.5 P377L32] as shown below: “NOTE 4 – All APs affiliated with the same AP MLD advertise the same SSID.”