## Slide 1: EHT PPET Capability Design
Date: 2021-02-04
Authors:

## Slide 2: Introduction
11be nominal packet padding capability is defined in two ways, similarly as 11ax:
  Nominal Packet Padding field: definition was agreed [1].
  PPE Thresholds field: definition is TBD
Several designs are proposed in [2, 3] following 11ax style.
We propose a design to further streamline the HE and EHT PPET signaling.

## Slide 3: Recap: Nominal Packet Padding Capability
2-bits field:
  Keep definition of 0~2 as 11ax, and redefine value 3.
  20us PE is allowed for RU>2x996 || Nss>8 || 4k-QAM.
Define EHT PPET based on similar rule.
Nominal Packet Padding | Encoding
0 | Set to 0 if the nominal packet padding is 0 μs for all constellations, NSS and RU allocations the STA supports.
1 | Set to 1 if the nominal packet padding is 8 μs for all constellations, NSS and RU allocations the STA supports.
2 | Set to 2 if the nominal packet padding is 16 μs for all constellations, NSS and RU allocations the STA supports.
3 | Set to 3 if the nominal packet padding is 16 μs for all modes with constellation<=1024, NSS<=8 and RU<=996*2, and 20us for all other modes the STA supports.

## Slide 4: Recap: HE PPET Design
Detailed nominal packet padding indication for each [Nss, RU]
HE PPE Thresholds field:
  NSTS: total number of NSTS that will have PPET elements
  RU Index Bitmask: 4-bit Bitmap for RU [242, 484, 996, 996x2].
  PPET Info field:
    Two PPET elements for each [Nsts, RU] : PPE16 and PPE8.
    QAM threshold for nominal packet padding of 16us and 8us.

## Slide 5: EHT PPET Design
EHT PPET needs to extend to cover
  Nss=16, RU=996x4 and 4k-QAM, and 20us nominal packet padding.
HE PPET indication logic is relatively complex and the overhead can be high for large Nss and RU.
EHT PPET design goals:
  Keep similar structure as HE PPET: the EHT PPET setting and parsing logic will be similar as HE
  Allow EHT PPET being skipped if EHT nominal packet padding is the same as HE for modes defined in HE PPET.

## Slide 6: EHT PPET
4-bit NSS = 1:16 [2]
5-bit RU Index Bitmask = 242, 484, 996, 996*2, 996*4 [2]
Two PPETs per [Nss, RU]: PPETx and PPET8
  PPET8 indicates QAM threshold for nominal packet padding =8us
  PPETx indicates QAM threshold for next higher nominal packet padding:
    16us for RU<=996*2 and Nss<=8 and QAM<=1024
    20us for other modes
PPETx | PPET8 | PPETx | PPET8 | … | PPETx | PPET8
NSS | RU Index Bitmap
…
Nss = 1
Nss = 2
Nss_max
RU4x996
PPETx | PPET8 | PPETx | PPET8 | … | PPETx | PPET8
PPETx | PPET8 | PPETx | PPET8 | … | PPETx | PPET8

## Slide 7: PPET Indication
PPET8 | PPETx |  | Nominal Packet padding
QAM >= PPET8 | QAM < PPETx ¦¦ PPETx is 7 |  | 8 us
QAM >= PPET8 ¦¦ PPET8==7 | QAM >= PPETx | QAM <= 5 && RU<=996*2 && Nss<=8 | 16 us
 |  | else | 20 us
else |  |  | 0
4096-QAM

## Slide 8: PPE Thresholds Present
In 11ax, “PPE Thresholds Present” bit indicates the presence of PPET field.
  PPET field is skipped if “PPE Thresholds Present” bit is set to 0.
For an EHT STA,
  EHT nominal PE for [Nss, RU] within HE modes can be the same as HE
  Only HE PPET needs to be present, and EHT PPET can be skipped.
  E.g.: 160 MHz or 320 MHz EHT STA with 2ss support
    The nominal PE for both EHT and HE PPDU is likely the same for all RU<=996x2 and Nss<=2.
  All corresponding EHT PPET elements can be skipped.

## Slide 9: EHT PPE Thresholds Present
In [2], the presence of PPE Thresholds field is indicated by “PPE Thresholds Present” subfield.
1: EHT PPET field is present
0: EHT PPET field is not present
  PHY Capability field of EHT Common Nominal Packet Padding is specified.
  If HE “PPE Thresholds Present”=1,
    EHT nominal packet padding is the same for all modes covered in HE PPET
      For Nss = 1:NSTS+1 and RU/MRU within the Bitmap range [242, 484, 996, 996x2], all rules of HE PPET parsing for NSTS and RU Index Bitmask apply.
      EHT nominal packet padding for 484+242 follows HE PPETs for RU996.
      EHT nominal packet padding for MRU 996+484, 996+484+242 follows HE PPETs for RU996*2.
    For nominal packet padding not covered in HE PPET, use the values indicated in EHT Common Nominal Packet Padding, i.e. RU > 996x2 or Nss>8 or 4K-QAM.
      EHT Common Nominal Packet Padding shall be larger than or equal to the larger normal packet padding values among all modes covered in HE PPET.
  If HE “PPE Thresholds Present”=0, EHT nominal packet padding follows the values indicated in EHT Common Nominal Packet Padding for all EHT PPDUs.
    EHT Common Nominal Packet Padding shall not be smaller than HE Nominal Packet Padding.

## Slide 10: SP1
Do you agree that EHT PPE Threshold Info field includes two PPET elements for each case with 1<=Nss<=NSS+1 and RU with value 1 in the RU Index Bitmask:
  PPET8 indicates QAM threshold for nominal packet padding of 8us
  PPETx indicates QAM threshold for next higher nominal packet padding:
    16us for RU<=996*2 and Nss<=8 and QAM<=1024
    20us for other modes

## Slide 11: SP2
Do you agree to EHT “PPE Thresholds Present” is defined as follows?
1: EHT PPET field is present
0: EHT PPET field is not present
  PHY Capability field of EHT Common Nominal Packet Padding is specified.
  If HE “PPE Thresholds Present”=1,
    EHT nominal packet padding is the same for all modes covered in HE PPET
      For Nss = 1:NSTS+1 and RU/MRU within the Bitmap range [242, 484, 996, 996x2], all rules of HE PPET parsing for NSTS and RU Index Bitmap apply.
      EHT nominal packet padding for 484+242 follows HE PPETs for RU996.
      EHT nominal packet padding for MRU 996+484, 996+484+242 follows HE PPETs for RU996*2.
    For nominal packet padding not covered in HE PPET, use the values indicated in EHT Common Nominal Packet Padding, i.e. RU > 996x2 or Nss>8 or 4K-QAM.
      EHT Common Nominal Packet Padding shall be larger than or equal to the larger normal packet padding values among all modes covered in HE PPET.
  If HE “PPE Thresholds Present”=0, EHT nominal packet padding follows the values indicated in EHT Common Nominal Packet Padding for all EHT PPDUs.
    EHT Common Nominal Packet Padding shall not be smaller than HE Nominal Packet Padding.

## Slide 12: SP3
Do you agree that the EHT Constellation Index table is defined the same as HE Constellation Index table except that value 6 is redefined as 4096-QAM?

## Slide 13: References
[1] Rui Cao and etc., 11-20-1331-00-00be-eht-pre-fec-padding-and-packet-extension
[2] Mengshi Hu and etc., 11-20-1847-00-00be-eht-ppe-thresholds-field
[3] Mengshi Hu and etc., 11-21-0089-01-00be-eht-ppe-thresholds-field-follow-up