## Slide 1: Protecting CH_BANDWIDTH_IN_NOT_HT (etc) in Service field
Date: 2021-06-20
Authors:

## Slide 2: Situation
Indication for ≥320 MHz non-HT duplicate PPDUs in 6 GHz now uses bit 7 in the Service field
No protection was defined for that bit (no Parity, CRC, etc)
The number of bits allocated to protection should account for the number of bits needed for other purposes:
  E.g., self-contained static or dynamic puncturing pattern index for non-HT duplicate PPDUs.

## Slide 3: Using the MPDU’s FCS as a proxy for Service field protection is suboptimal
Some individuals propose that the “CRC” for the Service field can be the FCS for the MPDU contained in the Data field. On the other hand:
  The Service field is a PHY-to-PHY communications channel, and architecturally it should not depend on the correctness or otherwise of the MAC-to-MAC payload
  We don’t know how the Service field will evolve, but we cannot rule out that some use cases may operate without regard to the correctness of the contained MPDU.
    E.g., enabled improved PER by utilizing the diversity of the punctured duplicates of the Data field
  The side-effects of the weak parity chosen for the LSIG field are well known. Certainly, we need to mandate additional or unavoidable RX checking: since these non-HT PPDUs are widely used for MAC protection, then weak implementations in third-party STAs hurt all transmissions.
  Additional RX checking can be of Parity/CRC in Service field; unavoidable RX checking might be that further action does not occur without a good MPDU.
  Adding a Parity/CRC now provides better and broader protection than adding it later when and if it becomes essential
  Using the FCS of the MPDU as Parity/CRC for the Service field is akin to defining an FCS of the MDPU that protects the whole MPDU except for the first few MPDU bits.
    But we would never propose that, because it’s an unnecessarily weak design
  The implementation cost of adding Parity/CRC on a few bits is utterly trivial, so if Parity/CRC provides any benefits at all then we should strongly consider adding it.

## Slide 4: Other Uses for the Service field: Signalling Puncturing Pattern Index
20, 40 MHz PPDU – N/A
80 MHz PPDU
  5 distinct values (1 unpunctured + 4 punctured values): i.e., 3 bits required
  Needed in both 5 GHz (where Service field should not be used) and 6 GHz
  Can use the same design for both 5 and 6 GHz using the Pad field (in an HESIGB-like design), and not needing any Service field bits (see sidebar)
160 MHz PPDU
  13 distinct values (1 unpunctured + 12 punctured values): i.e., 4 bits required
  Needed in both 5 GHz (where Service field should not be used) and 6 GHz
  Can use the same design for both 5 and 6 GHz using the Pad field (in an HESIGB-like design), and not needing any Service field bits (see sidebar)
320 MHz
  25 distinct values (1 unpunctured + 24 punctured values): i.e., 5 bits required
  Needed in 6 GHz only (where Service field can be used)

## Slide 5: Sidebar: Proposed TX Bit Processing for 80/160 MHz PPDUs

## Slide 6: Feasible Design for Service field in 320 MHz PPDUs
Bit 2 of CBINH
Puncturing pattern index
2R+ Parity or CRC
Sample encoding
  1 extra bit for CH_BANDWIDTH_IN_NOT_HT (CBINH) parameter to define ≥320 MHz bandwidths (already defined)
  5 bits available to signal puncturing pattern index
  1 Parity bit or 3 bits for CRC using x3 + x + 1
    CRC has a Hamming distance of 2, detects all 1-bit errors
  … which fits into 7 or 9 bits

## Slide 7: Performance Results
20B (RTS), 6 Mbps, 1TX x 1RX, ChB
Bad Service fields do occur, even with additional checks
If we choose simplicity. conditioning the use of the Service field on a good MPDU (blue dashed line) is very reliable
  Adding Parity (cyan dashed line) or especially a 3 bit CRC (red dashed line) helps further
If we choose architectural purity / future proofing, checking the Service field without regard to the MPDU via one Parity bit (solid cyan) is also a big improvement over no checking, and more so with a 3 bit CRC (solid red)
  But not as impactful as checking the MPDU

## Slide 8: Supporting More Puncturing Pattern Indices
Some people are interested in supporting more Puncturing Pattern Indices in 11beR2, to the extent that they wish for more than 5 bits
  Cannot use a 3 bit CRC in this scenario
There is no 2 bit CRC, but we can use parity in multiple ways:
  Separate parity on early / late bits in Service field (e.g. 7:9, 10:13)
  Separate parity on odd / even bits in Service field (e.g. 7:2:13, 8:2:13)
  Parity on the entire Service field (7:13) then an extra parity on early / late / even / odd bits
    The non-grayed options provide 2 bits of parity on the newly-defined bit of CH_BANWIDTH_IN_NON_HT
Performance from 2 bits of parity is expected to be partway between 1 bit of parity and a 3 bit CRC

## Slide 9: Strawpoll
Option A: No Parity or CRC to protect Service field
  Any future use of Service field should be conditional on a good MPDU (which is already implicit in today’s use of the Service field)
Option B: Add 1 bit of Parity to Service field bit 15 that protects Service field bits 7-14
Option C: Add 2 bits of Parity to Service field bits 14-15 that protect Service field bits 7-13 (Details TBD)
Option D: Add a 3 bit CRC to Service field bits 13-15 that protects Service field bits 7-12
Abstain
Pick your favorite option

## Slide 10: Backup

## Slide 11: Preamble Puncturing Modes
If needed, self-contained static or dynamic preamble puncturing signaling requires 3/4/5 bits for 80/160/320 MHz respectively:
Bandwidth (MHz) | Preamble puncturing modes | Count
20 | 1 | 1
40 | 11 | 1
80 | 1111; x111, 1x11, 11x1, 111x | 5
160 | 11111111; xx1111111, 11xx1111, 1111xx11, 111111xx; x1111111, 1x111111, 11x11111, 111x1111, 1111x111, 11111x11, 111111x1, 1111111x | 13
320 | 1111111111111111; xxxx111111111111, 1111xxxx11111111, 11111111xxxx1111, 111111111111xxxx; xx11111111111111, 11xx111111111111, 1111xx1111111111, 111111xx11111111, 11111111xx111111, 1111111111xx1111, 111111111111xx11, 11111111111111xx; xxxxxx1111111111, xxxx11xx11111111, xxxx1111xx111111, xxxx111111xx1111, xxxx11111111xx11, xxxx1111111111xx; xx1111111111xxxx, 11xx11111111xxxx, 1111xx111111xxxx, 111111xx1111xxxx, 11111111xx11xxxx, 1111111111xxxxxx | 25

## Slide 12: Signalling Punc Pattern Index for 80/160 MHz PPDUs Using Uncoded Pad bits
RTS, CF-End and PS-Poll are 20 octets; CTS is 14 octets
When transmitted in a non-HT PPDU, the number of uncoded Pad bits is always at least 10 bits (and assume NDPA can be padded to ensure this)
Can fit 3-4 bits of puncturing pattern index, 0-1 bits of Parity and a 6-bit Tail into 10 pad bits
  Akin to HESIGB/EHTSIG
Two ways to insert the new fields into the uncoded Pad field:
  Before the scrambler (for PAPR robustness)
  After the scrambler
Sample encoding
  3 bits of punc pattern index + 1 bit of even Parity at 80 MHz
  Or 4 bits of punc pattern index at 160 MHz
  Use 0000 for the unpunctured pattern, for backwards compatibility
Data bits
Append Tail, Pad
Scramble
Encode + Puncture
Interleave
Non-HT (Mbps) | nPad (RTS, CF-End or PS-Poll @ 20B) | nPad (CTS @ 14B)
6 | 10 | 10
9 | 34 | 10
12 | 10 | 10
18 | 34 | 10
24 | 10 | 58
36 | 106 | 10
48 | 10 | 58
54 | 34 | 82
Overwrite Pad with PuncPatInd (+Parity)
Overwrite Tail x2 with zeros