## Slide 1: Critical Update - Follow Up
Date: 2021-2-17
Authors:
Name | Affiliations | Address | Phone | email
Young Hoon Kwon Liwen Chu Manish Kumar Hongyuan Zhang Yan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap:
The following concepts regarding critical updates were agreed:
  802.11be supports that an AP within an AP MLD shall include in the Beacon and Probe Response frames it transmits the Change Sequence fields that indicate changes of system information for the transmitting AP and other APs within the same AP MLD, where the change sequence field value for each AP is initialized to 0, and is incremented when there is a critical update to the operational parameters for that AP.
Also, there has been a discussion on cases that some critical updates are directly included in Beacon and/or Probe Response frames on other links:
  Inclusion of (Extended) Channel Switch Announcement
  Inclusion of Quiet element
  NOTE: For the simplicity, let’s use the term “Direct inclusion event” for this case

## Slide 3: Issues
When a non-AP STA receives a Beacon frame from AP1 on link1 that has Direct inclusion event for AP2 on link2, where AP1 and AP2 are affiliated with the same AP MLD:
  Change Sequence value corresponding to AP1 in the Beacon frame is updated such that this value is higher than the saved Change Sequence value from the non-AP STA.
  Even though the Change Sequence value has been updated, the non-AP STA is not supposed to access link2.
  What if there are other critical updates happened together with the direct inclusion event? For example:
    Inclusion of a Quiet element
    Insertion of a Broadcast TWT element
  As the non-AP STA does not access link2, the non-AP STA does not update the other critical updates properly.

## Slide 4: Possible Solutions
Option 1
  When a direct inclusion event happens, the Change Sequence value is not updated.
    Or a direct inclusion event is not considered as a critical update.
  In this case, a non-AP STA will only check Beacon/Probe Response frames when a critical update that is not a direct inclusion event happens.
link1
Quiet IE, Cnt=3
Quiet IE, Cnt=2
bTWT element
Quiet IE, Cnt=1
bTWT element
Quiet Period
link2
CS = 100
Quiet IE, Cnt=3
CS = 101
Quiet IE, Cnt=2
CS = 102
Quiet IE, Cnt=1
CS = 100
CS = 102

## Slide 5: Possible Solutions
Option 2
  There are two fields defined:
    Critical update field: As in current definition
    Indication of other critical updates included in this update
      “0”: Only direct inclusion event happened in the critical update indicated by the Critical update field.
      “1”: Critical update other than the direct inclusion happened in the critical update indicated by the Critical update field.
link1
Quiet IE, Cnt=3
Quiet IE, Cnt=2
bTWT element
Quiet IE, Cnt=1
bTWT element
Quiet Period
link2
CS = 101, OCU=0
Quiet IE, Cnt=3
CS = 102, OCU=1
Quiet IE, Cnt=2
CS = 103, OCU=1
Quiet IE, Cnt=1
CS = 100, OCU*=X
CS = 103, OCU=1
*OCU: Other Critical Update

## Slide 6: Possible Solutions
Option 3
  When a direct inclusion event happens together with other critical updates on a Beacon frame of an AP affiliated with an AP MLD, all the critical updates are included in a Beacon and/or Probe Response frames of other APs affiliated with the same AP MLD.
link1
Quiet IE, Cnt=3
Quiet IE, Cnt=2
bTWT element
Quiet IE, Cnt=1
bTWT element
Quiet Period
link2
CS = 101
Quiet IE, Cnt=3
CS = 102
Quiet IE, Cnt=2
bTWT element
CS = 103
Quiet IE, Cnt=1
bTWT element
CS = 100
CS = 103

## Slide 7: Conclusions
Critical updates when direct inclusion event happens is discussed, and some possible solutions were discussed.
  Option 1: Excluding direct inclusion case from critical update
  Option 2: Having separate field for indicating direct inclusion
  Option 3: Including all events when direct inclusion event happens

## Slide 8: SP1
Do you agree that
  The following events are not considered as critical updates:
    Inclusion of a Channel Switch Announcement element
    Inclusion of an Extended Channel Switch Announcement element
    Inclusion of a Quiet element

## Slide 9: SP2
Do you agree that
  When more than one critical update is included in a Beacon frame of an AP that is affiliated with an AP MLD, and if any of the critical updates needs to be directly included in a Beacon and/or Probe Response frame of other APs that is affiliated with the same AP MLD, all critical updates shall be included in the Beacon and/or Probe Response frame of other APs that is affiliated with the same AP MLD.