## Slide 1: Resolving TBDs in Triggered SU operation
Date: 2021-02-1
Authors:

## Slide 2: Abstract
This document tries to resolve the TBDs on frame format and procedure for Triggered SU operation

## Slide 3: Signaling using modified MU-RTS frame
A scheduled STA can transmit P2P and UL frames during allocated time in a TXOP sharing TF (“ TS-TF”)
We agreed to use a modified MU-RTS frame as the TS-TF for Triggered SU operation.
We need to signal the following:
  Distinguish from baseline MU-RTS.
  The time allocation.

## Slide 4: Triggered SU variants
We propose that for more efficient QoS Management an AP can control whether the time allocation is only for UL traffic or not. As such there can be following two modes in R1:
  Mode 1: scheduled STA only transmits UL traffic.
  Mode 2: scheduled STA can transmit UL or P2P traffic.
The error recovery is simpler for Mode 1 as AP can just use PIFS recovery anytime it does not receive an expected frame.
We therefore, propose that a TBD field (e.g., GI And HE-LTF Type) in Common Info of an MU-RTS frame signals whether it’s a TS-TF as:
  Value 0 corresponds to baseline MU-RTS,
  Value 1 corresponds to TXOP sharing for UL only traffic (Mode 1).
  Value 2 corresponds to TXOP sharing for other traffic in addition to UL traffic (Mode 2)
  Other values are reserved.

## Slide 5: Time allocation in TS-TF
For R1 timeline we have only one STA and hence a field in Common Info (e.g., UL Length) would work.
However, in R2 we would like to allocate multiple STAs with potentially different allocations.
Hence, we prefer to signal the time allocation in a User Info field (e.g., B25-B31).

## Slide 6: Straw Poll 1
Do you support that for Triggered SU operations,
  The GI And HE-LTF Type subfield in the MU-RTS Trigger frame is set to a non-zero value as:
    Value 0 corresponds to baseline MU-RTS,
    Value 1 corresponds to UL only traffic (Mode 1).
    Value 2 corresponds to any traffic (Mode 2)
    Other values are reserved.
  B25-B31 of the User Info field signals the time allocation for a scheduled STA in units of 128us?

## Slide 7: Confirmation of allocation
AP considers CTS (from scheduled STA) as an indication that medium is idle.
If the AP determines the allocation is not successful, then it follows baseline rules (i.e., PIFS or backoff) for recovery.

## Slide 8: Straw Poll 2
Do you support for Triggered SU operation :
  An AP shall determine the STA scheduled in a MU-RTS TS-TF is going to use the allocation if it receives a CTS addressed to itself after MU-RTS TS TF transmission ?

## Slide 9: Regaining TXOP by AP in mode 2 (no error)
AP obeys following rules to regain TXOP at end of an allocation:
  If the CS mechanism signals the medium is idle after the end of the allocation, then SIFS after.
  Otherwise, the AP senses the channel and regain TXOP if the channel is determined to be idle at the TxPIFS slot boundary (to check: or after backoff) after the end of the medium busy event.
Notes: This is similar to HCCA (P1838)

## Slide 10: Straw Poll 3
Do you support for Triggered SU operation (mode 2):
  an AP regains TXOP SIFS after end of an allocation if the CS mechanism signals the medium is idle at the end of the allocation.
  Otherwise, the AP senses the channel and regain TXOP if the channel is determined to be idle at the TxPIFS slot boundary after the end of the medium busy event ?

## Slide 11: Error recovery for UL only case (mode 1)
STA is not allowed to perform any error recovery, AP continue to monitor medium and if detected IDLE for PIFS – it regains control.
  This may be the only rule needed for error recovery in mode 1.
In addition, the STA may explicitly terminate the session by signaling in an UL frame.
  This is a nice to have optimization but is of lesser value.

## Slide 12: Error recovery for mode 2
Only the scheduled STA can do error recovery following a Tx failure to a peer STA. There could be two options:
  Option 1 (do nothing): Follow the baseline. Con: allocated time is unused.
  Option 2: treat the time allocation as its own TXOP. If failed in initial PPDU transmission to peer, then return the unused medium after PIFS by transmitting a QoS NULL to AP [note: HCCA allows STAs to txmit to AP after PIFS P1839].
A STA shall return any unused time by transmitting a QoS NULL frame to AP until it receives the corresponding Ack or the allocation ends.

## Slide 13: Straw Poll 4
Do you support the following error recovery procedure for Triggered SU operation:
  For mode 1, only AP can perform error recovery anytime it does not receive any expected UL frame from scheduled STA
  For mode 2,
    only scheduled non-AP STA can do error recovery following a transmission failure
    A scheduled STA shall follow the same channel access recovery rules within allocated time as a STA that obtained TXOP except that
      if the failed PPDU transmission was to a peer STA and is the first non-CTS frame in its allocated time it shall return the remaining time to AP.
    The non-AP STA shall return remaining unused time in its allocation by transmitting a QoS Null frame to AP
      AP does not transmit within the allocated time until it receives the QoS Null frame?

## Slide 14: NAV operation for EHT STAs
For unscheduled EHT STAs:
  set their intra-BSS or Basic NAV as if it were a Basic TF (i.e., no CTS timeout).
An EHT STA may respond to a RTS sent by scheduled STA even if its NAV is set under TBD conditions.