## Slide 1: MLA: MLO Architecture Reference Model
Date: 2021-02
Authors:

## Slide 2: Background
On-going discussion of 802.11 MLO architecture in the ARC SC
Terminology of some frequently used MLO terms is shown in the next slide

## Slide 3: Simplified Diagram

## Slide 4: MLO MAC Sublayer
Can be split into:
  MAC Sublayer A (common functionalities for all links)
    Resides in the MLD
  MAC Sublayer B (per-link functionalities)
    Resides in each STA that is affiliated with the MLD
i.e., a “STA that is affiliated with the MLD” only inherents part of the original MAC Sublayer. The MLD takes the rest of the other functionalities.
Notes:
  Some functionalities may be performed jointly by both MAC Sublayers
  What’s described here is all modelling. Implementation is free as long as it produces identical behavior that is observable externally

## Slide 5: MLO MAC Sublayer A (AP side)
Functionalities:
  Authentication and (Re)Association (with a non-AP MLD)
  Security Association (PMKSA, PTKSA)
  SN/PN assignment for frames to be encrypted by PTK
  Encryption/Decryption using PTK
  Reordering of packets to ensure in-order delivery per each BA session
  BlockAck states maintenance (jointly with MAC Sublayer B)
  MLD-level management info exchange/indication via MAC Sublayer B

## Slide 6: MLO MAC Sublayer B (AP side)
Functionalities:
  Link-specific GTK/IGTK/BIGTK
  Link-specific encryption/decryption using GTK/IGTK/BIGTK
  Link-specific management info exchange/indication (e.g., Beacon)
  Group addressed frames delivery
  Link-specific control info exchange/indication (e.g., RTS/CTS, Acks, NDP, etc.)
  Link-level power save
  Frame reception MAC address filtering
  BlockAck state maintenance (jointly with MAC Sublayer A)

## Slide 7: Remaining Functionalities
Functionalities that may need joint processing between the Sublayers:
  Fragmentation and Defragmentation
  Retransmissions
  Combination of (de)frag and retx

## Slide 8: Reference Model for an MLD

## Slide 9: Data Plane Architecture for MLD

## Slide 10: 11be MLO Security
Authentication and Association have been moved to the MLD level
  AP MLD is the Authenticator and non-AP MLD the Supplicant
Security keys (PMK, PTK) are generated using the MLD MAC addresses of the peer MLDs (as opposed to the link MAC addresses of the STA-AP peer)
GTK/IGTK/BIGTK is per-link, maintained at each AP affiliated with the AP MLD. Sent during the 4-way handshake to the non-AP MLD
TA/RA fields in MAC header of OTA frames still use the corresponding link MAC addresses of the transmitter and receiver, respectively

## Slide 11: 11be MLO Security (Cont’d)
For unicast Data frames, the Nonce and AAD use the MLD MAC addresses instead of the link MAC addresses
  This is to allow AP architectures that encrypt data frames ABOVE the link level (so the encrypted frames can be transmitted on any links)
  All other frames use the pre-11be Nonce and AAD computations
Auth/Assoc/4way handshake shall be performed on a single physical link chosen by the non-AP MLD (yet to be discussed/agreed in IEEE)
  The AP shall include that link as one of the ML set up links or the AP shall deauth and disassoc with the STA (in which case the non-AP MLD may attempt Auth on another link. This is no different from today’s legacy rejection during Assoc Resp).

## Slide 12: 11be Auth/Assoc Call Flows
AP Discovery
MLD Authentication/Association
4-way handshake
Group key handshake (for group key change on any AP affiliated with the AP MLD post-association)

## Slide 13: AP MLD Discovery
Affiliated STA3
non-AP MLD/ Supplicant
NAMLD
Non-AP MLD Scans network
MLD Probe Resp (ML IE) (unicast/bcast)
AP MLD/ Authenticator
APMLD
Affiliated STA2
Affiliated STA1
Affiliated AP1
Affiliated AP2
Affiliated AP3
Legacy Probe Req
Legacy Probe Resp
Non-AP MLD learns AP3 supports AP MLD and all the APs affiliated with the AP MLD.
Non-AP MLS sends an MLD Probe Req to AP2
AP MLD includes ML IE that contains all the detailed info of the affiliated APs
Non-AP MLD learns all the details info of all the APs affiliated with the AP MLD (e.g., AP capability)
Non-AP MLD then picks a STA to initiate Auth/Assoc/4-way handshake
Non-AP MLD can also request additional one or more links to set up by the AP MLD
MLD Probe Resp (ML IE) (unicast)
Scan request

## Slide 14: MLD Authentication/Association (PSK for simplicity)
Affiliated STA3
non-AP MLD/ Supplicant
NAMLD
Non-AP MLD Selects network
Auth ( Open, RA=STA1, TA=AP1, ML_ADDR=APMLD)
AP MLD/ Authenticator
APMLD
Affiliated STA2
Affiliated STA1
Affiliated AP1
Affiliated AP2
Affiliated AP3
Auth ( Open, RA=AP1, TA=STA1. ML_ADDR = NAMLD).
Auth ( Open, ML_ADDR = NAMLD).
Auth ( Open, RA=AP1, TA=STA1. ML_ADDR = NAMLD).
Auth (Open, ML_ADDR=APMLD)
Auth (RA=STA1, TA=AP1, ML_ADDR=APMLD)
Non-AP MLD and AP MLD transition to State 2 on all affiliated links
ASSOC_RSP(RA=STA1, TA=AP1, SUCCESS, ML_ADDR=APMLD, RSNE, RSNXE)
ASSOC_REQ( RA=AP1, TA=STA1. ML_ADDR = NAMLD. RSNE, RSNXE ).
ASSOC_REQ( ML_ADDR = NAMLD = NAMLD, RSNE, RSNXE)
ASSOC_REQ ( RA=AP1, TA=STA1. ML_ADDR = NAMLD RSNE, RSNXE)
ASSOC_RSP(SUCCESS, ML_ADDR=APMLD, RSNE, RSNXE)
ASSOC_RSP(RA=STA1, TA=AP1, ML_ADDR=APMLD)
Non-AP MLD and AP MLD transition to State 3 on all affiliated links
IEEE 802.1X Control port blocked on all links
Non-AP MLD updates state in lower MAC on STA2 and STA3
AP MLD updates state in lower MAC on STA2 and STA3
AP MLD updates state in lower MAC on STA2 and STA3
NOTE 1: All OTA messages are carried over the same link
NOTE 2: MLD MAC addresses passed through ML element in Authentication/Association frames
Non-AP MLD updates state in lower MAC on STA2 and STA3

## Slide 15: 4-way handshake (PSK for simplicity)
Affiliated STA3
non-AP MLD/ Supplicant
NAMLD
EAPoL-Key (RA=STA1, TA=AP1, ML_ADDR=APMLD, ANonce)
AP MLD/ Authenticator
APMLD
Affiliated STA2
Affiliated STA1
Affiliated AP1
Affiliated AP2
Affiliated AP3
EAPoL-Key (RA=AP1, TA=STA1, ML_ADDR=NAMLD, SNonce, MLE, RSNE, RSNXE, MIC)
EAPoL-Key (ML_ADDR=NAMLD, SNonce, MLE, RSNE, RSNXE, MIC)
EAPoL-Key (RA=AP1, TA=AP1, ML_ADDR=NAMLD, Snonce, MLE, RSNE, RSNXE, MIC)
EAPoL-Key ( ML_ADDR=APMLD, ANonce)
EAPol-Key (RA=STA1, TA=AP1, ML_ADDR=APMLD, ANonce)
IEEE 802.1X control port unblocked
Non-AP MLD and AP MLD transition to State 4 on all affiliated links
Non-AP MLD derives PTK
AP MLD Derives PTK
Non-AP MLD installs GTKs to respective links
AP MLD installs PTK
NOTE 1: All OTA messages are carried over the same link
NOTE 2: ML Element (MLE passed in messages 2 and 3) along with RSNE and RSNXE
EAPoL-Key (RA=STA1, TA=AP1, ML_ADDR=APMLD, MLE, RSNE, RSNXE, {GTKs}link,MIC)
EAPoL-Key (RA=AP1, TA=STA1, ML_ADDR=NAMLD, MIC)
EAPoL-Key (ML_ADDR=NAMLD, MIC)
EAPoL-Key (RA=AP1, TA=STA1, ML_ADDR=NAMLD, MIC)
EAPoL-Key ( ML_ADDR=APMLD, MLE, RSNE, RSNXE, {GTKs}link,MIC)
EAPol-Key (RA=STA1, TA=AP1, ML_ADDR=APMLD, MLE, RSNE, RSNXE, {GTKs}link,MIC)
Non-AP MLD installs PTK and GTKs to respective links

## Slide 16: Group Key handshake for AP 2
Affiliated STA1
non-AP MLD/ Supplicant
NAMLD
AP MLD/ Authenticator
APMLD
Affiliated STA2
Affiliated STA3
Affiliated AP1
Affiliated AP2
Affiliated AP3
AP2 updates the GTK on link 2
AP2 generates a new GTK, GTK2
AP signals update complete. AP2 starts using GTK2
NOTE 1: All OTA messages are carried over the same link
EAPoL-Key (RA=STA1, TA=AP1, ML_ADDR=APMLD, {GTK2}2,MIC)
EAPoL-Key (RA=AP1, TA=STA1, ML_ADDR=NAMLD, MIC)
EAPoL-Key (ML_ADDR=NAMLD, MIC)
EAPoL-Key (RA=AP1, TA=STA1, ML_ADDR=NAMLD, MIC)
EAPoL-Key ( ML_ADDR=APMLD, {GTK2}2,MIC)
EAPol-Key (RA=STA1, TA=AP1, ML_ADDR=APMLD, {GTK2}2,MIC)
UpdateGTK (GTK2)
AP MLD performs Group Key handshake to associated non-AP MLDs for GTK2 on AP2
UpdateGTK (GTK2)
UpdateGTKComplete(GTK2)

## Slide 17: Proposals
Consider adding some of the diagrams in this slide deck to the 11be spec to describe MLO architecture and security call flows
  Emphasize all the original functionalities in the MAC Sublayer is now split/shared between MAC Sublayer A and MAC Sublayer B
The architecture diagram is modelling the functional blocks and their relative processing order in a reasonable manner. In a real implementation:
  Some functionalities can be performed in different orders than depicted in the diagram
  Some functionalities in MAC Sublayer A may be implemented in MAC Sublayer B, and vice versa