## Slide 1: Definitions and scenarios of the WLAN sensing – follow ups
Date: 2021-01-26
Authors:
Name | Affiliation | Address | Phone | Email
Rui Du | Huawei Technologies Co. Ltd | F3, Huawei Base, Shenzhen, China |  | Ray.du@Huawei.com
Meihong Zhang |  |  |  | 
Yingxiang Sun |  |  |  | 
Chenchen Liu |  |  |  | 
Danny Tan Kai Pin |  |  |  | 

## Slide 2: Outline
Abstract
Definitions of WLAN sensing
  Roles of WLAN sensing
  Related terms in WLAN sensing
  Sensing session
  Sensing types
Scenarios of WLAN sensing
Summary
References
Rui Du, et al. (Huawei)

## Slide 3: Abstract
Rui Du, et al. (Huawei)
WLAN sensing definitions and scenarios have been discussed in previous contributions[1-6].
Based on the discussion on our previous contribution[6], a follow up contribution is shown.
In this contribution, some of the typical WLAN sensing scenarios proposed in [6] are further introduced and discussed.

## Slide 4: Definition of roles in WLAN sensing
Rui Du, et al. (Huawei)
Roles in the WLAN sensing
Sensing initiator
Device who initiates the sensing session and wants the sensing results. It is not mandatory for the sensing initiator to participate in the sensing measurement or processing.
If sensing initiator also is sensing transmitter or receiver, it is a non-standalone initiator.
If sensing initiator is neither sensing transmitter nor receiver, it is a standalone initiator.
Sensing responder
Non-initiator device who participates in the sensing session.
Sensing transmitter
Device who transmits sensing illumination signal to illuminate the area of interest.
Sensing receiver
Device who receives echo signal and measure the area of interest.
Sensing processor
Device who processes the sensing measurements and gets sensing result.
Sensing processor could be the same device with sensing initiator, which means sensing measurements are processed at sensing initiator.
Sensing processor also could be different device with sensing initiator(could be sensing transmitter and/or receiver), which means sensing measurements are processed and the sensing results are further feedback to sensing initiator.
During the sensing session, there could be more than one sensing processor.
Note: the roles discussed here are functions rather than fixed roles of stations.

## Slide 5: Definition of related terms in WLAN sensing
Rui Du, et al. (Huawei)
Signals in the WLAN sensing
Illumination signal
The illumination signal is transmitted by a sensing transmitter to illuminate the area of interest.
The illumination signal could be non-dedicated illumination signal in the environment(un-coordinated or passive mode).
Echo signal
The echo signal is the signal received at the sensing receiver which contains the information of the area of interest.
Measurement result in the WLAN sensing
Sensing measurement
The sensing measurement is the measurement of the area of interest（e.g. raw CSI, received radar signal）.
Sensing result
The sensing result is the result after signal processing at the sensing processor(e.g. compressed CSI, range-Doppler map, range-time map).

## Slide 6: Definition of sensing session
Three phases are defined as follows.
Negotiation phase
During the negotiation phase, initiator negotiates with the station who will participate in the sensing session and identifies the transmitter, receiver and processer.
Measurement phase
During the measurement phase, sensing transmitter transmits the illumination signal to illuminate the area of interest, sensing receiver receives the echo signal to measure the area of interest.
Feedback phase(if needed)
During the feedback phase, two kinds of information could be feedback to the initiator.
If the sensing initiator also is the sensing processor, sensing measurement(s) will be feedback to the initiator and processed to get the sensing result.
If the sensing initiator is not the sensing processor, sensing measurement(s) will be sent to the sensing processor and the sensing result will be reported to sensing initiator.
Rui Du, et al. (Huawei)

## Slide 7: Definitions of sensing types
The transmitter and receiver do not need to be synchronized.
Coordinated
Sensing transmitter(s) will be involved in the sensing session and would transmit illumination signal to illuminate the area of interest. The sensing receiver receives the echo signal to measure the area of interest.
Un-coordinated
There is no dedicated sensing transmitter involved in the sensing session and the sensing receiver measures the area of interest by receiving the illumination signal in the environment.
Rui Du, et al. (Huawei)
CSI based sensing
The transmitter and receiver are usually synchronized (usually ask for much higher synchronization performance than wireless communication, e.g. STF ).
Active radar (coordinated)
Sensing transmitter(s) will be involved in the sensing session and would transmit illumination signal to illuminate the area of interest. The sensing receiver receives the echo signal to measure the area. There could be different geometries for active radar, e.g.
Monostatic radar
Bistatic radar
Multistatic radar
Passive radar (un-coordinated)
There is no dedicated sensing transmitter involved in the sensing session and the sensing receiver measures the area of interest by receiving the illumination signal in the environment. Although the transmitter and receiver are not synchronized in the passive radar, the reference signal channel and echo signal channel at the receiver are synchronized.
Radar based sensing

## Slide 8: Scenarios of WLAN sensing
Rui Du, et al. (Huawei)
January 2021
The scenarios of WLAN sensing are quite complicated and we classify them into different categories.
Each individual scenario is further discussed in the following slides.

## Slide 9: Scenarios of WLAN sensing 1-1 Coordinated CSI based sensing(one transmitter and one receiver)
Rui Du, et al. (Huawei)
Left figure:
  STA1 is the sensing initiator(non-standalone initiator) and sensing receiver, STA2 is the sensing transmitter.
  STA1 initiates the sensing session, STA2 transmits the illumination signal and STA1 receives the echo signal to measure the area of interest.
  The echo signal received at STA1 could be processed to get the desired information.
Middle figure
  STA1 is the sensing initiator(non-standalone initiator) and sensing transmitter, STA2 is the sensing receiver.
  STA1 initiates the sensing session, transmits the illumination signal and STA2 receives the echo signal to measure the area of interest.
  Sensing measurement or result could be fed back to sensing initiator (STA1) as request.
Right figure
  STA1 is the sensing initiator(standalone initiator), STA3 is the sensing transmitter, STA2 is the sensing receiver.
  STA1 initiates the sensing session, STA3 transmits the illumination signal and STA2 receives the echo signal to measure the area of interest.
  Sensing measurement or result could be reported to sensing initiator (STA1) as request.

## Slide 10: Scenarios of WLAN sensing 1-2/3 Coordinated CSI based sensing(multi transmitter or multi receiver, participators are transmitters or receivers)
Rui Du, et al. (Huawei)
Left figure:
  STA1 is the sensing initiator(non-standalone initiator) and sensing receiver, STA2/STA3 are the sensing transmitters.
  STA1 initiates sensing session, STA2/STA3 transmit the illumination signal and STA1 receives the echo signal to measure the area of interest.
  The echo signals received at STA1 could be processed to get the desired information.
Middle figure
  STA1 is the sensing initiator(non-standalone initiator) and sensing transmitter, STA2/STA3 are the sensing receivers.
  STA1 initiates sensing session, transmits the illumination signal and STA2/STA3 receive the echo signals to measure the area of interest.
  Sensing measurement or result could be fed back to sensing initiator (STA1) as request.
Right figure
  STA1 is the sensing initiator(standalone initiator), STA3/STA4 are the sensing transmitters, STA2 is the sensing receiver.
  STA1 initiates sensing session, STA3/SAT4 transmit the illumination signals and STA2 receives the echo signals to measure the area of interest.
  Sensing measurement or result could be reported to sensing initiator (STA1) as request.

## Slide 11: Scenarios of WLAN sensing 2 Un-coordinated CSI based sensing
Rui Du, et al. (Huawei)
Left figure:
  STA1 and STA2 are communicating.
  STA3 is the sensing initiator(non-standalone), sensing receiver and sensing processor. STA3 receives the echo signal to measure the area of interest.
  The echo signals received at STA1 could be processed to get the desired information.
Middle figure
  STA1 and STA2 are communicating.
  STA3 is the sensing initiator(standalone initiator), STA4 is the sensing receiver and sensing processor. STA4 receives the echo signal to measure the area of interest.
  Sensing measurement or result could be reported to sensing initiator (STA3) as request.
Right figure
  STA1 and STA2 are communicating.
  STA3 is the sensing initiator(non-standalone initiator), sensing receiver and sensing processor, STA4 is the sensing receiver.
  Sensing measurement or result could be reported to sensing initiator (STA3) as request.

## Slide 12: Scenarios of WLAN sensing 3-1 Active radar sensing(one monostatic radar)
Rui Du, et al. (Huawei)
Left figure:
  STA1 is the sensing initiator(non-standalone initiator), sensing transmitter, sensing receiver and sensing processor.
  STA1 initiates sensing session, transmits the illumination signal and receives the echo signal to measure the area of interest.
  The echo signals received at STA1 could be processed to get the desired information.
Right figure
  STA1 is the sensing initiator(standalone initiator), STA2 is the sensing transmitter, sensing receiver and sensing processor.
  STA1 initiates sensing session, STA3/SAT4 transmit the illumination signals and STA2 receives the echo signals to measure the area of interest.
  Sensing measurement or result could be reported to sensing initiator (STA1) as request.

## Slide 13: Scenarios of WLAN sensing 3-2 Active radar sensing(multi monostatic radars)
Rui Du, et al. (Huawei)
Left figure:
  STA1 is the sensing initiator(non-standalone initiator), sensing transmitter, sensing receiver and sensing processor, STA2 is the sensing transmitter and sensing receiver.
  STA1 initiates sensing session, STA1/2 transmit the illumination signals and receive the echo signals to measure the area of interest.
  The echo signals received at STA2 could be sent to STA1 as request.
Right figure
  STA1 is the sensing initiator(standalone initiator), STA2/3 are the sensing transmitters, sensing receivers.
  STA1 initiates sensing session, STA2/SAT3 transmit the illumination signals and STA2 receive the echo signals to measure the area of interest.
  Sensing measurement or result could be reported to sensing initiator (STA1) as request.

## Slide 14: Scenarios of WLAN sensing 3-3 Bistatic/multistatic radar sensing
Rui Du, et al. (Huawei)
Bistatic/multistatic radar sensing scenarios are similar with the scenarios have been shown in slide 9/10.

## Slide 15: Scenarios of WLAN sensing 4 Passive radar sensing
Rui Du, et al. (Huawei)
Passive radar sensing scenarios are similar with the scenarios have been shown in slide 11.

## Slide 16: Summary
Rui Du, et al. (Huawei)
In this contribution, relevant basic definitions of WLAN sensing are shown and discussed.
Details of some typical scenarios of WLAN sensing are presented and discussed.

## Slide 17: References
Rui Du, et al. (Huawei)
[1] 11-20-1849-01-00bf-wi-fi-sensing-definitions.pptx
[2] 11-20-1850-00-00bf-overview-of-wi-fi-sensing-scenarios.pptx
[3] 11-20-1805-00-00bf-discussion-on-wlan-sensing-roles.pptx
[4] 11-20-1804-00-00bf-discussion-on-wlan-sensing-procedure.pptx
[5] 11-20-1960-00-00bf-analysis-of-the-functionality-of-sensing.pptx
[6] 11-21-0035-00-00bf-definitions-and-scenarios-of-the-wlan-sensing.pptx

## Slide 18: SP 1
Rui Du, et al. (Huawei)
Do you agree with the following?
  A sensing initiator may act as a sensing transmitter, a sensing receiver, or neither.

## Slide 19: SP 2
Rui Du, et al. (Huawei)
Do you agree with the following?
  Measurements obtained in a sensing session shall be obtained by or reported to its initiator.

## Slide 20: SP 3
Rui Du, et al. (Huawei)
Do you agree with the following?
  The 11bf amendment shall define different types of sensing measurement results.

## Slide 21: SP 4
Rui Du, et al. (Huawei)
Do you agree with the following?
  The type of measurement performed in a sensing session shall be defined by its initiator.