## Slide 1: Discussion of Sensing Measurement Result Types
Date: 2020-03-05
Authors:

## Slide 2: Abstract
This contribution addresses measurement reporting as part of a WLAN sensing procedure.
We first discuss the need to enable WLAN sensing procedures that make use of measurement reporting, and then offer general comments on measurement result types.
Lastly, we consider two possible measurement results that could be defined for WLAN sensing reporting in sub-7 GHz applications.

## Slide 3: WLAN Sensing
The main contribution of the 11bf amendment will be the specification of procedures that allow for WLAN sensing applications to reliably and efficiently obtain measurement results.
Two broad configurations have been considered in various TGbf contributions:
  Configuration 1: STA that uses the measurements obtains them itself. Example:
  Configuration 2: STA that uses the measurements obtains them through reporting. Examples:
STA 1
STA 2
STA 3
Trigger
Measurement
STA 1
STA 2
STA 3
Measurement
Report
STA 1
STA 2
STA 3
Measurement
Report
STA 4

## Slide 4: WLAN Sensing
Ability of defining which STA(s) assume the roles of sensing transmitter and sensing receiver is an important characteristic of WLAN sensing and partially differentiates it from other measurement procedures.
Between the two configurations discussed in the previous slide, one may be preferred over the other depending on factors such as sensing application requirements and target coverage area, among others.
  For example, application/STA(s) that rely on implementation-dependent measurements may use configuration 1.
  Configuration 2 may be used, for example, to “sample” the environment at various locations.
  Certain applications may make use of both configurations – to, for example, allow for transmit STA and/or receive STA diversity (see 19/1416r0 among others).
Worth noting that “performance” (reliability, for instance) and network load of each configuration may be different.

## Slide 5: Measurement Results
The focus of this contribution is the case in which the “STA that uses the measurements obtains them through reporting.”
To support this case, the 11bf amendment will need to define one or more measurement result types (content) and their formats.
  Already in the SFD: “The 11bf amendment may define more than one type of sensing measurement results.”
Various factors must be considered. We provide a few general comments on measurement result types in what follows.

## Slide 6: Comments on Measurement Results
It is of our best interest to not define an excessive number of measurement results.
  We should strive to consider only fundamental types of measurement results, which support a wide range of sensing applications. Avoid implementation- and/or application-specific measurements.
We should also strive to reduce the load generated by the reporting of measurement results if and when appropriate.
  Example: Definition of procedures that may reduce/limit number of reporting transmissions.
  Example: Definitions that may reduce/limit length of individual reports.
Different measurement results will likely need to be defined for sub-7 GHz and 60 GHz applications due to differences in PAR scope and measurement result types.

## Slide 7: Measurement Reporting for Sub-7 GHz Sensing
Possible to make use of feedback/measurements already defined in the 802.11 standard, such as those for explicit feedback beamforming.
For example, the 11bf amendment could (re-)use:
  Compressed beamforming feedback matrix
  CSI matrix
Note: Our intent is not to limit 11bf’s discussion to these two measurement results only. We encourage the discussion and consideration of other types as well. We must also consider measurement results types for 60 GHz.

## Slide 8: Measurement Reporting for Sub-7 GHz Sensing
Compressed beamforming feedback matrix
  Beamforming steering matrix inherently describes the channel/environment “structure” and also shows channel variations in time/space.
  Supported by current implementations.
  Loss of information (beamforming steering matrix calculation + compression).
  Beamforming steering matrix calculation is, at least in part, implementation dependent.
To the best of our knowledge, value of its use for WLAN sensing is unclear at this point.
We welcome comments and feedback on the value of adopting compressed beamforming feedback matrix as a sensing measurement result type.

## Slide 9: Measurement Reporting for Sub-7 GHz Sensing
CSI matrix
  Real and imaginary parts of each element of the matrix (that is, sub-carrier for each antenna).
  Report would be the estimated CFR – no loss of information as in the compressed beamforming feedback matrix.
  Currently used in various WLAN sensing implementations (see below).
  Overhead-limiting approaches could be considered. For example, define grouping factors when specifying the measurement reporting frame.
Use of “full” CSI matrix has been extensively considered in the literature and in various SENS TIG/SG and TGbf presentations, including:
  Dash, "CSI-based Wi-Fi Sensing: Results and Standardization Challenges," 19/1769r1.
  Allegue, "Wi-Fi Sensing: Technical Feasibility, Standardization Gaps," 19/1803r0.
  Au, "Wireless Sensing: Use Cases, Feasibility and Standardization," 19/1745r0.
  da Silva, "Wi-Fi Sensing: Cooperation and Standard Support," 19/1416r0.

## Slide 10: Conclusions
The importance of specifying in the 11bf amendment the following two configurations was discussed:
  STA that uses the measurement results obtains them itself (no feedback/reporting).
  STA that uses the measurement results obtains them through feedback/reporting.
General comments on the reporting of sensing measurements were offered.
Lastly, two different measurement results that could be defined for WLAN sensing reporting in sub-7 GHz applications were identified.
We welcome comments and suggestions.

## Slide 11: SP
Do you agree that CSI matrix feedback should be defined as a sensing measurement result type?