## Slide 1: 802.11be MLD Architecture Discussion
Date: 2021-04-29
Authors:

## Slide 2: Abstract
This presentation considers architecture concepts for TGbe MLDs, AP and non-AP.
This is follow-on from ideas in 11-20/1639, and starts from assumptions/agreements from ARC sessions from Nov ’20 through Feb ’21, in that document.
The contents here are from ongoing discussions in the ARC group, and are still open discussions (TBDs, questions/question marks/TBRs are actions for the ARC group)

## Slide 3
MLD data plane agreed model
(See also, slide 9
of 11-21/0316r0)

## Slide 4: AP Data plane w/legacy operation added (Alt 2 of 11-20/1639)

## Slide 5: Reminder of (legacy) DS structure, Figure 7-1, in 802.11-2020

## Slide 6: MLO DS structure, Alternative 3
Each stack has a MAC SAP, which (on an AP) supports a DSAF, with a DS SAP
MLD AP and legacy APs look like (N+1) APs to the DS
The DS will route all downlink frames to the DS SAP that has “registered” this client (legacy non-AP STAs or MLO non-APs)
Portal hides the details to the outside world

## Slide 7
Add (ML) management operations, and consider the stack details:

## Slide 8
To add management concepts, we have this figure as the
fundamental reference model for a STA
(Figure 4-24 in 802.11-2020)
This adds MLME, PLME, SME concepts, and their SAPs
Do we want/need a similar reference model for MLDs?

## Slide 9
Suggest this was a bad idea – raises many questions about what
is this part ? Why isn’t the MAC SAP at the top? Are there
always exactly two STAs, Etc…

## Slide 10
Is this better, or still confusing?

## Slide 11
Is this any better (or is it worse)?
Other suggestions?

## Slide 12: What about non-AP?
Non-AP is always either MLO or legacy
So, no “combined” view. It’s either one or the other:

## Slide 13: Analysis of stack details – what is where?
Security SAs/Keys (In MLO, agreement, there is 1 PTK/PMK per “MLD-MLD (P2P) association”, managed by MLD stack) (GTKs are distributed via MLD-MLD association) | PTK/PMK: MLO: PTK/PMK in MLD stack; Legacy: legacy stack’s PTK/PMK; GTK, IGTK, BIGTK: in each legacy stack - (Any use case for pre-assoc Security SA (and PMKID) that needs to work post-assoc?)
(Re)(Dis)Association, (De)Authentication | AP: “Routing” RX’d to which stack is based on ML element indication (legacy or MLO)
Authenticator(s) | 1 per legacy + 1 for MLD (At least separate Authenticator IDs (AAs))

## Slide 14: Analysis of alternatives – what is where; what is different?
Address1 filter/RX frame routing “The value of the RA/TA fields sent over-the-air in the MAC header of a frame is the MAC address of the STA affiliated with the MLD corresponding to that link. [Motion 108, [30] and [186]]” | MLD Peer -> MLD (known by association) Legacy Peer -> Legacy stack Unassoc Peer -> Legacy stack (All RX’d frames, data, Auth/Assoc, Mgmt, etc.) Note: - Power Save affecting information: PM bit, PS-Poll frames, PS trigger frames – handled by coordination. - MLD knows when all links (or all relevant-TID links) are dozing, and buffers DL
SAP(s) | AP: 1 MLD, 1 per legacy – guarantees frame order w/in TS (DS is responsible for “routing” DL) - Note: to guarantee frame order, without block ack, can’t do cross-link parallel transmit/queuing. Non-AP: Consistent MAC address (MLD or legacy)

## Slide 15: Analysis of alternatives – what is where; what is different?
 | Alternative 2
Beacons; Probes | All go to/from legacy stack (but legacy stack will add ML-element, as appropriate) TIM bits? TBD
Robust management frames | Individually addressed – just works (PTK) Group addressed? Are there any “MLD” (not link-related/link-specific) group addressed management frames?
GAS/ANQP (Pre-Assoc or post-Assoc) | Given security and RX routing above, just works. (Pre-assoc is legacy, post-assoc is usual rules.)
QoS(EDCA) queues/retry buffers (includes how to “merge” TX traffic at the lower MAC boundary – implementation choice) | EDCA queues per lower MAC. Retries can “stay in their queue” (same link), or can be moved to another link (where in the queue is implementation choice).
Block Ack | ??
MLO channel configuration/modification of operation | 

## Slide 16: Analysis of alternatives – what is where; what is different?
 | Alternative 2
SN and PN (including QMF) | Number spaces per stack – need MLO RXr to keep separate
DMS | Legacy peer: as today; MLO peer: messy
Multiple BSSID sets | Are legacy and MLD stacks separate “multiple BSSs”?
Any impacts on DS interface? | Separate SAPs – so what (??)
What is an ESS/BSS? (In MLO, transitions to/from MLO) | 
Access Controls? | 
Multi-AP coordination? | 
(Mixed-mode) Mesh? Relays? OCB? TDLS? |