## Slide 1: Sensing Measurement sequence of 11bf
Date: 2021-03-10
Authors:
Name | Affiliation | Address | Phone | Email
Dongguk Lim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | dongguk.lim@lge.com
Insun Jang |  |  |  | insun.jang@lge.com
Sang Kim |  |  |  | sanggook.kim@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
March 2021

## Slide 2: Introduction
In [1], we introduced various use cases for WLAN sensing in the home environment. And, we assumed that numerous home appliances are used for the WLAN sensing and a specific home appliance can initiate the sensing operation in some use cases.
  To estimate the channel information between multiple sensing STAs, a sensing transmission between those STAs can be done simultaneously or separately.
In this contribution, we consider the sensing measurement phase which supports the WLAN sensing by multiple STAs.

## Slide 3: Sensing Protocol
Generally, we can consider the following 3 phases for the WLAN sensing protocol as in [2]
Initiator
Responder
Negotiation Phase
Measurement Phase
Teardown Phase
Measurement phase may be separated as 2 sub-phases.
  Channel measurement phase
  Feedback phase
According to channel measurement process, feedback phase can be omitted.

## Slide 4: Sensing roles
As discussed in [3][4], the WLAN sensing STAs can have various roles according to sensing use cases or sensing scenarios.
In the aspect of the initiator of the sensing operation, we assume that an initiator can be set to have the following roles
  Transmitter
    It may require the feedback of channel measurement information from the responders.
  Receiver
    It may not require the feedback from the responders.
  Also, we assume that the same role setting for initiator can be applied when sensing is initiated by a non-AP STA.
  And, regarding the other role setting for initiator, we need more discussion.
  The information related with role of initiator can be indicated by using the sensing parameter during the negotiation or before the measurement phase.
Therefore, since sensing STAs can have different roles in sensing session, we can consider the different measurement procedure regarding the roles of initiator STA.
  In this contribution, we focus on the two roles, i.e., transmitter and receiver, of the initiator.

## Slide 5: Measurement process
To obtain the channel information between sensing STAs, NDP based sounding sequence defined in 11ac and 11ax can be considered in measurement phase.
  According to the capability of STA that supports the sensing operation, either Non-TB sounding as in 11ac or TB sounding as in 11ax can be considered.
    Also, the ranging NDP as in 11az can be considered in 11bf.
In the sub-7GHz band, by using the either Non-Trigger based process or Trigger Based process for the channel measurement of between multiple sensing STAs, we can anticipate the following benefits.
  We can reuse 11ac/11ax or next PHY architecture for simplicity.
  We can support MU operation to improve the efficiency.
  We can support MIMO and full/partial bandwidth for enhanced accuracy.

## Slide 6: Initiator & Transmitter
According to sensing role of initiator, we can consider two cases for channel measurement as follows.
  Case 1 : A STA has a role for sensing initiator and sensing transmitter.
    For the channel measurement, either Non-TB or TB process can be used according to responder’s capability.
      For example, in the negotiation phase, it can be decided what measurement sequence is used in sensing operation.
    In accordance with whether an initiator is AP or non-AP STA, we can consider the different measurement procedure.
    Case 1-A : initiated by AP
      An STA as an initiator may transmit the measurement frame to multiple STAs acting as a responder.
Initiator & Transmitter
Responders & receiver
Initiation and measurement frame
Feedback frame

## Slide 7: I&T : initiated by AP
    Non-TB measurement process
      We can reuse the VHT sounding protocol for channel measurement. However, for the enhanced sensing measurement, we need to further discuss the newly designed NDPA and a new frame related to the channel measurement.
        And we can also consider the use of a unified frame format that is for newly designed for NDPA and Trigger frame for sensing.
      To obtain the channel measurement information from the responders, the initiator transmits the feedback request/query frame including the feedback report information, separately.
        For example, the feedback report information can include the feedback type, feedback granularity, BW, etc.
      All frame exchanges can be done in a same TXOP. But, if the TXOP doesn't have enough duration to accommodate the transmission of all of the feedback reports, the frame exchange may be done in the subsequent TXOP.

## Slide 8: I&T : initiated by AP
    TB measurement process
      To measure the channels between the initiator and multiple responders efficiently, it can starts with polling to request the participation in measurements for sensing(this may not be required every sensing measurement phase).
        The polling for the request is similar to 11az and by using the polling, the initiator can confirm the responders that are possible of the actual sensing operation.
      After the polling for sensing, the initiator transmits the NDPA and NDP frame to responders.
      The feedback of measurement information from each responder is solicited by the initiator and the feedback from responders can be transmitted simultaneously by using a triggering procedure.
        By using the simultaneous feedback not the sequential from each responder, we can achieve feedback air-time saving.
        For this, we can consider the OFDMA or MU-MIMO transmission.

## Slide 9: I&T : initiated by non-AP STA
    Case 1-B : initiated by non-AP STA
      As discussed in previous meeting, the sensing operation can be initiated by non-AP STA.
      And, since the exchange of NDPA and NDP between P2P STAs is not the scope of spec, we assume that at least one AP is included in sensing operation and instead of initiator, the AP that participates in the sensing operation transmits a polling frame such as the trigger frame or NDPA frame, to other sensing STAs to progress the channel measurement by the initiator.
        So, the TB measurement can be considered in this case.
        We assume that the information related to the sensing participator is already known through the negotiation before the measurement phase.
      But, we do not limit the exchange of those frames between non-AP STAs but need to have further discussion.

## Slide 10: I&T : initiated by non-AP STA
    TB measurement process
      The initiator is a non-AP STA that requests the sensing operation to responder_1(i.e., AP).
      After responding to the request of the sensing operation, the responder_1 progresses the sensing polling, then it transmits the trigger frame for requesting the transmission of NDP to the initiator and notifying the NDP transmission of Non-AP STA to other sensing STAs.
      After transmission of the NDP frame from the initiator, the responder_1 sends a solicit frame to responders for the channel measurement information of other responders.
        The feedback request frame may follow SIFS after NDP.
      The responder_1 transmits the feedback information including the other responders’ measurement information to the initiator after it received the measurement information from the all responders that participate in the sensing.

## Slide 11: Initiator & Receiver
  Case 2 : A STA has role for sensing initiator and sensing receiver.
    Depending on which STA initiates the sensing operation, the following two cases can be considered for channel measurement.
    Case 2-A : initiated by AP
      The TB process is used in measurement for sensing.
      An initiator transmits a frame (ex., Trigger ) to multiple STAs acting as the responder to solicit the NDP transmission.
      After receiving the trigger frame from initiator, the responder STAs transmit the NDP frame to initiator.
      It does not need to require feedback from the responder because the initiator can measure the channel information by using the received NDP frame from the responders.
Initiator & Receiver
Responder& Transmitter
Initiation frame
Measurement frame

## Slide 12: I&R : initiated by AP
  TB measurement process (w/o feedback)
    Similar to that described in slides 8, it starts with polling for sensing before actual measurements.
      An initiator can confirm the sensing responders that are able to actual measurement procedure.
    Based on the responses from the responders, the initiator transmits the specific frame (ex., Trigger frame) to solicit the transmission of NDP to the initiator.
      A new Trigger frame for sensing can be considered and we need more discussion.
    The transmission of NDP from the responders can be performed simultaneously or separately.

## Slide 13: I&R : initiated by non-AP STA
    Case 2-B : initiated by non-AP STA
      TB measurement process
        Initiator which is non-AP STA transmits the request for sensing operation to a specific responder (i.e., AP).
        After a specific responder (ex., responder_1) receiving the request from the initiator sends a response frame, that responder_1 can start with polling to request the participation in measurement for sensing
        And, after complete the polling progress, the responder_1 sends a solicit frame(ex., trigger frame) to multiple responders to demand the NDP transmission.
          Herein, after transmitting the trigger frame for requesting the NDP transmission of other sensing responders and notifying the NDP transmission of the other responders that includes non-AP STAs to the initiator, the responder_1 also participate to the NDP transmission.
          The transmission of NDP from the responders can be performed simultaneously or separately.

## Slide 14: Summary
By considering the various sensing scenarios and use cases, an AP or non-AP STA can be set as a sensing initiator and this sensing STA can have one or more roles in sensing operation.
  The role of the initiator or whether it needs the feedback from the responders can be indicated in polling of the sensing measurement phase or during the negotiation phase.
  Depending on the role of sensing initiator, the different measurement procedure can be considered.
For the channel measurement in sensing, NDP based measurement can be used in the sub-7GHz band and either Non-TB measurement or TB measurement is used according to sensing STA’s capabilities.
For efficient sensing measurement, existing frame, for example NDPA and Trigger, in the measurement phase of sensing can be newly designed for sensing purpose.
  We can also consider a unified frame format for those new frames.

## Slide 15: Straw Poll #1
Do you agree that NDP based measurement procedure is supported for channel measurement in the sub-7GHz band for 11bf?
  Y/N/A

## Slide 16: Straw Poll #2
Do you agree that the Trigger based measurement sequence and Non-Trigger based measurement sequence are supported in the sub-7GHz band for 11bf?
  Depending on the capability of STA participating in sensing operation, either the Non-TB measurement procedure or the TB measurement procedure can be used.
  Details are TBD.
  Y/N/A

## Slide 17: Straw Poll #3
Do you agree that the initiator of sensing operation may request the feedback of channel measurement information to the responders that have a role of receiver?
  Details are TBD.

## Slide 18: Reference
[1] 11-20/1239r0, Use Cases for Wireless LAN Sensing
[2] 11-20/1804r0, Discussion on WLAN Sensing Procedure
[3] 20/807r3, WLAN Sensing Definitions
[4] 20/1805r1 Discussion on WLAN Sensing Roles