## Slide 1: WLAN Sensing Discovery
Date: 2021-06-29
Authors:
Name | Affiliation | Address | Phone | Email
Pei Zhou | OPPO |  |  | zhoupei1@oppo.com
Lei Huang |  |  |  | huang.lei1@oppo.com
Chaoming Luo |  |  |  | 
Liuming Lu |  |  |  | 

## Slide 2: Background
Discovery phase should be done before sensing session. [1]
In discovery phase, sensing capabilities (supported sensing roles, supported sensing measurement types, etc.) should be exchanged between sensing initiator and sensing responder(s). [1][2]
In this contribution, we show how to indicate sensing capabilities for a STA.

## Slide 3: Possible Sensing Capabilities
The following possible sensing capabilities may be advertised during discovery:
  Supported sensing roles [3]:
    Sensing Initiator
    Sensing Responder
    Sensing Transmitter
    Sensing Receiver
  Supported sensing bands [4]:
    2.4 GHz
    5 GHz
    6 GHz
    60 GHz
  Supported sensing measurement result types [3]: More than one type of sensing measurement results may be defined (Motion 12).
    CSI-based sensing [3]
      e.g., for sub-7 GHz and 60 GHz: CSI matrix [5]
    Radar-based sensing [3]
      e.g., for 60 GHz: beam SNR [6]
  Other capabilities
  So far, we need more than 10 bits to indicate the above sensing capabilities of a STA. We believe that in the process of standardization, more sensing capabilities will need to be indicated.

## Slide 4: Container of Sensing Capabilities
  Option 1: Add all the sensing capabilities (e.g., possible sensing capabilities shown in slide 3) into the existing frame/element (e.g., Extended Capabilities element).
Note: The sensing capabilities are TBD.

## Slide 5: Container of Sensing Capabilities (Cont.)
  Option 2: Design a new ‘Sensing Capabilities element’ to carry all the sensing capabilities.
Note: The format of Sensing capabilities element is TBD.

## Slide 6: Container of Sensing Capabilities (Cont.)
  Option 3: Add one bit ‘Sensing Support’ signaling into the Extended Capabilities element for sensing capability indication and design a Sensing Capabilities element to carry the detailed sensing capabilities of a STA.
  Note: Detailed sensing capabilities may be exchanged when a sensing session is initiated (e.g., during setup phase).

## Slide 7: Option 1 vs. Option 2 vs. Option 3
 | Pros. | Cons.
Option 1 | Only >10 bits sensing capabilities are needed | Overhead will be large if a STA only want to participate in WLAN sensing
Option 2 | The presence of Sensing Capabilities element indicates the ability for WLAN sensing; Overhead will be small if a STA only want to participate in WLAN sensing | 2 additional octets are needed to indicate Element ID field and Length field
Option 3 | Detailed sensing capabilities can be exchanged when a sensing session is initiated | One more bit is need as compared with Option 2
  As described in the 802.11 spec (Clause 9.4.2.26):
    The Extended Capabilities element carries information about the capabilities of a STA that augment the capabilities specified in the Capability Information field.
    If a STA does not support any of capabilities defined in the Extended Capabilities element, then the STA is not required to transmit the Extended Capabilities element.
  For option 1 and option 3: if a STA that only want to participate in the WLAN sensing (in other words, the STA does not support any of capabilities defined in the Extended Capabilities element), the signaling overhead will be too large*.
  Therefore, it is justifiable and preferred to define a Sensing Capabilities element to carry all the sensing capabilities of a STA.
* At present, more than 97 bits have been defined in this element. [7]

## Slide 8: Sensing Discovery flow
Passive Scanning:
  Sensing capabilities (element) of AP can be carried in Beacon frame.
  Sensing capabilities (element) of STA can be carried in (Re)Association Request frame.
  Active Scanning:
  Sensing capabilities (element) of STA can be carried in Probe Request frame.
  Sensing capabilities (element) of AP can be carried in Probe Response frame.
or
  Sensing capabilities (element) of STA can be carried in (Re)Association Request frame.
  Sensing capabilities (element) of AP can be carried in (Re)Association Response frame.
Sensing capabilities (element) can be carried in Beacon, Probe Request, Probe Response, (Re)Association Request, (Re)Association Response frames, etc.
Active Scanning
Passive Scanning

## Slide 9: Summary
We discussed three kinds of sensing capabilities indication methods:
  Use the reserved bits of existing Extended Capabilities element to indicate all the sensing capabilities
  Design a new Sensing Capabilities element to carry all the sensing capabilities
  Use one bit of existing Extended Capabilities element to indicate ‘Sensing Support’ and design a new Sensing Capabilities element to carry all the sensing capabilities

## Slide 10: SP #1
Which option do you prefer when the 802.11bf amendment defines the container of sensing capabilities?
  Option 1: use the reserved bits in Extended Capabilities element to indicate all the sensing capabilities of a STA.
  Option 2: design a Sensing Capabilities element to carry all the sensing capabilities of a STA.
  Option 3: use one reserved bit in Extended Capabilities element to indicate ‘Sensing Support’ and design a Sensing Capabilities element to carry the detailed sensing capabilities of a STA.
  Note: The format of Sensing Capabilities element and the detailed sensing capabilities are TBD.
Option 1: 0
Option 2: 16
Option 3: 3
Abstain: 12
None: 8

## Slide 11: SP #2
Do you support that 802.11bf amendment shall define a Sensing Capabilities element to carry all the sensing capabilities of a STA?
Note: The format of Sensing Capabilities element is TBD.
Yes:
No:
Abstain:

## Slide 12: Motion #1
Move to add the following to 11bf SFD:
802.11bf shall define a Sensing Capabilities element to carry all the sensing capabilities of a STA.
Note: The format of Sensing Capabilities element is TBD.
Yes：
No:
Abstain:

## Slide 13: Reference
11-20-1851-04-00bf-overview-of-wi-fi-sensing-protocol
11-21-0370-01-00bf-considerations-of-sensing-negotiation
11-21-0147-03-00bf-definitions-and-scenarios-of-the-wlan-sensing-follow-ups
11-20-1804-01-00bf-discussion-on-wlan-sensing-procedure
11-21-0357-01-00bf-discussion-of-sensing-measurement-result-types
11-21-0407-03-00bf-multi-band-wifi-fusion-for-wlan-sensing
Draft P802.11az_D3.0