## Slide 1: Wired-Wireless TSN Configuration and Management
Date: 2021-04-20
Authors:

## Slide 2: Introduction
This presentation reviews the architecture, assumptions and requirements for an 802.11 BSS operation as a Wireless TSN bridge
It also discusses wireless challenges to be considered in the configuration & management of wired-wireless TSN domains and identifies potential areas for enhancement and collaboration between 802.1 and 802.11

## Slide 3: Challenges of wireless networks (incl. 802.11)
Wireless is different from other mediums in the 802.1 TSN ecosystem
  Fading leads to a wide variation in transmission speed (e.g. 1000->100Mb/s)
  Shared medium access can cause variable delay and jitter (e.g. random backoff)
  Path loss variability and STA mobility can cause change in best serving AP and thus TSN Bridge end-point
Thus, physical path from TSN talker to listener can change significantly!
Question: where in TSN architecture is this accounted for or abstracted ?

## Slide 4: Physical Wired-Wireless 802.1 TSN integration model
Control plane entities in a centralized management model (802.1 Qcc):
CNC: Central Network Configuration
CUC: Central User Configuration
The CUC collects traffic stream requirements from end devices (Talkers/Listeners), e.g., over OPC_UA
The CNC discovers the bridges capabilities
  Bridge parameters (802.1Qcc clause 12, 802.1Qdj)
The CNC configures TSN capabilities at the bridges (e.g., using YANG/Netconf interface)
WLAN Integration:
AP can be seen as a Wireless TSN Bridge
STAs can be configured as talkers or listeners
CNC uses same abstraction for wired & wireless domains
CNC needs to re-schedule upon every fading/mobility event
Notes: Network topology discovery is an implementation specific

## Slide 5
CUC
TSN Config. & Management
Talker End Stations
TSN Bridges
Listener End Stations
Stream Data
Stream Data
End Station( ) Configuration protocol
UNI
Wireless Talker End Stations
Wireless Listener End Stations
Stream Data
Stream Data
End Station( ) Configuration protocol
End Station( ) Configuration protocol
End Station( ) Configuration protocol
Wired-TSN
Wireless-TSN
Wireless TSN Bridge
CNC
Logical Wired-Wireless 802.1 TSN integration model
CNC: Central Network Configuration
CUC: Central User Configuration
The CNC uses same abstraction for wired and wireless domains
WTSN bridge abstracts mobility/fading
CNC never reschedules

## Slide 6
CUC
TSN
Talker End Stations
TSN Bridges
Listener End Stations
Stream Data
Stream Data
End Station( ) Configuration protocol
UNI
Wireless Talker End Stations
Wireless Listener End Stations
Stream Data
Stream Data
End Station( ) Configuration protocol
End Station( ) Configuration protocol
End Station( ) Configuration protocol
Wired-TSN
Wireless-TSN
WTSN
AP
CNC
Hybrid Wired-Wireless 802.1 TSN integration model
CNC: Central Network Configuration
CUC: Central User Configuration
WTSN Bridges form a WTSN Domain
TSN CNC is aware of WTSN domain
CNC adapts scheduling accordingly
WTSN Domain*
*AP/STA within WTSN domain support TSN (.1AS/Qbv)
No TSN translation (TT) needed

## Slide 7: Hybrid TSN integration model
CNC is wireless aware and logical TSN bridge has known dynamic range
  Realistic range of MCS/data-rates can be used to report reasonable delay bounds to CNC
  CNC scheduling can account for wireless variability (e.g. 99.9%-ile vs. 100%-ile worst-case)
Flexibility
  Designers can determine trade-off between necessity for gate re-computation vs. efficiency
  Systemic degradation can still be accommodated (i.e. by exception)
Key E2E TSN Benefits
  Gate over-runs (e.g. due to low speeds) mitigated via aggressive scheduling of upstream nodes
  Overall latency can be reduced by using high-confidence 99%-ile delay bounds

## Slide 8: Wired/wireless TSN Qbv Scheduling Use case description + WCL Computation
Talker
B1
B2
B3
B4
AP
Listener
Wired – 100 Mbps
Wireless – Wi-Fi 6
Listener
…
Data (DL MU OFDMA)
AIFS + Avg. Backoff
MU/BA
~200
Wired TSN domain
Wireless TSN domain
5 ns per meter delay (wired)
1 meter between hops
Switch input delay = 2.5 us
Switch processing delay = 2.5 us
Switch queue delay = 0
SIFS
Notes: D. Thiele, R. Ernst and J. Diemer, "Formal worst-case timing analysis of Ethernet TSN's time-aware and peristaltic shapers," 2015 IEEE Vehicular Networking Conference (VNC), Kyoto, Japan, 2015, pp. 251-258, doi: 10.1109/VNC.2015.7385584

## Slide 9: Wired/wireless TSN Qbv Scheduling 1 Time-sensitive Stream – Latency deadline 2ms – 128 Bytes Payload Case 1a: MCS3 / DL MU OFDMA (2 MHz RU)
Talker
Bridge 1
Bridge 2
Bridge 3
Bridge 4
AP
25
0.25
1
Traditional static Qbv Schedule
Notes: 28 bytes – protocol overhead
128 +28 bytes – guard band

## Slide 10: Wired/wireless TSN Qbv Scheduling 1 Time-sensitive Stream – Latency deadline 2ms – 128 Bytes Payload Case 1b: MCS3  MCS1 / DL MU OFDMA (2 MHz RU)
Talker
Bridge 1
Bridge 2
Bridge 3
Bridge 4
AP
25
0.25
Traditional static Qbv Schedule
1.33
Notes: 28 bytes – protocol overhead
128 +28 bytes – guard band

## Slide 11: Wired/wireless TSN Qbv Scheduling 1 Adapted Stream – Latency deadline 2ms – 128 Bytes Payload Case 1c: MCS 8 / MU-DL (2 MHz)
25
Talker
Bridge 1
Bridge 2
Bridge 3
Bridge 4
AP
Wireless-aware aggressive Qbv Schedule

## Slide 12: Configuration and Resource Management for hybrid model
CNC differentiates wired and wireless TSN (WTSN) domains
CNC aware of WTSN bridge and it’s dynamic range
  CNC doesn’t manage short-term changes in wireless link (WTSN bridge abstracts this aspect)
  WTSN bridge provides expected performance range (e.g. 99%-ile delay) and reports by exception any unexpected deviations (e.g. unplanned mobility)
  Tradeoff between efficiency and adaptation overhead/re-scheduling can be made
Elements in WTSN domain (AP, STA) support TSN (.1AS/Qbv) and can be managed via Qcc/dj-based interface

## Slide 13: Conclusions
Multiple wired/wireless TSN integration models are possible
Physical model most appropriate in absence of mobility
Logical model offers simplest integration with 802.1 TSN
NEW proposed hybrid model provides ability to trade limited management complexity for efficiency